## Slide 1
Proposal for
In-use Data Conversion Technique
( Re-Categorization of in-use data )
(*) WLTC : Worldwide harmonized Light duty
driving Test Cycle
version 1 : 22 March 2010
proposed by Japan
DHC group
under GRPE/WLTP informal group

## Slide 2: 1. Purpose
It was agreed that each CP has its own unique definition of each road type (urban/rural/motorway) during its 1st DHC meeting. This may lead the discrepancy on speed-acceleration distribution among CPs in same road category.
This document describes the technique to convert the in-use data into vehicle speed oriented categories.
  urban/rural/motorway -> low/middle/high speed
  This technique can be used for other re-categorization including more than three (3) divisions

## Slide 3
2. Definition of Road Type
 | Urban | Rural | Motorway
India | Paved roads in urban areas with a speed limit ≤40 km/hour (exclude mountain areas) | Paved non-motorways outside and inside urban areas with a speed limit between 40 and 60 km/hour | Paved motorways (multi-lane roads specifically constructed and controlled for fast traffic) with a speed 60 to 80 km/hour
Korea | Arterial, collector and local road inside and/or near central business district (CBD). Speed limit is from 40 to 80 km/h, depends on road type | Arterial, collector and local road inside non-urban area. Speed limit is from 50 to 80 km/h, depends on road type | Motorway which is designed, constructed and controlled for faster traffic in urban and rural area. Speed limit is from 100 to 120 km/h, depends on area
Japan | Densely Inhabited District (DID) ・Speed limit≦60km/h ・exclude mountain areas | ・Non-Densely Inhabited District ・Non motorways ・exclude mountain areas | Motorways (within City and between Cities) ・exclude mountain areas

## Slide 4: 3.1. Data analysis process - Step A-1 -
Categorize the collected data into original matrix with weighting factor
  < Matrix : road type/vehicle category/time period >
Record the collected data duration in each matrix
Road type Vehicle category | Urban |  |  | Rural |  |  | Motorway |  | 
 | Weekday |  | Week-end | Weekday |  | Week-end | Weekday |  | Week-end
 | On-peak | Off-peak |  | On-peak | Off-peak |  | On-peak | Off-peak | 
Passenger Car |  |  |  |  |  |  |  |  | 
Light Duty Commercial Vehicle |  |  |  |  |  |  |  |  | 
Collected data set

## Slide 5: 3.1. Data analysis process - Step A-2 -
Weighting factor matrix
The collected data duration
It is expected that the collected data volume in each matrix doesn’t match the weighting factor obtained based on vehicle statistical information.

## Slide 6: 3.2. Data analysis process - Step B -
  Need to compensate the weighting factor of each matrix since the specific short trip is possible to move into different matrix.
(1) Calculate the compensated weighting factor (wi’)
WU,PC,ON’ =
TU,PC,ON
WU,PC,ON
× AU,PC
WU,PC,OFF’ =
TU,PC,OFF
WU,PC,OFF
× AU,PC
WU,PC,E’ =
TU,PC,E
WU,PC,E
× AU,PC
Same equation will be applied to others
+
TU,PC,ON
WU,PC,ON
TU,PC,OFF
WU,PC,OFF
TU,PC,E
WU,PC,E
+
AU,PC =
WU,PC,ON
WU,PC,OFF
WU,PC,E
+
+
where

## Slide 7: 3.3. Data analysis process - Step C-1 -
Convert the each short trip data including the previous idling portion into new categories (Low/Middle/High) from original (Urban/Rural/Motorway) categories with the compensated WF (w’)
criteria : maximum vehicle speed of each short trip
Phase | Max. speed of each ST
Low speed | ~ 40* km/h
Middle speed | 40* ~ 80* km/h
High speed | 80* km/h ~
Proposed Criteria:
*) the specific vehicle speed subject to change based on the collected data.

## Slide 8: 3.3. Data analysis process - Step C-2 -
Time (s)
Speed (km/h)
Time (s)
Speed (km/h)
Time (s)
Speed (km/h)
Low speed database
Middle speed database
High speed database
Urban – ON Peak
Urban – Off peak
Urban - Weekend
wL,1=
wU,PC,ON'
wL,2=
wU,PC,ON'
wM,1=
wU,PC,ON'
wL,3=
wU,PC,ON'
wL,4=
wU,PC,OFF'
wM,2=
wU,PC,OFF'
wL,5=
wU,PC,OFF'
wM,4=
wU,PC,E'
wH,1=
wU,PC,E'
wM,3=
wU,PC,OFF'

## Slide 9
（修正版）3-4. Data analysis process - Step D -
The collected data was converted into new categories.
New weighting factors（wL, wM, wH） are calculated as follows.
This process will be done in each data collection CPs.
Then, move on to
“2.2.3. Test Cycle Development - Step3 – in WLTP-DHC-02-04”
with slight modification.

## Slide 10
3.5. Data analysis process – Modification 1 -
・
・
・
×
×
・
・
・
・
・
・
M,1
M,2
WM,1
WM,2
Speed-Acceleration distribution of each short trip should be multiplied by the compensated weighting factors (w’).

## Slide 11
3.5. Data analysis process – Modification 2 -
Frequency distribution for idling & short trip duration also should be multiplied by the compensated weighting factors (w’).
Vertical Axis :
Number of data
the compensated weighting factor
×

## Slide 12
3.6. Data analysis process
Then move on to
“2.2.6. Test Cycle Development – Step6 – in WLTP-DHC-02-04”
with no more modification.