## Slide 1: WLTC* Methodology ~ Initial Analysis Results & Modification on proposed methodology ~
Presented by Japan
GRPE/WLTP-IG/ DHC subgroup
14 October 2010
*) WLTC: Worldwide harmonized Light duty driving Test Cycle

## Slide 2: Table of Contents
Purpose
Initial analysis results
  2.1. Overview of collected in-use data
  2.2. Data analysis method
  2.3. Result of data analysis
  2.4. Conclusion
Validity of L/M/H method
  3.1. Overview of L/M/H method
  3.2. Consideration of threshold speed
  3.3. Analyzed example of L/M/H method
  3.4. Conclusion
Modification on proposed methodology
  4.1. Modification list
  4.2. Modification on proposed methodology

## Slide 3: 1. Purpose
Early studies
  Japan and UK proposed the methodology to develop WLTC (WLTP-DHC-02-04/05/06 as U/R/M method)
  Japan proposed the alternative technique to convert the in-use data to another categorization (WLTP-DHC-03-02 as L/M/H method)
    The alternative technique was well recognized but need more clear explanation
Initial analysis
  to make clear whether there is discrepancy in same road category or not
  to derive the potential problem in the current methodologies
Validity of L/M/H method
  to confirm that the alternative technique (L/M/H method) is valid to obtain similarity
  to make a decision which methodology is more appropriate
Modification on proposed methodology
  to improve the methodology based on the initial analysis

## Slide 4
Purpose
Initial Analysis Results
  2.1. Overview of collected in-use data
  2.2. Data analysis method
  2.3. Result of data analysis
  2.4. Conclusion
Validity of L/M/H method
  3.1. Overview of L/M/H method
  3.2. Consideration of threshold speed
  3.3. Analyzed example of L/M/H method
  3.4. Conclusion
Modification on proposed methodology
  4.1. Modification list
  4.2. Modification on proposed methodology
2. Initial Analysis Results

## Slide 5
2.1.1. Definition of Road Type
 | Urban | Rural | Motorway
India | Paved roads in urban areas with a speed limit ≤40 km/hour (exclude mountain areas) | Paved non-motorways outside and inside urban areas with a speed limit between 40 and 60 km/hour | Paved motorways (multi-lane roads specifically constructed and controlled for fast traffic) with a speed 60 to 80 km/hour
Korea | Arterial, collector and local road inside and/or near central business district (CBD). Speed limit is from 40 to 80 km/h, depends on road type | Arterial, collector and local road inside non-urban area. Speed limit is from 50 to 80 km/h, depends on road type | Motorway which is designed, constructed and controlled for faster traffic in urban and rural area. Speed limit is from 100 to 120 km/h, depends on area
Japan | Densely Inhabited District (DID) ･ Speed limit ≤ 60km/h ･ exclude mountain areas | ･ Non-Densely Inhabited District ･ Non motorways ･ Speed limit ≤ 60km/h ･ exclude mountain areas | Motorways (within City and between Cities) ･ Speed limit ≤ 100km/h ･ exclude mountain areas
EU | The definition depends on EU countries | The definition depends on EU countries | The definition depends on EU countries
USA | ? | ? | ?
China | ? | ? | ?
It was agreed that each CP has its own unique definition of each road type (urban/rural/motorway) during 1st DHC meeting. This may lead the discrepancy on speed-acceleration distribution among CPs in same road category.

## Slide 6: 2.1.2. Overview of Collected In-use Data
Country / Region | Area | No. of vehicles |  | Total driving duration(*) (hr) | Total driving distance(*) (km)
 |  | Passenger car | Light duty commercial vehicle |  | 
EU (*)ongoing | Germany, Italy, Slovenia, France, Belgium, Switzerland | 67 | 6 | Approx. 2,800 | Approx. 145,000
Japan | 12 prefecture: Tokyo, Osaka , Kyoto, Nagoya, Shizuoka, etc | 11 | 13 | Approx. 1,800 | Approx. 55,000
Korea(**) | Seoul | 6 | 2 | Approx. 1,100 | Approx. 35,000
(*) Exclude NG data
(**) Korea: Not exist Weekend data in Urban and Rural

## Slide 7: 2.1.3. Traffic Volume Weighting in Driving Conditions
Temporary weighting for initial analysis

## Slide 8: 2.2.1. Preparation for Data Analysis
Common points
  Remove the noise by filtering process.（T4253H filter）
  Find the acceleration by applying differential equation αi = (Vi+1 - Vi-1) / (Ti+1 - Ti-1)
  Generate the Speed-acceleration distribution, V：5km/h intervals, α：1km/h/s intervals
  Eliminate the ST with max speed 250km/h or higher
Japanese data
  Include incomplete ST that transfer to High phase (e.g. Vmax≧80, 90km/h)
  (See the next slide for more details on incomplete ST）
EU data（Pre-check methodology）
  not_ok is set “true”, when failures or inconsistencies were found during data preprocessing and when the following indicators are set “true”,
  not_ok_dv is set “true”, when the difference between the original vehicle speed v and the smoothed speed vg is < -7 km/h or > 7 km/h. This is typically the case, when there are gaps or jumps in the speed pattern.
  not_ok_v_start_end is set to “true”, when v_start and/or v_end of a short trip is higher than 12.6 km/h.
  not_ok_a_min_max is set to “true”, when the acceleration exceeds 4 m/s² or is less then -4.5 m/s².
  Datasets and short trips, indicated with those not_ok indicators should be excluded from the further analysis.
Korean data
  Apply same method as Japanese data

## Slide 9: 2.2.2. Incomplete Short Trip
Both complete and incomplete in-use data that transfer to High phase are analyzed.
  Because of long driving duration at high speed, including the STs with no start acceleration phase or braking phase does not impact.
  If the data is excluded, the few remaining data might not represent actual driving conditions.
Time
Veh. speed
Time
Veh. speed
Time
Time
①Complete ST
②Incomplete ST

## Slide 10: 2.3.1. Parameter Comparison-1
◆Driving distance

## Slide 11: 2.3.1. Parameter Comparison-2
◆Average speed

## Slide 12: 2.3.1. Parameter Comparison-3
Average ST duration
Average IDLE duration
Ratio of 4 driving mode

## Slide 13: 2.3.2. Speed Acceleration Distribution
Discrepancy in speed-acceleration distribution was observed in each road category.

## Slide 14: 2.3.3. Frequency of ST Maximum Speed （Y axis：Frequency of driving duration）
Discrepancy in ST maximum speed distribution was observed.

## Slide 15: 2.3.4. Other Parameters
Discrepancy in ST/IDLE duration distribution was observed.

## Slide 16: 2.4. Conclusion of Initial Analysis
It was observed that speed-acceleration distribution/driving characteristics in each region have discrepancy in same road categories.
This discrepancy may mislead the representativeness when developing the harmonized driving cycle.
Therefore, it is necessary to convert to another category where driving characteristics are similar in each region. L/M/H methods is one of countermeasures.

## Slide 17
Purpose
Initial analysis results
  2.1. Overview of collected in-use data
  2.2. Data analysis method
  2.3. Result of data analysis
  2.4. Conclusion
Validity of L/M/H method
  3.1. Overview of L/M/H method
  3.2. Consideration of threshold speed
  3.3. Analyzed example of L/M/H method
  3.4. Conclusion
Modification on proposed methodology
  4.1. Modification list
  4.2. Modification on proposed methodology
3. Validity of L/M/H Method

## Slide 18: 3.1. Overview of WLTP-DHC-03-02
WLTP-DHC-03-02 described the technique to convert the in-use data into vehicle speed oriented categories.
  Urban/Rural/Motorway -> Low/Middle/High
Urban
Rural
Motorway
◆Image
Low
Middle
High
The segments that composed of ST and IDLE move into L/M/H categories with the compensated WF.

## Slide 19: 3.2.1. Detail of L/M/H Method
Considering the threshold vehicle speed
  Consider threshold based on each countries’ traffic condition and driving characteristic
  Find the threshold that shows similar VA distribution of each countries
Calculate the compensated WF
  Using Drive condition WF and total driving duration
Convert in-use data（U/R/M => L/M/H）
Analyze VA distribution and driving characteristics （L/M/H）
Generate the driving cycle in each phase

## Slide 20: 3.2.2. Consideration of Threshold Speed - 1
<Method1> Based on similarity of VA distribution
The threshold of Low/Middle
  Vmax ≤ 40 ?, Vmax ≤ 50 ?, Vmax ≤ 60 ?, Vmax ≤ 70 ?
The threshold of Middle/High
  VL/M < Vmax ≤70 ?, VL/M < Vmax ≤80 ?, VL/M < Vmax ≤90 ?, VL/M < Vmax ≤100 ?

## Slide 21: 3.2.2. Consideration of threshold speed - 2
<Method2> Based on parameter value
Select the candidate threshold speed based on least discrepancy in each characteristic.

## Slide 22: 3.2.2. Consideration of threshold speed - 3
<Method3> Based on maximum speed distribution
50 / 90?
65 / 110?
60 / 90?
After completion of all data acquisition, final threshold speed will be determined by taking into account of three methods.
50 / 80?

## Slide 23: 3.3.1. Analysis Sample - VA distribution
It was confirmed that VA distribution is similar in L/M category but slight discrepancy in High category still exist.

## Slide 24: 3.3.2. Analysis Sample - Average speed
U/R/M
L/M/H (threshold: 50/90)
As an example, convert into L/M/H at 50/90km/h

## Slide 25: 3.3.3. Analysis Sample - Parameters

## Slide 26: 3.4. Summary of L/M/H Method
It was observed that each region driving characteristics and VA distributions comparatively show similarity by converting into Low/Middle/High speed based on ST max speed.
The appropriate threshold will be decided based on each countries’ traffic condition, driving characteristic and VA distribution after completion of all in-use data collection.

## Slide 27
4. Modification on Proposed Methodology
Purpose
Initial analysis results
  2.1. Overview of collected in-use data
  2.2. Data analysis method
  2.3. Result of data analysis
  2.4. Conclusion
Validity of L/M/H method
  3.1. Overview of L/M/H method
  3.2. Consideration of threshold speed
  3.3. Analyzed example of L/M/H method
  3.4. Conclusion
Modification on Proposed Methodology
  4.1. Modification Lists
  4.2. Modification on proposed methodology

## Slide 28: 4.1. Modification Lists
Based on the initial in-use data analysis, it was observed that the following items need to be revised for improvement of driving cycle development and for efficient work.
  Method for ST/IDLE selection
  Method for cycle development of high speed mode
  Method for ST selection combination in each mode

## Slide 29: 4.2. Method for ST/IDLE Selection
Original (Boundary)
  Divide cumulative frequency distribution into “Ni, ST +1”
  Select the durations on each boundary (dividing) line
Revised (Average)
  Divide cumulative frequency distribution into “Ni, ST”
  Select the average duration in each class
ST/ID duration
Cumulative frequency
STD1
STD2
STDN
・・・・・
ST/ID duration
Cumulative frequency
STD1
STD2
STDN
・・・・・
100%
(N+1)
100%
N
It is possible to develop more representative cycle by applying revised method

## Slide 30: 4.3.1. Concerns on High-speed Driving Cycle Development
Since most of ST duration（e.g. 696sec, Japan） in high-speed mode are longer than cycle duration, the number of potential STs will be dramatically reduced. This may lead the critical discrepancy in its representativeness.
Example) Japan High phase（90km/h < ）
Average ST duration: 696 sec
Average Idling duration: 20 sec
Number of ST: (600 - 20) / (696 + 20) = 0
Idling ratio: 3.1 %
Driving ratio: 96.9 %

## Slide 31: 4.3.2. Process of high-speed cycle development
Determine the high-speed cycle duration (e.g. 600 sec.)
Determine the ST duration based on average ST duration and idling duration ratio of in-use data, the divide the ST into 5 parts (take-off1, take-off2, cruise, slow-down1, slow-down2).
Extract the driving data which meet each part configuration from the complete in-use ST.
Select the least chi-squared extracted driving data in each part, then combine the selected data to develop the complete cycle.
(note) if the complete in-use data is less chi-squared value than combined cycle, this specific data can be used for high-speed cycle.

## Slide 32: 4.3.3. Divide into 5 Parts of High-Speed Cycle
Speed range | Frequency (%) | Target duration | Divide part
Idling | 3.1 | 18 | 9
0~75, 75~0 | 36.1 | 217 | 108
75~90, 90~75 | 30.0 | 179 | 89
90~ | 30.9 | 186 | 
Total | 100 | 600 | 
0 ~ 75 km/h, 108 sec
75 ~ 90 km/h, 89 sec
90 ~ 90 km/h, 188 sec
90 ~ 75 km/h, 89 sec
75 ~ 0 km/h, 108 sec
30%
31%
36%
Adjust 2 sec.
100％ = 600 sec.
3 %
Generate speed range and duration
  Divide into 3 speed range based on dividing frequency distribution
    Example: 0~75 km/h, 75~90 km/h, 90 km/h～
  Decide target duration in each range, then divide into two portions (take-off and slow-down)
    Example of 0~75km/h: 36% => 217 sec => take-off part 108 sec，slow-down 108 sec
(take-off1)
(Cruise)
(slow-down2)
(take-off2)
(slow-down1)

## Slide 33: 4.3.4. Extraction of Driving Data
Extract the driving data which meet each part definition* from complete ST.
  Sample definition <Take-off 1 part>
  speed range : 0 ~ 75 km/h (with±0.5km/h), duration : 108sec.
Time
Veh. speed
Time
Veh. speed
Time
Veh. speed
0~75 | 75~90 | 90~90 | ・・・ | 75~0
 |  |  | ・・・ | 
 |  |  | ・・・ | 
 |  |  | ・・・ | 
 |  |  | ・・・ | 
 |  |  | ・・・ | 
0～75 km/h
108 s
0～75 km/h
108 s

## Slide 34: 4.3.5. Method to Develop High-Speed Driving Cycle
(take-off1)
(Cruise)
(slow-down2)
(take-off2)
(slow-down1)
Candidate driving data
combined
Least chi-squared distribution
Seek the combination cycle with least chi-square value compared with unified cycle

## Slide 35: 4.3.6. Selection of Complete Short Trip
◆complete short trip -1 (X2=1.12)
◆complete short trip -2 (X2=1.15)
Few possibility to find the complete in-use data to represent the unified cycle
◆United VA distribution (90<)
◆There is only a few complete STs with target duration in Japan database
◆Comparison of VA distribution

## Slide 36: 4.4.1. Method for the ST Combinations
◆Japan reference database
Average ST duration: 42.7 sec
Average Idling duration: 26.5 dec
TST | 8 | 15 | 22 | 30 | 39 | 51 | 67 | 111
NST | 960 | 764 | 685 | 689 | 556 | 419 | 250 | 75
Combination number = 1.5 × 1021 (Only Japan data)
When it takes 0.1 sec for chi-square calculation per one combination, it takes 4.8×1012 Year（1.5×1020 Sec） for all possible combinations (only Japanese data). Therefore, it is necessary to reduce number of combinations for practical work.
◆The candidates for each short trip duration for the total combination numbers and short trip numbers
◆Short trip duration in Low phase (threshold: 50/90)
◆Test cycle
Desired cycle duration: 600 sec
NST = (600 - 26.5) / (42.7 + 26.5) = 8.3
Number of short trips NST: 8
TST: 8, 15, 22, 30, 39, 51, 67, 111 = 343 sec
Average ST duration: 42.9 sec

## Slide 37: 4.4.2. Selection of each ST duration
ST selection criteria
  ST within average ±1σ in each ST duration
    Average vehicle speed
    Acceleration duration ratio
    Deceleration duration ratio
  Smaller chi-squared value is higher priority
The number of potential STs in each ST duration
  Longer ST has more potential STs since it has bigger influence on chi-square value.
  Total number of combinations is less than 107～8 .
    Approximately 3 days on Xeon X5492 (Quad core, 3.4GHz)
X1
X2
X3
X4
X5 sec.
Y sec.
N units
N * X5/Y units
N * X4/Y
・・・