## Slide 1: WLTC* Construction
Proposed by Japan
GRPE/WLTP-IG/ DHC subgroup
14 October 2010
*) WLTC : Worldwide harmonized Light-duty driving Test Cycle

## Slide 2
Contents
Cycle Construction
Cold/Hot Start Weighting
Gear Shift Points
Table of Contents

## Slide 3: 1. Cycle Construction
Cycle Construction
  1.1. Current Test Cycle in EU, US and Japan
  1.2. Requirement on Test Cycle
  1.3. Proposed Cycle Construction
  1.4. Justifications

## Slide 4
1.1. Current Cycle Construction
 | Urban / Rural | Motorway | Aggressive mode | AC test
US | Cold start Hot | Hot start | Hot start | Hot start
EU | Cold start |  | NA | NA
JAPAN | Cold start and Hot start |  | NA | NA
10 min.soak
According to WLTP-DHC-05-04, Urban/Rural/Motorway phase will be converted to Low/Middle/High phase respectively.
(independent test
with preconditioning)

## Slide 5
Flexibility
Unique test procedure
HEV
Regeneration system
EV range
Unique Vehicle
City commuter
Low power vehicle
1.2. Requirement on Test Cycle
Representativeness
Driving characteristic
Cold start (e.g. 6 or 12 hours soak)
Hot start
intermediate soak (e.g. 10 min. soak)
warm up (e.g. 15 min. drive @ 60kph)
Performance
Emission
Fuel consumption/GHG
Target Area
Test effectiveness
Equipment restriction
Chassis dynamometer
Bag analysis duration
Minimum sample volume
Test flexibility
Human respect

## Slide 6
Low phase
Middle phase
High phase
1.3. Proposed Cycle Construction
Cold start
Hot start
Low phase
Middle phase
TL
TM
TL + TM = equal to or less than 1372 sec.
TL : TM =
TH= equal to or less than 765 sec.
can be skipped if same condition as cold start phase
High phase test can be conducted after middle phase or independently

## Slide 7
1.4. Justifications
Representativeness
Driving characteristic
Cold start
Hot start
intermediate soak (e.g. 10 min. soak)
warm up (e.g. 15 min. drive @ 60kph)
Performance
Emission
Fuel consumption/GHG
Flexibility
Unique test procedure
HEV
Regeneration system
EV range
Unique Vehicle
City commuter
Low power vehicle
Test effectiveness
Equipment restriction
Chassis dynamometer
Bag analysis duration
Minimum sample volume
Test flexibility
Human respect
Low phase should be first
No WF in each phase is best solution.
Each phase duration should be based on
the traffic volume ratio.
Current longest cycle duration is first step.
Independent high phase test is inevitable.
Either condition is acceptable by adjusting
the Cold/Hot weighting factor. The “warm up” condition is more effective for testing flexibility.

## Slide 8: 2. Cold/Hot Start Weighting
Cold/Hot Start Weighting
  2.1. How to obtain real-world emissions ?
  2.2. Average Emission per Trip
  2.3. Cold Start Trip Ratio
  2.4. Calculation of Cold Weighting Factor
  2.5. Summary
  2.6. Required Data

## Slide 9: 2.1. How to obtain real-world emissions ?
Emission that should be evaluated
Average emission per trip
＝
◆Requirements
Average emission per trip
Emission during cold start trip
Emission during hot start trip
Emission under cold condition
Emission under hot condition
◆Detail of average emission per vehicle trip
Emission under hot condition

## Slide 10: 2.2. Average Emission per Trip and Cold Weighting Factor
Total Emission Etotal (g/km) formula is as following.
Cold start emission under cold condition
Cold start emission under hot condition
0 km
Dcycle
Dtrip
Cold start trip
×Rcold +
×(1 - Rcold)
Hot start emission
0 km
Dtrip
Hot start trip
EC (g/km)
EH (g/km)
EH (g/km)
ECT (g/km)
(*) ECT = (EC * Dcycle + EH * (Dtrip – Dcycle))/ Dtrip
Etotal = ECT * Rcold + EHT * (1 – Rcold)
= (Dcycle*Rcold/Dtrip) * EC + (1-Dcycle* Rcold/Dtrip) * EH
= WFC * EC + (1 - WFC) * EH
WFC = Dcycle * Rcold / Dtrip
WFc: Cold start weighting
Rcold: Cold start trip ratio
Dtrip: Average one trip distance (km)
Dcycle: Cycle distance (km)
ECT: Cold start trip emission (g/km)
EHT: Hot start trip emission (g/km)
EC: Cold start emission (g/km)
EH: Hot start emission (g/km)
EHT (g/km)
=

## Slide 11: 2.3. Cold Start Trip Ratio
Ambient temp.
Frequency
Soak time
◆Frequency of soak time
◆Cold start factor
Coolant temp. drop ratio
Coolant temp.
Soak time
i
Cold start trip ratio Rcold :
Where,
Rcold: Cold start trip ratio (= Average cold start emission increment ratio)
Fsoak: Frequency of soak time
Fcold: Cold start factor (Coolant temp. drop ratio )
Generate the cold start trip ratio by multiplying the soak time distribution and the coolant temperature drop ratio as the emission increase ratio
Fsoak(i)
Fcold(i)

## Slide 12: 2.4.1. Calculation Sample
Low/Mid. Hot
Cold Start Trip
★Low/Mid. cold + Low/Mid hot + High hot
High Hot
WF | WLM |  | WH
Distance (km) | Dtrip |  | 
 | Dtrip * WLM |  | Dtrip * WH
 | DC,LM | Dtrip * WLM – DC,LM | 
Emission (g/km) | ECT |  | 
 | EC,LM | EH,LM | EH,H
Mass (g) | MCT |  | 
 | DC,LM * EC,LM | (DT * WLM – DC,LM) * EH,LM | (Dtrip * WH) * EH,H
ECT = MC,T / Dtrip
= (DC,LM * EC,LM + (Dtrip * WLM – DC,LM) * EH,LM + (Dtrip * WH) * EH,H) / Dtrip
◆Emission during cold start trip ECT (g/km)
Low/Mid. Cold

## Slide 13: 2.4.2 Calculation Sample
EHT = WLM * EH,LM + WH * EH,H
◆Emission during hot start trip EHT (g/km)
Etotal = ECT * Rcold + EHT * (1 – Rcold)
= (DC,LM * Rcold / Dtrip) * EC,L + (WLM – DC,LM * Rcold / Dtrip) * EH,L + WH * EH,H
= WFLM,C * EC,L + WFLM,H * EH,L + WFH,H * EH,H
◆Total emission Etotal (g/km)
WFLM,C = DC,LM * Rcold / Dtrip
WFLM,H = WLM – DC,LM * Rcold / Dtrip
WFH,H = WH
◆Cold/Hot weighting factor
★Low cold + Low hot + Middle hot + High hot (conti.)
Low/Mid. Hot
EH,LM (g/km)
High Hot
EH,H (g/km)
Dtrip * WH
Dtrip * WLM

## Slide 14: 2.5. Summary
◆Required information/data
  Investigate the following two items based on actual vehicle usage
    Distribution of soak time
    Driving distance per trip
  Investigate the following based on engine bench test
    Coolant temperature drop ratio
  Other factors
    Test cycle distance
    The ratio of traffic volume in each phase (L/M/H)
In Japan, these figures are obtained based on survey and traffic senses.
◆Calculation process
  Calculate cold start trip ratio
    Generate the cold start ratio by multiplying the soak time
    distribution and the coolant temperature drop ratio
  Calculate cold start WF
    Generate the cold start WF based on average one trip distance
    cold start trip ratio and test cycle distance

## Slide 15: 2.6. Required Data -1
◆Distribution of soak time
Soak time | Frequency | 
 | Passenger Car | Light duty commercial vehicle
(hour) | (%) | (%)
0 – 0.25 | 10.0 | 10.0
0.25 – 0.5 | 11.0 | 11.0
0.5– 0.75 | 7.0 | 7.0
0.75 – 1.0 | 12.0 | 12.0
1.0 – 2.0 | 10.0 | 10.0
2.0 – 3.0 | 5.0 | 5.0
3.0 – 4.0 | 3.0 | 3.0
4.0 – 5.0 | 2.0 | 2.0
5.0 – 6.0 | 3.0 | 3.0
6.0 – 9.0 | 6.0 | 6.0
9.0 – 12.0 | 18.0 | 18.0
12.0 – 24.0 | 5.0 | 5.0
24.0 -48.0 | 3.0 | 3.0
48.0 - | 4.0 | 4.0
Total | 100.0 | 100.0

## Slide 16: 2.6. Required Data -2
◆Cold start factor
Soak time | Passenger car |  | Light duty commercial vehicle | 
 | Coolant temp. | Cold start factor | Coolant temp. | Cold start factor
(hour) | (℃) | (-) | (℃) | (-)
0 | 110 | 0 |  | 
0 – 0.25 | 73 | 0.41 |  | 
0.25 – 0.5 | 47 | 0.70 |  | 
0.5– 0.75 | 40 | 0.78 |  | 
0.75 – 1.0 | 36 | 0.82 |  | 
1.0 – 2.0 | 29 | 0.90 |  | 
2.0 – 3.0 | 25 | 0.95 |  | 
3.0 – 4.0 | 22 | 0.98 |  | 
4.0 – 5.0 | 20 | 1.0 |  | 
5.0 – 6.0 | 20 | 1.0 |  | 
6.0 – 9.0 | 20 | 1.0 |  | 
9.0 – 12.0 | 20 | 1.0 |  | 
12.0 – 24.0 | 20 | 1.0 |  | 
24.0 -48.0 | 20 | 1.0 |  | 
48.0 - | 20 | 1.0 |  | 

## Slide 17: 3. Gear Shift Points
Gear Shift Points
3.1. Analysis Method
3.2. How to define the gear position ?
3.3. Definition of Shift Change
3.4. Factor Analysis / Frequency Distribution
3.5. Regression Analysis
3.6. Analysis Sample (JC08)

## Slide 18: 3.1. Analysis Method
In-use data collection
Factor analysis
Frequency distribution
Regression Analysis
Develop Shift point equation
Validation
G(x)=a*V+b*A+・・・・
Developed gear shift points based on in-use survey to represent the real driving behavior.
ex. 2nd Gear Analysis

## Slide 19: 3.2. How to define the gear position ?
In case of manual gear shift, the formula for calculating vehicle speed would be the following if the clutch was engaged.
Consequently, gear position can be defined by calculating gear ratio during driving
where,
V: Vehicle speed (km/h)
Ne: Engine speed (1/min)
r: radius of tire
it: Gear ratio
if: final reduction ratio

## Slide 20: 3.3. Definition of Shift Change
Shift up_1: Clutch release point for up-shifting
Shift up_2: Clutch engage point after putting in higher gear
Shift down_1: Clutch release point for down-shifting or neutral

## Slide 21: 3.4. Factor Analysis / Frequency Distribution
Calculate the vehicle speed in each gear position (both up-shift and down-shift), then generate various frequency distribution by each vehicle category and analyze the factors that effect shift operation.
  Vehicle speed frequency distribution （0 ≤ V ≤ 100 km/h，1km/h step）
  Vehicle acceleration frequency distribution （-10 ≤ a ≤ 10 km/h/s, 1km/h/s step）
  Engine speed frequency distribution （600 ≤ r ≤ 6000 rpm, 100rpm step）
  Standardized engine speed frequency distribution （0 ≤ r ≤ 100 %, 10 % step）

## Slide 22: 3.5.1. Regression Analysis
Develop the shift point equation by Stepwise selection method
Dependent variable | Explanatory variable | Remark
Gear position | Vehicle speed (km/h) | 
 | Engine speed (1/min) | 
 | Normalized engine speed (%) | 
 | Acceleration (km/h/s) | 
 | Vehicle category | 1: M1, 2: N1, 3: N2,,,
 | Fuel type | 1: Petrol, 2: Diesel, 3: LPG,,,
 | No. of gear | 
 | Curb weight (kg) | 
 | Maximum pay load (kg) | 
 | Gross vehicle weight (kg) | 
 | Displacement (cc) | 
 | Maximum power (kW) | 
 | Maximum torque (Nm) | 
 | Power to mass ratio (kW/t) | 
 | Torque to mass ratio (Nm/t) | 
 | Normalized vehicle weight | Wn = Curb weight / GVW
 | Drive train coefficient (DTC) | Refer slide 3.5.2

## Slide 23: 3.5.2. Drive Train Coefficient （DTC）
DTC : Drive Train Coefficient
2πr / (im * if) ： running distance
per engine speed (m)
r ： tire radius (m)
im ： gear ratio
if ： final reduction gear ratio
V ： vehicle speed （km/h）
Ne ： engine speed （rpm）
y = DTC * G(x)
G(x)
Final reduction gear

## Slide 24: 3.6.1. Analysis Sample (JC08) - shift up speed

## Slide 25: 3.6.2. Analysis Sample (JC08) - downshift speed

## Slide 26: 3.6.3. Analysis Sample (JC08) - Explanatory variable of shift up
After completion of all data acquisition, the explanatory variable will be determined based on stepwise selection method.

## Slide 27: 3.6.4. Analysis Sample (JC08) - Explanatory variable of downshift
After completion of all data acquisition, the explanatory variable will be determined based on stepwise selection method.

## Slide 28: 3.6.5. Analysis Sample (JC08) - Gearshift equation
Shift up
Shift down
G(x) :Gearshift equation
V :Speed in km/h
A :Acceleration in km/h/s
Wn :Normalized vehicle weight (Curb weight / GVW)
E :Engine speed in rpm
DTC :Drive train coefficient
After completion of all data acquisition, the gearshift equation for WLTC will be developed.

## Slide 29: 3.6.6. Analysis Sample (JC08) – Final Shift Points
Vehicle Categorization
  Passenger Car
  Light Duty
  Commercial Vehicle
◆for Passenger cars
◆for Light duty commercial vehicles
Average of PC
Wn=0.80, DTC=0.11
Average of LDCV
Wn=0.58, DTC=0.09