## Slide 1: WLTP Test Procedures for Hybrid Electric Vehicle Testing
Chris Nevers - U.S. EPA
April 14, 2010
WLTP-DTP-01-12

## Slide 2: Outline
Overview of current US domestic test
Overview of test procedure opportunities
Keys to hybrid electric testing

## Slide 3: Current Test Procedures
The United States currently regulates passenger cars utilizing 40 CFR Part 86.
For Light Duty Hybrid Electric Vehicles, part 86 references California Exhaust Standards and Test Procedures for 2003 and Subsequent Model Zero-Emission Vehicles and 2001 and Subsequent Model Hybrid Electric Vehicles
Room for improvement in end of test criteria, retest criteria/ testing variability, complexity reduction

## Slide 4: Current HEV Procedures
Sampling/ data collection additions to conventional vehicle
  Integrated Amp-hours (State of Charge)
  Full double UDDS (4 bag FTP), no stabilized substitution
  Evaporative worse case emissions still requires 3 bag FTP
Unique Procedures
  Dynamometer Road Load Derivation (regenerative braking disabled)
  Regenerative braking differences (on road versus dynamometer)
  Canister load for non-integrated canisters

## Slide 5: Current PHEV Procedures
Sampling/ data collection additions to conventional HEV vehicle
  Recharge Amp hours
Unique Procedures (add. to conv. HEV)
  Testing throughout entire charge deplete range
  Charge deplete end of test criteria

## Slide 6: Procedure Opportunities
End of Test Criteria (PHEV/ HEV)
  Allow maximum effort for driver trace without terminating test
  Charge sustain operation could be ended before CS SOC is reached
Retest Criteria (PHEV/ HEV)
  State of Charge correction factor
  Energy Analysis, similar to Test Cycle Power Calculator
All Electric Testing (EV/ PHEV)
  Allow substitution for multiple vehicle applications of same battery using different vehicle loads

## Slide 7: Procedure Concerns
Double Cold Jeopardy (PHEV)
Test on 4wd dynamometers where applicable (all regen)
Coast down Techniques without true mechanical neutral ( On-Road)
Test Vehicle miles
System Durability beyond criteria pollutant impact

## Slide 8: Keys to HEV Test Procedures
Provide building blocks for array of possible CO2, criteria pollutant, and alternative fuel programs beyond worse case emissions
  Electric range/ usage
  CO2 displacement
  “zero emission” programs
  Alternative fuel programs
Level Playing Field
  Test procedures that are unique to HEV are needed to quantify HEV operation and are not designed to benefit one technology over another