## Slide 1: WLTP Test Procedures for Chassis Dynamometer Testing
Chris Laroo - U.S. EPA
April 14, 2010
WLTP-DTP-01-13

## Slide 2: Outline
Overview of current US domestic test procedures, WHDC, and NRMM GTR
Overview of proposed WLTP test procedures
Conclusions

## Slide 3: Current Test Procedures
The United States currently regulates passenger cars utilizing 40 CFR Part 86.
For engine testing, we regulate to 40 CFR Part 1065.
Recently the NRMM GTR was finalized
  The test procedures in this document closely resemble 1065.
  WHDC GTR also closely resembles 1065.
EPA believes that 40 CFR Part 1065 should be adapted to chassis testing to create a more robust test procedure.

## Slide 4: Draft WLTP Test Procedure Organization
Section and Title Intended Audience
100s Dynamometer Laboratory Equipment Specifications Lab Facilities
200s Measurement Instruments Instrument Procurement
300s Calibrations and Performance Checks Instrument Operator
500s Dynamometer Laboratory Test Protocols Test Operator
600s Calculations and Required Data for Certification Reporting Engineer
700s Analytical Gases Supply Procurement
800s Testing with Oxygenated Fuels Specialized Technician
1000s Definitions and Other Reference Information All

## Slide 5: Highlights
Uses International System of Units (SI) “metric”
Measurement and control specifications scaled to
  Emissions standards
  Specified gas standard accuracy scaled as function of emissions standards

## Slide 6: Highlights
Molar based emission calculations
  Uses chemical balance, iteratively solved, to determine
    Removed water correction
    Amount of dilution gas per mole of exhaust, xdil/exh
    Requires only total dilute exhaust flow measurement
  Provides for a more robust emission calculation and background correction.
  Note, chemical balance is not necessary if you directly measure two of the following flow rates:
    Dilution air flow – Used directly for background mass emission calculation
    Exhaust flow – Used to determine dilution air or CVS total flow
    Dilute exhaust total flow – Used directly in vehicle mass emission calculation

## Slide 7: 100s: Equipment
Dilution equipment
Probes, sample lines: heated as necessary
Sample-conditioning equipment
  NO2 to NO converter
  Dryers
  Pumps
  PM preclassifiers
PM sampling and stabilization conditions

## Slide 8: 200s and 300s
Measurement Parameter | 200s: Instrument Specifications | 300s: Calibrations Verifications
Update and Record | 202 | 
Press, Temp, Dewpoint | 215 | 315
Diluted Exh. Flow | 240 | 340, 341
Sample Flow | 245 | .345
Gas Divider | 248 | 307

## Slide 9: Subparts C and D
Measurement Parameter | 200s: Instrument Specifications | 300s: Performance Checks
CO and CO2 | 250 | 350, 355
NMHC | 260, 265 | 360, 362, 365
NOx | 270, 272 | 370, 372, 376, 378
PM, gravimetric balance | 290 | 390
PM, inertial balance | 295 | 395

## Slide 10: Highlighted Verifications
303: Verification frequency
  Linearity, response, leaks, interference, penetration, quench, conversion efficiency…
307: Linearity
  Verifies calibrations
  Note 35-day gas analyzer linearity verifications
308 and 309: signal update, response, and alignment
  For continuous gas analyzers

## Slide 11: 500s: Performing an Emission Test
510 Dynamometer procedure
515 Pre-test checks
520 Emission Test Sequence
525 Vehicle starting and restarting
550 Gas analyzer range validation, drift validation
Validation of test driver power demand
590 PM sampling media (e.g., filters) preconditioning and tare weighing
595 PM sample post-conditioning and total weighing.

## Slide 12: 600s: Calculations
Examples
  General statistics
  Molar based emissions calculations
  Removed water correction
  Drift validation and correction

## Slide 13: 600: Mass emission and background calculations
Mass emission calculation
  Here ndot is the dilute exhaust flow rate
  For background determination, ndot is the dilution air flow rate
Background mass calculation using chemical balance

## Slide 14: Conclusions
EPA believes that one set of improved test procedures for labs should improve repeatability
One set of test procedures provides pathway for significant international harmonization across all testing platforms
40 CFR 1065 should be used as a basis for international harmonization across all certification platforms (chassis and engine).