## Slide 1: WLTP DTP PM-PN Subgroup Activities, Progress & Future Plans
3rd DTP Meeting
Vienna
12th October 2010
Chris Parkin

## Slide 2: Outline
      Objectives for June-October
      Meetings Held
      Small Groups
      Open Issues
      Cross sub-group Issues
      Future Plans

## Slide 3: Outline
      Objectives for June-October
      Meetings Held
      Small Groups
      Open Issues
      Cross sub-group Issues
      Future Plans

## Slide 4: Objectives June – October 2010
To identify PM-PN relevant content in regional legislation
To identify differences (“Open Issues”) in PM relevant content for discussion and resolution in next phase
To identify elements of PN measurement procedures worth reviewing based on practical experience with PN measurement to date

## Slide 5: Objectives June - October
Documents
Terms of Reference & Plan of Activity
  WLTP-DTP-PMPN-01-02
Regional Legislation
  US CFR Parts 86 & 1065, Manufacturer Guidance Letters (CISD-06-20, CCD-04-08, CCD-01-01, CISD-OB-17)
  Japan Attachment 42
  UN-ECE Reg 83.05

## Slide 6: Outline
      Objectives for June-October
      Meetings Held
      Small Groups
      Open Issues
      Cross sub-group Issues
      Future Plans

## Slide 7: Subgroup Meetings Held
1st Web Conference – 7th July
  Agreed Terms of Reference and Plan of Activity
  Agreed decision on whether to mandate both PM and PN measurement was for DTP, WLTP or GRPE
  Measurement ranges of <2 – 50mg/km PM & <6x1011 – 5x1013 #/km PN (to include OBD test cases)
  PN during regen identified as an Open Issue
2nd Web Conference – 11th August
  Regulatory content comparison work subdivided into themes for examination by “small groups”
  Use of secondary dilution, CVS max temperature during regen and background correction identified as additional Open Issues

## Slide 8: Subgroup Meetings Held
3rd Web Conference - 15th September
  Relevant regulatory content template completed
  Small group regulatory comparison initial conclusions reported
  Planning of further small group meetings
4th Web Conference – 1st October
  Further conclusions from small group regulatory comparison work reported
  Plan of post October Activity agreed

## Slide 9: Small Groups
Subjects | Leader
Transfer, dilution system, residence time, diluent conditioning, PM probe, sample conditions, filter holder & media, residence times | Les Hill – Horiba les.hill@horiba.com
Weighing chamber & balance spec, PM sampling preparation, calculations, corrections & calibration | Phil Price – Ford pprice40@ford.com
DPF periodic regeneration, degreening and stabilisation/loading | Penny Dilara - JRC panagiota.dilara@jrc.ec.europa.eu
PN measurement system specification, calculations, corrections & calibration | Chris Parkin – DfT chris.parkin@dft.gsi.gov.uk

## Slide 10: Outline
      Objectives for June-October
      Meetings Held
      Small Groups
      Open Issues
      Cross sub-group Issues
      Future Plans

## Slide 11: Open Issues
Transfer & dilution system
Transfer tube insulation (Jp) or heating or remote mixing tee for SI
Determination of transfer tube length, especially where remote mixing tee used
Permissible variation in static pressure at tailpipe +/-0.1kPa @ 70km/h (Jp), +/-1.25kPa (US), +/-0.75kPa @ 50km/h +/-1.25kPa full test (ECE)
Dilution tunnel design, length, residence time, heating, PM probe location
Dilution air filtration efficiency 99.97% (US), 99.95% or H13 (ECE)
Dilution air temperature >15°C (Jp), 25°C +/-5°C (US)
CVS temperature during regen <190°C (ECE & Jp), <52°C single dilution <190°C double dilution (US)
Prevention of condensation, heating of surfaces (US)

## Slide 12: Open Issues
Transfer & dilution system
Clarification of measurement point for requirements on dilution tunnel pressure at mixing point
CVS suction device capable of 5-7 dilution factor (US), preventing water condensation (ECE). Maximum CO2 concentration needs to be specified for E85
CVS residence time 1-5 seconds (US), undefined (ECE)
Heat exchanger required (Jp & US Part 86), not required (ECE & US part 1065)
Double dilution permitted (Jp & US), not permitted (ECE)
Pre-conditioning for tunnel (ECE & US) or vehicle (ECE)
Molar or volume based calculations

## Slide 13: Open Issues
PM probe & sampling
PM sample probe internal diameter 12mm (ECE)
PM transfer tube length (ECE) or residence time (US) spec
Confirmation of proportionality of PM sampling +/-5% (ECE) , various (US)
Minimum data logging rates for this
PM flow meter temperature variation +/-3K, unnecessary with real time flow calculation
Bare wire thermocouple design (US)
PM flow meter calibration requirements at test flow rate (ECE) over range (US)
Pre-classifier must be immediately upstream of filter holder (Jp), only permitted with sharp edged probe (US). ECE text less clear, apparently more flexible.
Location of PM sampling pump, on filter holder (Jp)

## Slide 14: Open Issues
PM Filter Media & Conditions
PM filter PTFE membrane recommended (US) membrane or coated (ECE)
PM filter specification 99% 0.3m DOP @ 35cm/s (ECE) @35-100cm/s (Jp)
PM filter holder specific design (US) or “even flow distribution” (ECE)
PM filter holder minimum stain area diameter 37mm (Jp & ECE) 38mm (US)
PM filter(s) single (ECE), one for each phase (US)
Recommended minimum filter loading 20g (ECE) none (Jp)
PM filter face temperature <52°C (ECE & Jp), 47 +/-5°C (US)
PM filter face velocity 20-80cm/s (ECE), 100-105 cm/s (US), 35-100cm/s (Jp)

## Slide 15: Open Issues
Weighing chamber & microbalance
Tolerances for temperature, dew point temperature and relative humidity. Not all regions have requirements for all three parameters.
Micro-balance precision tighter in US 1065 & J42 than for US 86 and R83. Various recommendations are given for micro-gram balance installation, static neutralisation & shielding.
Filter conditioning time US 1065 has no maximum time. Differences exist in max time permitted between removal of filter from stabilisation environment and emissions test; time allowed to return filter to stabilisation environment after the emissions test; and max conditioning time permitted.
Sample filter handling various guidance provided.

## Slide 16: Open Issues
Weighing chamber & microbalance
Microbalance calibration weight requirements not specified (US part 86 & ECE), “E2” weights (Jp), NIST traceable within 0.1 % uncertainty (US part 1065). Only US part 1065 puts a specification on cal mass relative to unused filter mass.
Microbalance calibration frequency discrepancy between zero/span requirements and annual cal requirements.
Reference filter weighing, max time between sample and ref filter weighing after the emissions test vary. Acceptance criteria and actions if initial results out of tolerance vary. US part 86 requires ref filters to be covered at all times. US part 1065 recommends balance exercise and substitution weighing method.
PM calculations equivalent except US 1065 generalised, not CVS specific.
PM dilution air background correction permitted (US & Jp), tunnel background permitted (ECE)

## Slide 17: Open Issues
PN
VPR filtration specification for dilution air and leak checks
VPR minimum solid particle penetration efficiency (none at present ECE)
Background correction consistency with PM
PN measurement during DPF regen
  Is VPR volatile removal efficiency sufficient
  Is tetracontane appropriate for evaluating efficiency if used for regeneration measurements
PNC calibration frequency (12 months)
PNC calibration aerosol materials
PNC flow check tolerance (+/-5%)
VPR particle concentration factor validation (3 monodisperse sizes)

## Slide 18: Outline
      Objectives for June-October
      Meetings Held
      Small Groups
      Open Issues
      Cross sub-group Issues
      Future Plans

## Slide 19: Cross Subgroup Issues
Issue | Relevant Subgroup
CVS specification – dimensions, temperatures, residence time | Lab processes
Dilution air filtration efficiency | Lab processes
Prevention of condensation in dilution and PM sampling system | Lab processes

## Slide 20: Outline
      Objectives for June-October
      Meetings Held
      Small Groups
      Open Issues
      Cross sub-group Issues
      Future Plans

## Slide 21: Future Plans
November 2010 – May 2011
Objectives
  Gather (primarily existing) data to review and resolve Open Issues
  Commence drafting of PM-PN elements of GTR text
Working Method
  Subject specific “small groups”, meeting by web and telephone conference, will gather data and develop proposed solutions to Open Issues
  Proposed solutions, along with rationales, will be circulated to the subgroup. The subgroup will decide whether to accept the proposed solution or refer back to the small group for further consideration

## Slide 22: Future Plans
June 2011
Objectives
  Reach final agreement on all Open Issues
  Continue drafting PM-PN elements of GTR text
July – September 2011
Objectives
  Complete drafting of PM-PN elements of GTR text