## Slide 1
Proposal of the
Warning Timing for AEBS
AEBS/LDWS-05-04

## Slide 2
1. Proposal of Warning Timing
2) Since the warning timing is based on the driver
response time, common value of warning timing
shall be used for
① Vehicles in all categories
② Both moving and stationary target
③ Both high speed and low speed range
1) Warning for AEBS shall be given at least 0.8
second before the activation of emergency brake.

## Slide 3
2. Driver Reaction Time
Experiments on driving simulator
20 panels
With different sleepiness level
Experimental Scenario
Study on Driver Reaction Time in FVCWS (1999, JARI)

## Slide 4
2. Driver Reaction Time
Result 1: Braking Time from Preceding Vehicle’s Deceleration
Without warnings, the braking time increases with the level of sleepiness.
With warnings, the braking time does not increase.
Level of Sleepiness
Difference of Braking Time
from Normal Awareness
Situation sec.
0
1
2
3
○
Without
Warnings
●
With
Warnings

## Slide 5
2. Driver Reaction Time
Level of Sleepiness
Driver Reaction Time sec.
1
0
2
3
Result 2: Driver Reaction Time
When drivers are sleepy (level 2 - 3), average reaction time is 0.75 sec..