## Slide 1
<number>
Warning Timing, Driver Distraction, and Driver Response to Imminent Rear-End Collisions
review of some research literature referred to in the ITS guidelines for high-priority warnings
AEBS/LDWS-06-08

## Slide 2
<number>
ITS guidelines for high-priority warnings
(WP.29-150.22)

## Slide 3
<number>
ITS guidelines for high-priority warnings
(WP.29-150.22)

## Slide 4
<number>
Effect of warning timing on collision avoidance
Note: RECAS = Rear-End Collision Avoidance System

## Slide 5
<number>
Effect of warning timing on collision avoidance
The data demonstrate that RECAS warnings provide a substantial benefit, particularly if the warning is given early.
Compared with no warning at all, an early RECAS warning reduces the number of collisions by 80.7%.
Assuming that collision severity is proportional to kinetic energy, the early warning reduces collision severity by 96.5%.
In contrast, the late warning reduces collisions by 50.0% and severity by 87.5%.
Note: RECAS = Rear-End Collision Avoidance System

## Slide 6
<number>
Effect of warning timing on driver response

## Slide 7
<number>
Effect of warning timing on driver response
The data identify how a warning affects the driver response.
RECAS aids drivers in avoiding collisions by speeding accelerator release, but it does not enhance any other aspect of the response. Drivers do not depress the brake more quickly or brake harder when they receive a warning.
In fact, because compliance with the RECAS warning generated a faster accelerator release, drivers were able to brake more gradually. The difference in mean deceleration suggests a potential indirect benefit of the warning: less abrupt deceleration may decrease the risk of being struck from the rear, a common occurrence when abrupt deceleration of one vehicle triggers a multiple-car crash.

## Slide 8
<number>
Effect of warning timing and driver distraction on collision avoidance

## Slide 9
<number>
Effect of warning timing and driver distraction on collision avoidance
Collisions occurred for undistracted drivers 14.2% of the time
without a warning and 0.7% of the time when a warning was given.
In comparison, collisions occurred for distracted drivers 37.9% of the time without the warning and 2.1% when a warning was given.
The warning also reduced collision velocity: without a warning, drivers collided at 2.1 m/s, compared with 0.1 m/s for drivers who received a warning.
The warning also increased the minimum adjusted TTC: without a warning, drivers had a minimum adjusted TTC of 1.0 s, compared with 3.5 s for drivers who received a warning.
The data provide no evidence to suggest that providing undistracted drivers with a collision warning could degrade driving safety.

## Slide 10
<number>
Effect of warning timing and driver distraction on response time

## Slide 11
<number>
Effect of warning timing and driver distraction on response time
Neither warning nor distraction affected the transition time from accelerator to brake.
The warning did increase the time between initial brake press and maximum deceleration, however.
Given a warning, drivers moved from initial brake application to maximum brake application in 1.96 s, compared with 1.62 s for no warning. In contrast, distracted drivers depressed the brake faster than did undistracted drivers.
Both distracted drivers and undistracted drivers responded faster with the warning and maintained a greater safety margin.
The data do not indicate that a warning might undermine
safety for an undistracted driver.

## Slide 12
<number>
Conclusions
An early warning is of greater benefit than a late warning.
Drivers respond to the collision warning as automation that redirects attention, not as automation that triggers a
braking response. The data show that an enhanced accelerator release response is the only warning effect.
Consequently, the benefits of early warnings in providing drivers with additional time to interpret and respond to the situation probably outweigh the costs associated with inappropriate braking responses to nuisance alarms.
Both distracted and undistracted drivers benefited from the warning. Beyond the direct benefit of avoiding collisions with the lead vehicle, drivers who received the warning decelerated
more gradually, which may decrease the risk of being struck from the rear.