## Slide 1: Driver Reaction Time
AEBS/LDWS-07-05
20100913
Notes: <number>

## Slide 2
Event Recognition
Focus on
event
Event analysing
0,48s
0,93s
0,45s
Base re-
action time
Starting muscular reaction
0,19s
1,12s
Moving
foot
Touch brake pedal
Brake res-
ponse time
Brake pressure increase
0,05s
1,17s
0,17s
Pressure
Built up
Start ABS-Control
1,34s
The „Kölner-Modell“ was defined in 1982 and is still today legal basis for the German legal practice for traffic jurisdiction for passenger cars. (Burkhardt)
Recognition
Of warning
AEBS-warning (audible/haptical)

???
ABS braking
time
Vehicle stop
„Kölner-Modell“
Notes: <number>

## Slide 3: Influence factors
Anticipation of a incident
Age of the driver
Gender (female)
Medicine, alcohol
Wrong shoes
Imminent danger
More than one alternatives
Visibility conditions (darkness, low sun…)
Driver distraction (accident, fire, woman…)
Shorter Longer
Subjective!!
Notes: <number>

## Slide 4
Overview of research results
 | Situation | Brake reaction time
Rumar, K. (1971) | surprise situation in traffic | Av. 0,9s, 75%: 1,2s
Olson, P.L. (2002) | „straightforward“ | 90-95% between 0,75s and 1,5s
Green, M. (2000) | Expected event Unexpected event (e.g. Brake lights) - Surprise intrusion event (e.g. objects moving suddenly into the drivers path) | Av. = 0,75s Av. = 1,20s to 1,35s Av. = 1,50s
Summala (1990) | Real driving: suddenly stationary object | Reaction time between 0,86s and 1,39s
Mehmood (2009) | Driving simulator* - normal - surprise condition - stationary object | Reaction time between 0,92s und 1,94s Reaction time between 0,66s und 1,04s Reaction time between 0,58s und 0,94s
Burckhard (1985) | Tests and accident reality | Reaction time between 0,7s (2%) and 1,34s (98%)
Schmitt (2007) | Real driving: Emergency braking of preceeding vehicle | Reaction time between 0,51s ((5%) and 0,99s (95%)
Schittenhelm (2005) | Driving simulatior*: end of traffic jam, cut in of a vehicle | Av. Reaction time (w/o evasion manoeuvre): 0,95s Av. Reaction time (w/ evasion manoeuvre): 1,12s
Krause et al. (2007) | Real driving: suddenly critical object (bike coming from the right) | Av: 0,43-0,6s, 98%: 0,88s-1,13s
Notes: <number>

## Slide 5
CLEPA opinion: to give the driver a realistic chance, to react on the warning, we propose a warning time of min. 2s before the system reacts with emergency braking
Notes: <number>