## Slide 1
<number>
ACC, AEBS -> The same hardware in use
ACC: In ordinary situations
AEBS: In emergency situations
AEBS should be activated only in emergency situations.
Justification
If the system is activated only in emergency situations, rarely happen, the over-reliance does not occur to a driver.
AEBS/LDWS-10-04

## Slide 2
<number>
Drivers’ action
<In ordinary situations>
A driver operates the avoiding maneuver while TTC is long.
A driver does not operate braking with a high deceleration.
<In emergency situations>
A driver operates the avoiding maneuver after TTC becomes short.
A driver operates braking with a high deceleration to reduce the damage or to avoid a collision.
Justification

## Slide 3
Most drivers operate braking to avoid a collision at the earlier time than 1.6s at most of overlapping ratio.
There is no interference with drivers’ operations.
The speed reduction of Japan proposal is based on 1.6s.
Most drivers operate braking to avoid a collision at the earlier time than 3.0s in conditions of overlapping ratio 100%.
It is the number which distinguishes an ordinary driving from an emergency operation to avoid a collision.
Justification
<number>
TTC sec.
Unladen, V = 60 km/h
Overlapping Ratio %
Experiments
on proving ground
Real world
1.6sec.
Sampling on public roads
3sec
In ordinary
situations
In emergency
situations
Requirements of AEBS’s deceleration are based on here.
Requirements of AEBS’s activation
Drivers’ avoiding maneuver for forward obstacles
Notes: <number>

## Slide 4
Justification
If the system is activated only in emergency situations, the over-reliance does not occur to a driver.
TTC equal to or less than 3.0s is for a definition of the emergency area.
If AEBS is activated in other situations except emergency, it is a problem because it affects other traffic.