## Slide 1
Vehicle Stability Function
● Directional Control ● Roll-over Control
A functional overview with regard to commercial vehicles
AMEVSC-03-04e August 2010
Prepared by AMEVSC Secretary

## Slide 2
Vehicle Stability Function – functional overview
● Directional Control
● Roll-over Control
an electronic control function for a vehicle which improves the dynamic stability of the vehicle.
● Vehicle Stability Function
Definitions *
* UN ECE Regulation 13 paragraph 2.34.
a function within a vehicle stability function that assists the driver, in the event of under steer and over steer conditions, within the physical limits of the vehicle in maintaining the direction intended by the driver in the case of a power-driven vehicle, and assists in maintaining the direction of the trailer with that of the towing vehicle in the case of a trailer.
a function within a vehicle stability function that reacts to an impending roll-over in order to stabilise the power-driven vehicle or towing vehicle and trailer combination or the trailer during dynamic manoeuvres within the physical limits of the vehicle.
AMEVSC-02-08e August 2010

## Slide 3
Vehicle Stability Function – functional overview
Conditions influencing functionality
High unladen/laden ratio (7,5 tons to >40 tons)
Complex physics due to additional degrees of freedom (tractor/semi-trailer combinations)
High/variable center of gravity
Huge number of vehicle variants (geometry, axles, suspension, engines, cabs etc.)
Large number of different vehicle combinations and payloads (unknown trailers, load etc.)
High demands concerning driver acceptance (professional drivers and priority placed on traction)
AMEVSC-02-08e August 2010

## Slide 4
Vehicle Stability Function – functional overview
Over-steering – directional control stabilizing interventions
Over-steering
Loss of lateral control at motor vehicle rear axle
Danger of jack-knifing for tractor/semi-trailer combinations
Directional control intervention
Braking of outside front wheel
Reduction of engine torque
Braking of trailer (stretch braking)
=> Vehicle stability maintained
AMEVSC-02-08e August 2010

## Slide 5
Vehicle Stability Function – functional overview
Under-steering – directional control stabilizing interventions
Under-steering
Loss of lateral control at motor vehicle front axle
Danger of running off the road
Directional control intervention
Braking of inside rear wheel
Reduction of engine torque
=> Vehicle stability maintained
AMEVSC-02-08e August 2010

## Slide 6
Vehicle Stability Function – functional overview
Directional control process
Vehicle
dynamics
Steering
Drive train/
Brakes
Driver
Direction control function
Sensors
Environment
control
strategy
reference
model
steering
angle
controller
control error
vehicle
braking pressures
and engine control
YRS
measured yaw rate
vehicle
speed
band of
desired yaw rate
Control loop
Block diagram
Control algorithm adapted to actual vehicle configuration and wheelbase through end-of-line programming - intervention threshold adapted
Driver selected direction of travel – steering wheel angle sensor
Actual direction of travel – yaw rate sensor
Vehicle speed – ABS wheel speed sensors
Appropriate application of brakes and engine torque reduction when actual yaw rate crosses the intervention threshold
AMEVSC-02-08e August 2010

## Slide 7
Vehicle Stability Function – functional overview
Directional control process
45
46
47
48
49
50
51
52
53
54
55
-0.4
-0.2
0
0.2
0.4
Time [s]
Yaw Rate [rad/s]
Intervention Threshold
Measured Yaw Rate
Start of Intervention
Stop of Intervention
AMEVSC-02-08e August 2010

## Slide 8
Vehicle Stability Function – functional overview
Roll-over control stabilizing interventions
Rolling-over
The force resulting from the vehicle weight and its centrifugal force at the centre of gravity, acting outside the effective track causes the vehicle to roll-over
Roll-over control intervention
Once the lateral acceleration of the vehicle exceeds the intervention threshold, the vehicle speed is reduced by automatically applying the brakes and reducing the engine power
If wheel ‘lift off’ is detected maximum vehicle speed reduction is requested
Effective track
AMEVSC-02-08e August 2010

## Slide 9
Vehicle Stability Function – functional overview
Roll-over control process
Control algorithm based on lateral acceleration with intervention threshold derived from vehicle type, loading condition, fast/slow steering, travelling uphill/downhill, demanded engine torque by driver, taking into account e.g. frame stiffness, suspension, tires and driver acceptance considerations
Control algorithm adapted to actual vehicle configuration through end-of-line programming - intervention threshold adapted
Control algorithm adapts intervention threshold to actual loading condition of vehicle (centre of gravity height) – vehicle mass estimated from engine torque (engine management system information modified to account for drive-line losses) and vehicle acceleration (driver demand and wheel speed information
Appropriate application of brakes and engine torque reduction when actual lateral acceleration exceeds the intervention threshold
AMEVSC-02-08e August 2010

## Slide 10
Vehicle Stability Function – functional overview
Roll-over control process
Measured Lateral Acceleration
Start of Intervention
Stop of Intervention
Roll-over Threshold
Intervention Threshold
90
95
100
105
110
115
-7
-6
-5
-4
-3
-2
-1
0
1
Time [s]
Lateral Acceleration [m/s2]
AMEVSC-02-08e August 2010

## Slide 11
Vehicle Stability Function – functional overview
Towing vehicle and trailer combinations - trailer
Motor vehicle establishes if a trailer is connected using the trailer electrical demand via the electrical connectors between motor vehicle and trailer
  24N (ISO 1185) – stop lights
  5 pin ISO 7638 – ABS power and warning light
  7 pin ISO 7638 – CAN communication between trailer and motor vehicle braking ECU
Only stop light demand indicates a non ABS equipped trailer – typically no demand for trailer braking with unladen trailer, pulsed braking with laden trailer
ABS equipped trailer – no/low trailer braking demand with unladen trailer, trailer braking demand as determined appropriate by motor vehicle for part/fully laden trailer
CAN communication enables the motor vehicle to evaluate the trailer and request appropriate trailer braking. In the case of a self generated braking demand, e.g. trailer roll-over control, and motor vehicle requested trailer braking, the highest value is implemented
AMEVSC-02-08e August 2010

## Slide 12
Vehicle Stability Function – functional overview
Typical hardware – electronic braking system (EBS) (2 axle motor vehicle)
CAN J1939
CAN Brake
CAN Sensor
Steering angle sensor
Yaw rate and lateral acceleration sensor
1 channel pressure control modules
2 channel pressure control module
Trailer control
module
Engine ECU
Foot brake module
Retarder ECU
EBS ECU
Wheel speed sensors
AMEVSC-02-08e August 2010