## Slide 1
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Background
New applications involving the brake system are constantly approaching.
In the close perspective: Fully Automatic Coupling Systems, FACS
In a bit more distant perspective: “Totally Integrated Vehicle Combination Control Systems”, (TIVCCS)
The GRRF has previously got information about FACS.
TIVCCS involves control of propulsion, braking, handling, … for the entire vehicle combination.
  See Project description summary “Integrated control of Propulsion,Braking and steering of Long Modular Vehicle Combinations”, Reg. no. 2009-004340 with the Swedish Energy Agency
  This will include regenerative braking and propulsion in the trailers. For regenerative braking in general for commercial vehicles see:
  http://www.cvdc.org/recent_papers/Energy_Consumption_2009-09-23.pdf
These emerging application have in common that they are incompatible with the ISO7638 connector.
Transmitted by the experts from Sweden
Informal document No. GRRF-68-19
(68th GRRF, 21-23 September 2010
agenda item 3(e))

## Slide 2
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Proposal
Make ECE Regulation 13 more robust and resilient to take on these emergent challenges.
  In the definition section add definitions of the braking related signals handled through ISO7638 today.
    This is to remedy the lack of nomenclature causing ISO7638 “litter” all parts of the R13
    As a consequence nearly all references to ISO7638 are replaced with signal references
  New paragraphs are added to describe how the braking related signals shall be handled safely
    Traditional couplings stay with ISO7638
    FACS get strict requirements both for physical requirements and handling to prevent electrical coupling errors. Eventually standards like the in progress ISO13044-x will apply
    As TIVCCS come along a special paragraph will be added to rule how the braking/propulsion related signals are handled.
      Some new signals relevant may need to be defined.
    The remainder of the regulation text will stay unchanged.
Transmitted by the experts from Sweden

## Slide 3
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Justification
New technology applications will call for a more versatile handling of braking related signals.
The current way to use ISO7638 as an implicit definition of nomenclature for braking related signals has worked fine.
  Keep these benefits by the introduction of explicit definition of nomenclature.
    In this way we avoid exemption texts for new applications at all places where the implicit definition would have been used.
As new applications come along as it will, only limited changes to the R13 text will be needed
  The explicit definition of nomenclature may occasionally need to be changed
  A specific paragraph addressing the new application requirements would be needed.
    Full focus on the risks and merits of the particular application.
    Existing applications remain unchanged
Now is the right time to act on this matter
  Changes will inevitably be needed sooner rather then later.
  Now the complexity is “small” which reduces risk with doing the change.
Transmitted by the experts from Sweden

## Slide 4
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Thank you for your attention!
Transmitted by the experts from Sweden

## Slide 5
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Back UP
Transmitted by the experts from Sweden

## Slide 6
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Transmitted by the experts from Sweden

## Slide 7
Supporting document for Informal document No. GRRF-68-09 Presentation summary
Transmitted by the experts from Sweden