## Slide 1
The EC proposal contains the provisions as Annex 8 on technical services inter-laboratory comparison testing and machine alignment so as to minimize variances in the measurement results between technical services.
Basically Japan supports this idea, but
- The alignment procedures in the EC proposal is vague, and
- Current test procedures in ISO28580 does not specify to maintain the accuracy among each technical service test sites.
Background
Proposal for Alignment procedure using RRC value among Technical Services
Informal Document No. STD-04-11
1
Transmitted by the expert from Japan

## Slide 2
Japan proposal for Annex 8
To add Technical Services Alignment Procedure to obtain “RRC Standard Value” in the following slides.
2
Notes: <number>

## Slide 3
Technical Services |  |  |  |  | 
 | 7.2 | 8.3 | 9.8 | 10.8 | 12.0
 | 7.5 | 9.5 | 10.6 | 11.7 | 12.5
 | 7.3 | 8.6 | 9.6 | 10.6 | 11.7
 | 6.8 | 7.9 | 9.9 | 11.0 | 12.5
 | 7.4 | 8.5 | 9.6 | 11.1 | 12.3
Average | 7.5 | 8.6 | 9.9 | 11.0 | 12.2
D
E
② Measurement of alignment tyres
(using same batch tyre) at Technical Services (TSs)
Adopting average value as ‘Standard Value’
A
B
C
TS:
A
B
C
D
E
① Decide five Specific Alignment Tyres ( Para. 3)
1
2
3
4
5
1
2
3
4
5
3
Notes: <number>

## Slide 4
③ Calibration Formula
Transforming each site’s measurement value to calibrated value by using the correlation line which is calculated from the standard values.
B
Measurement Value Tested Tyre
A
Calibrated value
Measurement value in each site
4
Measurement value in each site
Calibrated value
Notes: <number>

## Slide 5
③ Calibration Formula
5
C
Calibrated value
Measurement value in each site
Calibrated value
Measurement value in each site
Calibrated value
Measurement value in each site
D
E
Notes: <number>

## Slide 6
③ Calibration Formula
（Example of transformation measurement value to calibration value）
A
Calibration Formula:
Calibration value (Evaluation value)
= (0.980 × Measurement value) + 0.411
6
7.2
12.0
7.5
12.2
9.00
9.231
Approximation line
Calibrated value
Measurement value in each site
If the measurement value is 9.00,
then the evaluation value is 9.231.
Notes: <number>

## Slide 7
Conclusion
Adopting the alignment procedures proposed among Technical Services, it will be possible equally to compare the compliance test results among different Type Approval Authorities.
7
Notes: <number>