## Slide 1
Regulation No. 117 – Annex 6
Annex 6 reflects part of ISO Standard 28580 (sections 1 – 9):
mainly terms and definitions, test conditions and data analysis
TEST PROCEDURE FOR MEASURING ROLLING RESISTANCE
STD-04-14

## Slide 2
Regulation No. 117 – Annex 9
e.g. how to perform the alignment between a Technical Service as aligned according to Annex 8 and any measurement machine
PROCEDURE FOR
MEASUREMENT MACHINES ALIGNMENT
AND MONITORING REQUIREMENTS

## Slide 3
Regulation No. 117 – Annex 8
Annex 8 is intended to describe the procedure to be followed to perform inter-laboratory comparison in order to define a reference machine as composed by multiple laboratory machines for the purpose of implementing rolling resistance machine alignment procedure.
The current Annex 8 text shall be improved to specify the criteria for such inter-laboratory comparison to define a reference machine as a network
PROCEDURE FOR TECHNICAL SERVICES INTER-LABORATORY COMPARISON

## Slide 4
Network of reference machines
Annex 8 and 9
how to make a network reference machine?
Annex 8: shall be detailed enough
how to align Candidate Labs with Reference lab?
Annex 9
(e.g. another procedure is defined in ISO28580)
Candidate labs

## Slide 5
The need of the alignment for different machines
Tire load (500kgf)
Tire load (500kgf)
Tire load (500kgf)
The same tire is measured on three different machines of same type…
4.5kgf
4.55kgf
4.35kgf
Machine A
Machine B
Machine C
RRC=9.0N/kN
RRC=9.1N/kN
RRC=8.7N/kN
Only 150g difference makes RRC going from 9.0N/kN to 8.7N/kN.

## Slide 6
This machines alignment procedure requires at least five predetermined alignment tyres of the same sizes used by the candidate laboratory operating the machine. The set of tyres is used to align several machines by comparing the measured Cr results among each laboratory. An inter-laboratory alignment formula is then established and shall be used to translate the results obtained on different machines into aligned results in order to define a reference machine as constituted by a network of multiple machines. Each machine in the network can provide assigned Cr values to candidate machines when aligning with one candidate.
Annex 8 and 9 are clearly very similar in the content: this is unavoidable because in both of them it is described an alignment procedure between laboratories which differ only for some boundary conditions due to their different purpose.
Regulation No. 117 – Annex 8 – ETRTO proposal

## Slide 7
Tyre Industry is asking for the creation of a Technical Support Group dedicated to Rolling
Resistance (RR) measurement machines alignment for the following reasons:
  A measurement machines alignment procedure is necessary in order to get comparative RR values and give an appropriate competitive playground for the declaration of RR labelling values according to European Regulation 1222/2009
  As of today this procedure shall be built up, because it is only partially described both within ISO28580 and, with some differences, within draft UN/ECE Regulation R117.02
  The procedure should be based upon the generation of Reference or "assigned" RR values through a Technical Services Inter-Laboratory comparison.
Regulation No. 117 – Annex 8 – ETRTO proposal
  Tyre Industry is asking for the creation of a Working Group, composed of the Technical Services willing to participate to the inter-laboratory comparison.
  A fast launch of this Working Group will allow Tyre Industry companies to quickly know the reference values in order to comply to the European Tyre Labelling Regulation where we need to start the tests of our tyre lines first quarter of 2011 at the latest.

## Slide 8
TECHNICAL PARAMETERS FOR THE ALIGNEMENT PROCEDURE
HOW A REFERENCE LAB COMPOSED BY SEVERAL LABS WORKS
PRINCIPLES
Regulation No. 117 – Annex 8 – ETRTO proposal
P.1
P.2
P.3

## Slide 9
The definition of a Virtual Lab: open points
An average is performed among the Type Approval Authorities in order to define the reference values to be used by the other Testing Machines to be aligned.
The same set of physical alignment tires circulated In Sequence for the alignment
TAA #1
TAA #2
TAA #3
TAA #4
TAA #i
TAA #1
TAA #2
TAA #3
TAA #4
TAA #i
The sets of similar alignment tires used In Parallel for the alignment
There are pro/cons in the 2 possibilities in terms of accuracy, efficiency,.. that can be further investigated

## Slide 10
The definition of a Virtual Lab: open points
How the correlation works
Tyre
Drum
Tyre
Drum
TESTING MACHINE A
TESTING MACHINE B
Measures the alignement tyres and obtains RRCs: Bx
RRCs
from B
RRCs
from A
A1
A2
B1
B2
Linear regression correlation formula by which any other RRC can be aligned to the other machine
Measures the alignement tyres and obtains RRCs: Ax
For a proper linear regression an appropriate “range” for Cr values should be considered (e.g. 3N/kN according to ISO28580, or 1.5±0.5N/kN according to Annex 9), depending also on the number of tyres.
Tyre Industry assessment need to be completed.