## Slide 1: LT/C Harmonization
Update for informal Tyre gtr group
24 September 2010
Working Paper N° : TYREGTR-09-06
(ETRTO – Progress on the harmonisation work for LT/C tyres)

## Slide 2: Timing
Phase 1: Harmonized requirements
for radial PC, non-harmonized
requirements for radial LT/C tyres
Q4
2009
Q1
2010
Q2
2010
Q3
2010
Q4
2010
Q1
2011
Q2
2011
Q3
2011
Q4
2011
2012
2013
2014
Meeting with some CPs, Technical
sponsor, Chairman of ad hoc WG at
WP29
Publication of draft GTR text
Meeting of ad hoc WG after GRRF;
validation of Roadmap
Take into account CP reactions to
GTR text
Adoption of draft GTR text with
harmonised PC tests by GRRF
Presentation of final draft GTR text
(PC only) to WP.29
Adoption of GTR text (Phase 1) by
WP.29
Q1
Adoption by UN in New York
Q2
Phase 2: Harmonized requirements
for all radial tyres for vehicles up to
4536 kg
Tyre Industry works on LT/C test
harmonisation (* = meetings of ad hoc
tyre GTR WG, where work will be
shared)
*
*
*
* *
* *
Q1, Q2
*
Presentation of proposal for validation
by CPs
Q3
Take into account CP reactions to
LT/C harmonisation proposal
Q3, Q4
Q1, Q2
Adoption of draft GTR (PC and LT/C)
by GRRF
Q3
Adoption of complete GTR (PC and
LT/C) by WP29
Q4
General
AC.3 works on "administrative
marking" issue for GTRs in general
Action plan to be defined by WP.29
AC3
Today
Today +
4 years

## Slide 3: Requirements to be Harmonized
High speed test (FMVSS 139 and R54)
Endurance test (?)
Physical dimensions test
  Pressures not yet harmonized, but not technically difficult
Plunger energy (breaking energy) test
  Limits in FMVSS 139 based on Load Range, which doesn't exist for all tires

## Slide 4: High Speed Test
Work has begun
Intent is to use same method as HS test for PC tyres
  Compare steps above limit to determine which test is most severe for different speed symbols
  Use one existing test for one set of speed symbols, other existing test for remaining speed symbols
Preliminary data should be available at next meeting (Feb 2011)

## Slide 5: Endurance Test
In FMVSS 139, endurance test required for all LT/C tyres
In R54, endurance test only required for tyres with Speed Symbol < Q (160 km/h)
  For Q and above, requires high speed test instead
These 2 tests have very different conditions and harmonizing them will be difficult and long
One solution is to restrict scope of gtr to radial tyres for vehicles up to 4536 kg with speed symbols ≥ Q (160 km/h)
  LT/C tyres with speed symbol < Q would be treated under existing regional regulations (i.e. regional tyres)
  In USA all tyres must pass a high speed test with final speed of 160 km/h

## Slide 6: Breaking Energy
Only one test, from FMVSS 139
But limits are defined based on Load Range
No mathematical conversion from Load Index to Load Range
Thus no way to know which limits to apply for a given LI
Not technically difficult, but needs to be harmonized using pressure equivalence table, for example

## Slide 7: Two Open Questions (1) Limit scope to include only lower than Q speed symbols?
Limit scope for LT/C tyres to ≥ Q speed symbol?
  Reduces the number and complexity of tests to harmonize without large impact on number of tyres covered by gtr
    Endurance test is technically hard to harmonize
  Tyres with speed symbol less than Q would continue to be treated by current regional regulations
  All tyres under FMVSS 139 have to pass a high speed test at a final speed of 160 km/h, which acts as a "de facto" limit

## Slide 8: Two Open Questions (2) Exclude Deep Tread Tyres?
In USA, LT/C tyres with tread depth > 18/32 inch (14.3 mm) are treated under different US regulation
  Endurance test is different (less severe)
  High speed test is different (less severe)
If treated under FMVSS 139 they exhibit testing failures which do not reflect real life behaviour in normal road use
Should they be excluded from gtr?