## Slide 1: Informal adhoc EVPC Working Group
Geneva, may 18 th, 2010
Proposal from FRANCE based on EVPC informal group work
Informal document No. GRSP-47-19
(47th GRSP, 17 - 21 May 2010,
agenda item 17)

## Slide 2: PROPOSALS
ECE/TRANS/WP.29/GRSP/2010/19 – R12
ECE/TRANS/WP.29/GRSP/2010/20 – R94
ECE/TRANS/WP.29/GRSP/2010/21 – R95
modified as:
ECE/TRANS/WP.29/GRSP/47-01 – R12 Rev1
ECE/TRANS/WP.29/GRSP/47-02 – R94 Rev1
ECE/TRANS/WP.29/GRSP/47-03 – R95 Rev1

## Slide 3: AIMS
To have material to homologate electric vehicle regarding crash test requirements
    To use R 94 as a basis for performing the crash test requirements - no modification of the existing R 94, only introduction of new prescriptions to take into account EV/HEV.
    Idem for R 95 (similar modifications)
    Idem for R 12, (similar modifications and update)

## Slide 4: CONTENT
No change for the scope of R 94, R 95, and introduction of EV for R 12.
Definitions:
  R 100 amendment (ECE/TRANS/WP.29/GRSP/2010/52)
  EV vehicle type and vehicle information
  Passenger compartment and Automatic disconnect
Spillage requirements /cells locations
Electrical safety requirements
Method of measurement (annex )

## Slide 5: EV vehicle type and information
Vehicle type
The locations of the RESS, in so far as they have a negative effect on the result of the impact test prescribed in this Regulation,
Information document
A general description of the RESS electrical power source type, and location and the electrical power train (e.g. hybrid, electric).”

## Slide 6: Passenger compartment definition
“2.7.2. “Passenger compartment for electric safety assessment” :
means the space for occupant accommodation, bounded by the roof, floor, side walls, doors, outside glazing, front bulkhead and rear bulkhead, or rear gate, as well as by the electrical protection barriers and enclosures provided for protecting the power train from direct contact with high voltage live parts.”

## Slide 7: Electrical safety requirements after impact test
residual voltage (s) lower than the high voltages values (if > 60 V and ≤ 1500 V in DC or > 30 V and ≤ 1000 V in AC (rms).
Residual energy on high voltage bus less than 0,2 j.
Physical Barrier protection for live parts against direct contact and resistance between the electrical chassis and all exposed conductive parts shall be less than 0.1 ohm against indirect contact
Isolation resistance: if not IPXXB :500 Ohm/V for AC and 100 Ohm/V for DC circuit (in between chassis and high voltage bus/portion

## Slide 8: Modifications
Isolation resistance not applicable if more than a single potential of a part of the high voltage bus is not protected under the conditions of protection IPXXB.
Clarification for the possibility to calculate the residual energy for X and Y capacitors

## Slide 9: Spillage
5.2.8.2. Electrolyte spillage
no electrolyte from the RESS shall spill into the passenger compartment, and no more than 7 per cent with a maximum of / 5.0 liters of electrolyte shall spill from the RESS outside the passenger compartment.

## Slide 10: Cells and RESS locations
RESS located inside the passenger compartment shall remain in the location in which they are installed and RESS components shall remain inside RESS boundaries.
No part of any RESS that is located outside the passenger compartment for electric safety assessment shall enter the passenger compartment during or after the impact test procedures.

## Slide 11
Test with all or part (s) of PT not energized, using Physical Protection (PT) or Isolation Resistance (IR) requirements
  With additionnal evidence ( to take into possible effects like short circuit on high voltage cables.
Test possible with automatic disconnect triggered with additionnal information to proove the functionnality ( trigger information, nominal current cut, etc.)

## Slide 12: Annex 11 (9),(7)
Deactivation of the on-board isolation resistance measuring system
Clarification on the measurement of Vb at the right place
Threshold limited to 60 VDC
Additionnal formulas to calculate the energy for X and Y capacitors.

## Slide 13: Test conditions
1.4.4.1. RESS be at any state of charge, which allows the normal operation of the power train as recommended by the manufacturer.
1.4.4.2. The electrical power train shall be energized with or without the operation of the original electrical energy sources (e.g. engine-generator, RESS or electric energy conversion system)

## Slide 14: Annexes – test procedures
Test setup and equipment
Bus voltage
Isolation resistance measurement method (taken from R 100 amendments)
Electrical Energy
Physical Barrier