## Slide 1: 47th GRSP Session Status report of Informal Group on CRS
Pierre CASTAING
Chairman
Informal Document No. GRSP-47-27
(47th session, 17-21 May 2010,
agenda item 23)

## Slide 2: Terms of reference of the informal group
The informal group shall consider the development of a new regulation for “Restraining devices for child occupants of power-driven vehicles” for consideration by GRSP.
The basis of the discussion will be informal documents N°. GRSP-42-2 and GRSP-42-27.
A step by step approach shall be implemented
  Phase1: Develop definitions, performance criteria and test methods for ISOFIX Integral “Universal” CRS
In its work, the informal group will take into consideration amongst others the technical expertise of EEVC WG18, EEVC WG12, ISO TC22/SC12, and NPACS as well as the results of the discussions held in the informal group and at GRSP.
If necessary, the informal group shall develop complementary test methods and propose alternative judgement criteria.
The target completion date for the informal group shall be the forty-sixth session of GRSP (December 2009) for this first phase.

## Slide 3: Status of the work done
18 meetings from January 2008
till April 2010
First draft regulation covering phase 1 presented as formal document:
  ECE/TRANS/WP.29/GRSP/2010/26
Amended by informal document:
  GRSP-47-06 - Draft amendment to ECE/TRANS/WP.29/GRSP/2010/26

## Slide 4: Principles of this new regulation
Independent regulation. The ECE R44 remains valid
  Multi steps approach
The scope of this new regulation cover only “ISOFIX – Universal – Integral” CRS in first step
New philosophy of classification
  No groups
  Classification based on standing height, maximum permissible weight (Child + CRS) and age limit for forward facing use.
Use of measurement device for CRS size control
Use of the Q dummies for frontal, rear and lateral dynamic impact on a new test bench
Use support leg as well as top tether as universal anti rotation device

## Slide 5: Independent regulation
ECE R44 remains valid
Multi steps approach
  Integral CRS + ISOFIX
  Non integral CRS + ISOFIX
  Adult safety belt dependent CRS
Transitional provisions for “soft landing” between ECE R44 and the different phases of this new regulation

## Slide 6: Scope of this regulation for the first step
ISOFIX “universal” integral CRS
  ISOFIX
    2 lower anchorages + 1 anti rotation device:
      Top Tether
      Support leg
    No use of the adult safety belt for the restraint of the child seat
Universal
  <F2X ISO fixture for FF & <R2 ISO fixture for RF (*)
  With top tether or support leg (**)
  Integral
    Child is restraint only by the CRS restraint system (harness)
    No use of the adult safety belt for the restraint of the child
(*)(**) others could fall into “Integral ‘specific vehicle’ ISOFIX” category

## Slide 7: New philosophy of classification
No group approach

## Slide 8: Classification on standing height
Geometrical dimensions of
-Size child restraint systems
Stature mm | Sitting height mm | Shoulder breadth mm | Hip breadth mm | Shoulder height mm | 
Every 50mm | 95%ile | 95%ile | 95%ile | 5%ile | 95%ile
Standing Height
Seating Height
Shoulder Height
Shoulder Breadth
Hip Breadth

## Slide 9
Source : IFTH – Projet 3D Child

## Slide 10: Age / Stature

## Slide 11: Weight / Stature

## Slide 12: Shoulder breadth / Stature

## Slide 13: Seating height / Stature

## Slide 14: Shoulder height / Stature

## Slide 15: Hip breadth / Stature

## Slide 16: The measurement device inside a CRS
Front
Section
Based on the range of size declared by the CRS manufacturer

## Slide 17: Limitations of use
Maximum weight of acceptable children
= 33 kg – CRS weight. (info to consumer)
Maximum stature of acceptable children
= declared by EM and controlled by TAA. (info to consumer)
Minimum age of acceptable children
15 months for FF. (Mandatory marking)

## Slide 18: Examples of information to the user
This FF CRS is suitable for a child older than [15th] with a mass not exceeding [22]kg and a stature comprised between 75 and 125 cms
This RF CRS is suitable for a child with a mass not exceeding [18]kg and a stature comprised between 40 cms and 95 cms
Age limit
Weight limit
Size limits

## Slide 19: Use of the Q dummies
For dynamic behaviour in:
Frontal impact
Rear impact
Lateral impact

## Slide 20: Frontal Impact configuration
Same as ECE R44 for input pulse.
New criteria and requirements for dummies readings
Same as ECE R44 for head displacement requirement
For monitoring purpose

## Slide 21: Rear Impact configuration
Same as ECE R44 for input pulse.
New criteria and requirements for dummies readings
Same as ECE R44 for head displacement requirement
For monitoring purpose

## Slide 22: Test Bench
Test bench according NPACS proposal
Backrest cushion NPACS proposal with a 50 mm cut
Seat cushion NPACS proposal but without gaps
90° rotation of the test bench for lateral impact

## Slide 23: Test Rig
Door
PU Tubes
Bench
Backrest Cushion
Seat Cushion
Sliding Isofix Anchorage Points
Support device for the door

## Slide 24: Door Panel Definition
Relative velocity corridor to be confirmed by evaluation program
Door Panel Dimensions
20 max
600
500
Tbd in
Phase2

## Slide 25: Test Parameters
 | ISO/PDPAS N623E | 
Intrusion velocity | 7-10 m/s | 
Intrusion depth | 200-300 mm | 
Sled deceleration | 10-14 g | 
Intrusion surface height | 500 mm | 

## Slide 26: Forward Facing with TT - Dummy Q3

## Slide 27: Some open issues to be validated (1)
Floor /support leg interface
  Support leg definitions:
    “Support foot”
    “Support leg contact surface”
    “Support leg contact volume”
    “Vehicle contact area”
    “Vehicle contact volume”
  ECE R14 & R16 modification
    Assessment of “i-Size ready ” vehicles

## Slide 28: Some open issues to be validated (2)
Age limit [18, 15 or 12 month]
  Taking into consideration ISO fixtures dimensions
Side impact procedure
  Dummy positioning
  Pulse corridor
  Criteria
    Containment
    HIC
    g (3ms) level
  Requirements

## Slide 29: Some open issues to be validated (3)
Geometrical characteristics
  Seating height upper limit / Standing height
  Shoulder breadth upper limit / Standing height
  Hip breadth upper limit / Standing height
  Shoulder height upper and lower limits / Standing height
  Measurement tool and tolerances

## Slide 30: Conclusion and Future work
The Group proposes to GRSP to endorse the draft and to start implementation of Phase 1 and ask for extended mandate to continue with Phase 2:
“ISOFIX universal non-Integral CRS”
Next meeting (19th) 30 June (Madrid ?)