## Slide 1
TEG Proposals
ECE/TRANS/WP.29/GRSP/2010/2
and GRSP-47-13
How to make a progress on the gtr9 amendments with Flex-PLI
Main issues | gtr9 Amendments (TEG proposal)
Tibia Relaxation Zone | Preamble and Regulatory Text TEG proposed to have 380 Nm relaxation zone initial five years
ACL/PCL Requirements | Preamble and Regulatory Text TEG proposed to conduct ACL/PCL monitoring with 13 mm 1) initial 60 months
Impactor Selection | Regulatory Text Choice of manufacturers 2) which impactor can use
Transitional Period (EEVC/WG 17 legform -> Flex) | Preamble Some TEG members proposed to have 96 months 3)
Main issues | gtr9 Amendments (Japan proposal) | New ECE 01 series amendments
Tibia Relaxation Zone | Preamble and Regulatory Text Same as TEG proposal | Regulatory Text Same as TEG proposal (use Regulatory text)
ACL/PCL Requirements | Preamble and Regulatory Text If a car does not pass ACL/PCL less than 13 mm with Flex-PLI, the car shall pass Shearing Displacement less than 6 mm with EEVC/WG 17 legform (initial five years). | Regulatory Text Same as Japan proposal.
Impactor Selection | Regulatory Text Choice of Contracting Parties which impactor can use | Regulatory Text Same as TEG proposal
Transitional Period (EEVC/WG17 legform -> Flex) | Preamble Some TEG members proposed to have adequate lead time | Regulatory Text Same as TEG proposal (use Preamble text)
Japan Modified Proposals
based on several comments from several CPs
US can not accept to write monitoring in the regulatory text. EC can not accept less stringent requirement than EU Regulation. 2) US would like to select the impactor by themselves. 3) US difficult to accept to write an actual transitional period in the preamble.
Transmitted by the expert from Japan
Informal document No. GRSP-47-34
(47th GRSP, 17 - 21 May 2010,
agenda item 4.1)
Notes: This is the TEG proposal for main issues.
For the Tibia relaxation zone is set as 380 Nm, and no concerns on this item.
However, for the ACL/PCL, monitoring is not acceptable for US and EC. US can not accept to write monitoring tings in the regulatory text, and then EC need regulatory item on ACL/PCL by somehow. For the Impactor Selection, US can not accept manufactures choice, and for the transitional period, US can not accept to write an exact number of months.
So, Japan made a modified proposal on these items as follows (with considering New ECE regulation with gtr9 contents).
For the tibia relaxation zone, no need to change.
For the ACL/PCL requirements, we change it is as "If a care ....". It is not monitoring, i.e. regulatory requirements.
For the Impactor selection, we change it as contracting choice based on the US concerns. On the other hand, if it is suit for manufacturer's choice for ECE regulation, we do not oppose to write that in the ECE regulation.
For the Transitional period, the transitional period is change as adequate lead time based on the US concerns. On the other hand, if it is suit to write exact transitional period for ECE regulation, we do not oppose to write it in the ECE regulation.
This is the Japan proposal based on several comments form several contracting parties, so if everyone agree on this proposal, we would like to make a progress on the gtr9 amendment with Flex-PLI based on this proposal. Actually, Japan need gtr9 amendment with Flex-PLI ASAP, because we would like to introduce the Flex-PLI to domestic regulation from very near future.

## Slide 2
<number>
Appendix: Informal document No. GRSP-47-32
Notes: <number>