|  | INF.5 |
| --- | --- |
| Economic Commission for Europe Inland Transport Committee Working Party on the Transport of Dangerous Goods Joint Meeting of Experts on the Regulations annexed to the European Agreement concerning the International Carriage of Dangerous Goods by Inland Waterways (ADN) (ADN Safety Committee) Eighteenth session Geneva, 24–27 January 2011 Item 4 of the provisional agenda Proposals for amendments to the Regulations annexed to ADN | 4 January 2011 |

Omission in table C: UN 3475

Request for mandate for substances working group

Submitted by the Netherlands

UN 3475 in table C

The product UN 3475: ETHANOL AND GASOLINE MIXTURE or ETHANOL AND MOTOR SPIRIT MIXTURE or ETHANOL AND PETROL MIXTURE, with more than 10% ethanol, is currently listed in table A. In column 8 (carriage permitted 3.2.1) a "T" is entered. In the explanatory notes it is stated: If column (8) contains code “T”, carriage is permitted in packages and in tank vessels. In the event of carriage in tank vessels, the requirements of Table C are applicable (see 7.2.1.21).

It seems the Safety/Administrative Committee has failed to make an entry for table C for this product. The Netherlands delegation would like to suggest the Safety Committee gives a mandate to the substances working group to draw up a proposal for such an entry. The entry could be entered into ADN 2013.

Special Authorization

The Netherlands would like to inform the ADN secretariat and the member states that we have received a request for a Special Authorization for the transport of UN 3475. The transport is intended to take place within the Netherlands only. The authorization has not yet been granted. The application; the material safety data sheet; and the proposed entry for table C are included and can be used by the substances working group, should they receive their mandate.