## Slide 1: NL FORMAL ASEP
(2011-02-15)
July 30, 2026
Informal document GRB-53-21
(53rd GRB, 15-17 February 2011,
Agenda item 3(c))

## Slide 2: Update of NL ASEP proposal (doc GRB-2011-08) what has changed what is the difference with the GRB chairman's proposal (doc GRB-2011-02) issued by the Netherlands GRB 53, February 2011
<number>
Notes: <number>

## Slide 3: Reminder: why ASEP
<number>
Annex 3 covers the part of the engine map with lower revs;
Decision made to have Additional Sound Emission Provisions to cover a wider part of the engine map (higher revs).
Notes: <number>

## Slide 4: Reminder: why ASEP
<number>
Annex 3 limits for M1 and N1 will be around 70 dB(A)
    (68-75 depending on stage and vehicle)
What noise emission can we expect, and can we allow at conditions of higher acceleration and/or higher rpm?
Notes: <number>

## Slide 5: Keep in mind: dB is logarithmic
10 dB louder = 10 times as many vehicles
20 dB louder = 100 times as many vehicles
30 dB louder = 1000 times as many vehicles

## Slide 6: Why NL proposal: concern
GTI’s and similar:
    PMR 80-150 kW/t
    Affordable to mass public
    Client wishes sound design
    Driven sporty

## Slide 7: Why NL proposal: concern
New technologies starts at the high end.
Drop down very fast to the cheap end,
Will also be with ‘sound/noise design’
<number>

## Slide 8: Example NL concern
Measured GTI in urban street:
    Lmax = 105 dB(A)
      PMR = 110 kW/t
      a = 4,2 m/s2 in 2nd gear
NOT TESTED IN 2nd GEAR
IN ASEP PROPOSAL CHAIR
due to:
acceleration 4,2 > boundary of 4
Note: 1 x 105 dB(A) > 3000 x 70 dB(A)
105 dB(A) is loud!

## Slide 9: Text missing in Formal doc 8
Page 11 Par 4:
Two major changes have been incorporated:
1. implementations of the proposals for improvement from the TNO Venoliva report
2. transition to a fixed Not To Exceed Level in dB(A), instead of a delta relative to the Annex 3 limit.
Page 11 Par 5:
In GRB 52 the TNO Venoliva report was presented (ECE-TRANS-WP29-GRB-52-inf07e).
Besides a preference for the NL ASEP proposal, it contains several proposals to improve the NL ASEP proposal.
The Netherlands has taken on board these proposals for improvement from the TNO report in this update.
‘Improvements’ secretariat: Page 11 Par 5.B.ii
TNO is not the technical service of the Netherlands
TNO is the research contractor of the EC and author of the VENOLIVA report

## Slide 10: What has changed in NL ASEP?
Adoption of TNO venoliva recommendations
    Skip 2 m/s2 boundary in Annex 3
    Slightly more lenient ASEP parameters
    Increase ASEP boundary 4 -> 5 m/s2
    Limit curve as function of vehicle speed (not rpm)
    ASEP limit also applies to partial throttle
Now fixed Not-To-Exceed level in dB(A)
    Instead of Delta relative to Annex 3 limit
    NTE = 81-85 dB(A) (depending on vehicle class)

## Slide 11: Remember NTE 81-85 dB(A)
Equal to 10-30 times 70 dB(A)
Equal or higher than limit Heavy Trucks
Is this stringent?

## Slide 12: Is it stringent ?
Yes, compared with industry wish for freedom for sound/noise (up to +100 dB)
No, compared with normal technology
<number>

## Slide 13: Does it lead to extra costs?
No: costs are in tuning close to the limitation and designing jumps outside the control range
Remember:
99% of uncritical vehicles passes NL ASEP

## Slide 14: Top 10 most silent vehicles (source: informal doc 3 GRB feb 2000)
Most silent car is a sports car
  9,7 dB under the limit!

## Slide 15: Relation between price and noise
Loud vehicles are more expensive!

## Slide 16: What is the effect of NL proposal?
99% of uncritical vehicles pass ASEP
86% of vehicles of concern fail ASEP
    Further information: GRB-52-inf15

## Slide 17: Effect of Chair part 1proposal
17% of uncritical vehicles fail
64% of vehicles of concern pass
<number>

## Slide 18: Comparison Chair ASEP vs NL ASEP
For many vehicles chair ASEP and NL ASEP are not very different,
exept the silent and the noisy vehicles!!
Veh107-04 PMR=56
Veh200-02 PMR=105

## Slide 19: Some essentials of chairman's ASEP different from NL ASEP
Boundary conditions (Annex 10 par 2)
  Acceleration boundary of 4 m/s2
  Skipping 1st gear
Slope method (Annex 10 par 3)
  no bonus for silent vehicles
  Virtually unlimited limit line in case of high rpm
Lurban method Annex 10 par 6 (Moore)
  Needs additional study/discussion
  First results: more liberal than slope method
  Limit Lwot sensitive to small changes
<number>

## Slide 20: Boundary: acceleration in 2nd gear
Acceleration around 4 m/s2 is found frequently
  Also in family cars, turbo diesels and GTI’s
  Due to a 4 m/s2 limit in ASEP such vehicles cannot be tested in 2nd gear
Acceleration above 5 m/s2 is found only in supersportcars (> 200 kW/t)
Max acceleration in 2nd gear (m/s2) | # of vehicles in ASEP dBase (out of 123 vehicles) | PMR range (kW/t)
>3,5 | 23 | 69-246
>4 | 10 | 101-246
>5 | 4 | 205-246
>6 | 1 | 246

## Slide 21: Relevance of the bonus
Silent vehicles become ‘normal’ in higher revs area.
Without bonus ‘jumps’ are punished
With bonus: silent vehicles will pass tougher limitation options
No bonus  more vehicles rejected  supports pleas for weaker limitation
<number>

## Slide 22: Effect of bonus on silent vehicles example vehicle: 5,5 dB under Annex 3 limit (veh 1-26)
<number>
Without bonus
ASEP becomes critical
 = 0,4 dB(A)
With bonus
ASEP is uncritical
 = 6 dB(A)

## Slide 23: Virtually unlimited limit line
If the slope of 5 dB / 1000 rpm is combined with a very high engine speed range, this leads to extremely high limit curves, well above 100 dB(A)

## Slide 24: ‘Moore’ method, introduction
Nice idea:
  Based on acceleration instead of rpm
  Design independent
Needs to be studied in more detail
First impressions
    Rather liberal for high powered vehicles
    Stringency very much dependent on
      A3 limit
      Tyre noise
    Sensative to measurement errors acceleration
<number>

## Slide 25: Example of Lurban ASEP normal vehicle: substantial room to increase
Vehicle 200-08
PMR 112 kW/t
Assumed limit A3: 70 dB(A)
Lurban ASEP more liberal than
  Chair ASEP (3-7 dB)
  NL ASEP (5-8 dB)
  R51.02 (8 dB)

## Slide 26: Example of Lurban ASEP vehicle of concern: early jump allowed
Vehicle 200-09
PMR 159 kW/t
Assumed limit A3: 72 dB(A)
Lurban ASEP more liberal than
  Chair ASEP (5-10 dB)
  NL ASEP (3-12 dB)
  R51.02 (7 dB)

## Slide 27: Example of Lurban ASEP noisy vehicle > 100 dB allowed
Vehicle 200-16
PMR 239 kW/t
Assumed limit A3: 73 dB(A)
Lurban ASEP more liberal than
  Chair ASEP (5-15 dB)
  NL ASEP (5-20 dB)
  R51.02 (15 dB)
Note: significant spread in Lurban limit due to spread in acceleration

## Slide 28: Lurban ASEP sensitive to small changes
The ASEP dBase contains values of Kp,ASEP up to 0,8
this means
   Lwot,ASEP = 5 x  Lurban and  Lwot,ASEP = 4 x  Lcrs,
  1 dB change in Lurban gives a 5 dB change in Lwot,ASEP
  1 dB change in Lcruise gives a 4 dB change in Lwot,ASEP
Example: A lowering of the Annex 3 limit by 2 dB meanwhile enforces a 10 dB lowering of the noise emission in ASEP
Might be as low as 0,2

## Slide 29: Example Lurban ASEP sensitivity
Annex 3 procedure

## Slide 30: Example Lurban ASEP sensitivity
Expected behavior in ASEP

## Slide 31: Example Lurban ASEP sensitivity
Allowed: 3 dB Margin on Lurban in ASEP

## Slide 32: Example Lurban ASEP sensitivity
Consequence: 12 dB Margin in Lwot,ASEP

## Slide 33: TNO audit ‘Moore’
Advantage of the alternative method is that it is not limited to vehicles with an
internal combustion engine, in contrary to the current GRBIG method.
<number>

## Slide 34: TNO audit ‘Moore’ (2)
So the main conclusion is that the alternative proposal as it stands now, is a very liberal and therefore environmental unfriendly alternative for the modified GRBIG proposal, which is somewhat more ambitious as the original proposal.
<number>

## Slide 35: My conclusion
As long as the ‘Moore’ method is in
for every vehicle
There’s no sense in having more stringent alternatives (‘Chair’, ‘NL’)
<number>

## Slide 36: 4e Stage of weakening? Effects of changes in the method
Eurocities, Brussels
2006 November 28
source abatement: let’s speed it up
<number>
Notes: <number>

## Slide 37: In NL view
‘Moore’ proposal should be used for vehicles which can not be measured in Annex 10.
<number>

## Slide 38
Thank You

## Slide 39: ACEA study
COSTS – BENEFITS
Reaction on TNO feasibility and effect study
<number>

## Slide 40: ACEA study (expert opinion)
The general approach of calculating benefits for noise is rather standard, and as can be expected every possibility is used to keep benefits low:
Only WTP value: no estimate for health (DALY’s or addition of night noise reduction)
25€/dB: the 2001 figure should be corrected for inflation
Threshold: is 50 dB, so again an underestimate. It is true that the 50-55 is more difficult to obtain from EU-data, but extrapolations from other data could be used.
The effect of limit reduction is likely to effect the whole distribution, making the final effect larger (eg 5 dB lower limit only 2 dB fleet reduction?)
All in all, the benefits are likely to be underestimated by a factor 2
<number>

## Slide 41: ACEA study 2 (expert opinion)
The ACEA costs calculation had to addopt some very discutable assumptions to arrive at the astronomic figures for reducing noise. For example, the list of additional costs contain quite a number of measures which are already common. Actually leaving them out would cost more than introducing them. These costs then are thought to persist for 20 years. It is not easy to explain that the development of an absorbing layer continues to burden the manufacturer for 20 years.
<number>

## Slide 42: ACEA study 3 (expert opinion)
In short the undescriminate application of these assumptions lead to a caricature of CBA.
<number>

## Slide 43
THANK YOU

## Slide 44
<number>

## Slide 45: Calculations FIGE
Eurocities, Brussels
2006 November 28
source abatement: let’s speed it up
<number>

## Slide 46: Mercedes fight to fulfill the limits Effects of changes in the method
Eurocities, Brussels
2006 November 28
source abatement: let’s speed it up
<number>
Notes: <number>