## Slide 1: Research into a new road side enforcement test for the noise emission of mopeds GRB 54; September 2011 issued by the Netherlands
<number>
Informal document GRB-54-11
(54th GRB, 19-21 September 2011,
agenda item 13)
Notes: <number>

## Slide 2: Noise emission of mopeds in the Netherlands
Vehicle category: L1 (2 wheelers, max speed 45 km/h)
Most important source of noise nuisance in the Netherlands
1 milion mopeds (vs 16 milion inhabitants)
Often used by youngsters (age: 16 -18)
  if 18+ transfer to cars and motorcycles
Estimated: 40-60% tampered
  Main goal: increased speed (+10 up to +60 km/h)
  Main effect: increased noise (+10 up to +40 dB(A))

## Slide 3: Police experience with stationary road side enforcement test
All Police departments have received special noise measurement equipment + instruction
Use: relatively scarce, 1 a 2 active departments
Why?
  Lack of manpower/priority
  Complicated and time consuming
  Need for special trained staff
  Measurement method is not OK
    Depends on RPM, troublesome to get rpm signal, calibration
    Hard to reproduce measurement (Instable rpm, lack of load)
    50% S is not representative for average moped usage
    Hard to explain criteria to the public (Reference value instead of fixed limit)
    Measurement values do not correlate with subjective judgment (false result)

## Slide 4: New idea for road side enforcement: noise measurement on rollerbench
Stationary test under load could
  Depend on speed instead of RPM
  Reduce complexity noise test
  Improve reproducability
  Improve correlation to nuisance
  Enable absolute limits
  Improve acceptance

## Slide 5: Pilot project: 4 mopeds and 3 measurements
Roller bench test
Pass by test
Stationary test

## Slide 6: Analysis / conclusions with respect to roller bench test
Background noise low enough
  Self induced noise
  Tyre/roller interaction
Stable test condition (load and speed)
Good reproducibility
Good correlation to pass by noise

## Slide 7: How to proceed?
Feedback of GRB is most welcome!
More vehicles need to be tested to
  Explore correlation with nuisance
  Explore boundaries of roller bench test
  Explore transition to motorcycles