## Slide 1: Proposal for subcategories of CVs (N2, N3, M2, M3)
<number>
ＪＡＳＩＣ
Restricted
Informal document GRB-54-14
(54th GRB, 19-21 September 2011,
agenda item 3(b))

## Slide 2
In 1982
R51-00
In 1988
R51-01
In 1995 R51-02
In 2011
New Generation of Vehicles
Ex. HV, EV etc.
Up-to-date Threshold
by 125kW &250kW
Subcategories for ECE R51
Japan proposes the simple and globally applicable classification based on the current technology and reflecting the applicable future technology.
<Background>
30 years have passed since ECE R51-00 was established, and the test method has been modified. It is time to consider the new subcategories for the new test method.
<Concept of our proposal> 1) Main classification is based on weight as same as current classification.
2) Noted the change of power (KW) according to the changes of the times.
Concept 1)
Two classification
(No Bus: GVW≦2t)
Concept 2)

## Slide 3
In this proposal, Japan revises the current subcategories in R51.02 reflecting the current technology as well as considering subcategories proposed by TNO report and ACEA.

## Slide 4
The outside view of each category concerning M

## Slide 5
The outside view of each category concerning N

## Slide 6: 1. Proposal for subcategory for M2 GVW ≤5t (passengers of 10 or more)
<number>
ECE R51.02 |  | JAPAN Regulation
GVW≤2t |  | No threshold
2t<GVW≤3.5t |  | 
3.5t<GVW ≤5t | P<150kW | P≤150kW
 | 150kW≤P | 150kW<P
-There is no vehicles over 150kW in these 30 years.
-Different test method is applied to the vehicles below 3.5t. (same test method as M1)
- There is no vehicle below 2t now.
Current Subcategory
ECE R51.02 |  | JAPAN Proposal
GVW≤2t |  | 
2t<GVW≤3.5t |  | GVW≤3.5t
3.5t<GVW ≤5t | P<150kW | 3.5t<GVW≤5t
 | 150kW≤P | 
JAPAN Proposal
Change of sales volume of M2
0
500
1000
1500
2000
2500
3000
3500
4000
50
60
70
80
90
100
110
120
130
140
150
Engine power [ｋＷ]
Average of sales volume per year (unit)
1981-1983
2007-2009
Mainly passengers of 27
2010
1980

## Slide 7: 2. Proposal for subcategory for M3 5t < GVW
<number>
ECE R51.02 | JAPAN Regulation
P<150kW | P≤150kW
150kW≤P | 150kW<P
Current Subcategory
-Considering the alignment with the engines for trucks, the threshold could be changed to 250kW.
-Most of vehicles over 250kW are intercity and sightseeing buses.
80kW UP
JAPAN Proposal
Mainly driving on motorway and/or in sightseeing areas
Driving urban area
150kW
現行規制
250kW提案
Change of sales volume of M3
0
200
400
600
800
1000
1200
1400
1600
1800
2000
80
100
120
140
160
180
200
220
240
260
280
300
320
Engine power [ｋＷ]
Average of sales volume per year(unit)
1981-1983
2007-2009
150kW
Proposal:250kW
Increase
80kW UP
ECE R51.02 | JAPAN Proposal
P<150kW | P<250kW
150kW≤P | 
 | 250kW≤P
2010
2010
1980

## Slide 8
M3 Driving urban area Bus pictures
瀬谷市 神奈川中央
(177kW)
荻窪市 関東バス
(177kW)
江戸川区 都営バス
長江通りにて離合（おのみちバス・中国バス）
出展：http://ja.wikipedia.org/wiki/狭隘路線 Onomichi bus and Chugoku Bus.JPG
(191kW)
(191kW)
M3 Bus with over 180kW engine drives urban areas in Japan.
These M3 Buses should be the same subcategory as M3 Buses with up to 180 kW engine.

## Slide 9: 3. Proposal for subcategory for N2 (3.5t < GVW ≤ 12t)
<number>
ECE R51.02 | JAPAN Regulation
P<75kW | P≤150kW
75kW≤P<150kW | 
150kW≤P | 150kW<P
ECE R51.02 | JAPAN Proposal
P<75kW | 
75kW≤P<150kW | P<125kW
 | 125kW≤P
150kW≤P | 
-There is no vehicle below 75kW
-The current threshold 75kW could be shifted to 125kW
JAPAN Proposal
GVW less than 7.5t
For urban driving
（P<125kW)
GVW over 7.5t
Not for urban driving
(125kW≤P)
150kW
75kW
現行規制
2007年以降75kW以下に車両無し
125kW提案
５0kWUP
Current Subcategory
Change of sales volume of N2
0
10000
20000
30000
40000
50000
60000
70000
50
60
70
80
90
100
110
120
130
140
150
160
170
180
190
200
engine power [kW]
Average of sales volume per year (unit)
1981-1983
2007-2009
150kW
75kW
No vehicles below 75kW after 2007
Increase
by 50kW
Proposal: 125kW
1980
2010
2010

## Slide 10: 4. Proposal for subcategory for N3 (12t<GVW）
<number>
-There is no vehicle below 75kW
-The current threshold 150kW could be shifted to 250 kW
JAPAN Proposal
80kWUP
150kW
現行規制
Current Subcategory
Change of sales volume of N3
0
2000
4000
6000
8000
10000
12000
14000
16000
110
130
150
170
190
210
230
250
270
290
310
330
350
370
Engine power [ｋＷ]
Average of sales volume per year (unit)
1981-1983
2007-2009
Increase
80kWUP
150kW
ECE R51.02 | JAPAN Regulation
P<75kW | 
75kW≤P<150kW | P≤150kW
150kW≤P | 150kW<P
ECE R51.02 | JAPAN Proposal
P<75kW | 
75kW≤P<150kW | P<250kW
150kW≤P | 
 | 250kW≤P
For bulky load
For heavy load ,tractor etc
Proposal:250kW
2010
2010
1980

## Slide 11
<number>
Thank you
Japan proposes the simple and globally applicable classification for the time being.