## Slide 1
19-21 September 2011
JASIC
Kei-truck of N1
Informal document GRB-54-15
(54th GRB, 19-21 September 2011,
agenda item 3(b))

## Slide 2: Summery
Background
Key Point of Proposal
Kei trucks are unique vehicles in Japan. They are used mainly on agriculture or transportation of goods etc..
There are not data in European database.
The vehicle structure and the vehicle sound level of Kei N1 are different from those of light N1. Therefore the sub category for Kei N1 should be defined within light N1. The proposed border is “PMR(GVM)<35”.

## Slide 3
Specification for Kei car
Limited specification |  | 
・Vehicle length： | < | 3.40 m
・Vehicle width： | < | 1.48 m
・Vehicle height： | < | 2.00 m
・Engine displacement： | < | 660 cc

## Slide 4
Light commercial vehicles Kei (9 million)
Heavy duty trucks (4 million)
Light commercial vehicles without Kei (4 million)
The number of vehicles owned for
commercial vehicles in Japan

## Slide 5
Usage of Kei truck

## Slide 6
Kei N1
Light N1 (GVM ≤ 2.0t)
Heavy N1 (GVM > 2.0t)
different
Similar
Same group
Truck type
Difference between van and truck
Van type

## Slide 7
Power to Mass(GVM) Ratio
0
10
20
30
40
50
60
PMR (Rated engine power/GVM)x1000
35
Light N1
Kei N1
〈Ref.〉 Heavy N1
Kei N1 should be separated from Light N1 by “PMR(GVM) ≤ 35”.
Truck type
Van type

## Slide 8
“6.2.3. Additional sound emission provisions
… intended especially for non-lockable transmissions with variable gear ratios (CVT).
Vehicle of category N1 are exempted from ASEP if one of the following
conditions is fulfilled:
− The driver's R point is either forward of the front axle or
longitudinally rearwards of the front axle transverse centre
line by a maximum of 1100 mm.
− The engine capacity is not exceeding 660 cc and the power-to-
mass ratio PMR calculated by using the maximum
authorized vehicle mass is not exceeding 35.
− The payload is at least 850 kg and the power-to-mass ratio
PMR calculated by using the maximum authorized vehicle
mass is not exceeding 40.
N1 exemption from ASEP
PMR(GVM) ≤ 35 is used in the text in ASEP for R51

## Slide 9
category |  | vehicles
GVM ≤ 2.0t or GVM ≤ 2.5t | PMR ≤ 35 ( ≤ 660cc) | Kei N1
 | PMR > 35 | Light N1
GVM > 2.0t or GVM > 2.5t | - | Heavy N1
Sub categories for N1

## Slide 10
Sound level for Method B from the TNO report
10%
M1
N1

## Slide 11
0
1
2
3
4
5
66
67
68
69
70
71
72
73
74
75
76
L urban, dB(A)
Frequency
0%
20%
40%
60%
80%
100%
Distribution of Kei N1sound level on Method B
10% cut off level is 74dB(A).
Percentage non-compliant vehicles, %
10%

## Slide 12
74dB
OICA
TNO
>2.000kg GVM
>2.500kg GVM
Kei N1
Heavy N1
Light N1
L.urban in dB(A)
3000
2500
2000
1500
1000
500
0
test mass in kg
Kei N1
Sound level for Kei N1 on Method B
78
76
74
72
70
68
66
64
Sound level for Kei N1 on Method B is different from that of Light N1.

## Slide 13
Conclusion
The vehicle structure and the vehicle sound level of Kei N1 are different from those of light N1. Therefore,
• the sub category for Kei N1 should be defined within light N1. The proposed border is “PMR(GVM)<35”.
• The limit value of Kei N1 should be same as that of heavy N1 since the 10% cut off sound level for Kei N1 is 74 dB(A) and same sound level of heavy N1.