## Slide 1: Difference between TNO and OICA Analysis for M1 Sub Categories
19-21 September 2011
JASIC
Informal document GRB-54-16
(54th GRB, 19-21 September 2011,
agenda item 3(b))
Notes: <number>

## Slide 2: Comparison between TNO and OICA analysis for M1 category
 |  | TNO |  | OICA | 
 |  | Normal | Off Road | Normal | Off Road
M1 | PMR≤125 kW/t | 72 dB(A) | 73 dB(A) | 72 dB(A) | 74 dB(A)
 | 125<PMR≤150 kW/t | 72 | 73 | 73 | 74
 | 150 kW/t<PMR | 73 |  | 75 | -

## Slide 3: 10% cut off sound level (TNO data)
10% cut off
M1 72dB(A)
10% cut off
M1G 74dB(A)
TNO analyzed M1 and M1G (off road) separately
but PMR is not taken into account.
Notes: <number>

## Slide 4
10% cut off sound level (OICA data)
M1-A PMR<125
M1-B PMR=125:150
M1-C PMR>150
M1-D Off Road
10% cut off
OICA divided M1 into 3 sub categories depending on PMR
and analyzed M1 and M1G.
Notes: <number>

## Slide 5
90%
0%
20%
40%
60%
80%
100%
62
64
66
68
70
72
74
76
78
80
Lurban, dB(A)
累積頻度, %
M1 PMR<125
M1 PMR=125:150
M1 PMR>150
M1 Off Road
10% cut off sound level (re-analyze TNO data)
10% cut off
cumulative frequency
TNO data were divided into the same sub categories as OICA
and re-analyzed.
M1-A PMR<125
M1-B PMR=125:150
M1-C PMR>150
M1-D Off Road
Notes: <number>

## Slide 6
OICA
72
73
74
75
TNO
10% cut off sound levels in TNO data base are same as those in OICA results in analyzing with same sub categories.
10% cut off
10% cut off
cumulative frequency
Results of OICA analysis and TNO re-analysis
M1-A PMR<125
M1-B PMR=125:150
M1-C PMR>150
M1-D Off Road

## Slide 7: Summary
The results of TNO and OICA are same when the data are analyzed with the same condition.
Appropriate condition for analysis should be defined.