| Transmitted by the expert from Japan | Informal document No. GRE-65-02 (65th GRE, 28 -31 March 2011, agenda item 14(c)) |
| --- | --- |

Proposal for Corrigendum 1 to Supplement 19 to the 01 series amendment to Regulation No. 6

Note: The modifications to the current text of the regulation are strikethrough characters.

I.       PROPOSAL

Paragraph 6.1.2., correct to read:

"6.1.2.      When an assembly of two or more lamps having the same function is deemed to be a single lamp, it shall comply with the requirements for:

(a)    Maximum intensity when all lamps together are lit (last column of the table);

(b)    Minimum intensity if one lamp has failed."

II.	JUSTIFICATION

The words “(last column of the table)” were deleted from the paragraph 6.1.6. in Regulation No. 7 according to ECE/TRANS/WP.29/GRE/2009/19 because the structure of the table was modified. The paragraph 6.1.2. in Regulation No.6 should be amended as well.