Comments to ECE/TRANS/WP.29/GRE/2011/18, 
Proposal for Supplement 38 to the 03 series of amendments

Note:	The text reproduced below was prepared by the expert from the International Electrotechnical Commission (IEC) in order to in order to clarify some provisions as proposed by GTB to GRE in document in GRE/2011/18.  The modifications to the current text of Regulation No. 37 are marked in bold characters.  The modifications to GRE/2011/18 are marked in red characters.

I.	Proposal

Paragraphs 8.3. and 8.4., amend to read:

"8.3.	No filament lamps of the categories or of the types within the categories listed below shall be used in lamps submitted for type approval after the period following the entry into force of the Supplements to 03 Series of amendment, as indicated for each category in the table below of group 3 in annex 1.

8.4.		However, Contracting Parties applying this Regulation may continue to grant approvals for lamps in which filament lamps of categories or of types within categories listed below are used, provided that these lamps are intended as replacement parts for installation on vehicles in use, for the period after entry into force of the Supplements to 03 Series of amendment as indicated below in the table of group 3 in annex 1.

"

Annex 1, the list of categories of filament lamps and their sheets, amend to read:

"....

Group 1

Without general restrictions:

| Category |  | Sheet number(s) |
| --- | --- | --- |
| H1 | *6 | H1/1 to 3 |
| H3 | *6 | H3/1 to 4 |
| H4 |  | H4/1 to 5 |
| H7 |  | H7/1 to 4 |
| H8 |  | H8/1 to 4 |
| H8B |  | H8/1 to 4 |
| H9 | *3 | H9/1 to 4 |
| H9B | *3 | H9/1 to 4 |
| H10 |  | H10/1 to 3 |
| H11 |  | H11/1 to 4 |
| H11B |  | H11/1 to 4 |
| H12 |  | H12/1 to 3 |
| H13 |  | H13/1 to 4 |
| H13A |  | H13/1 to 4 |
| H15 |  | H15/1 to 5 |
| H16 |  | H16/1 to 4 |
| H16B |  | H16/1 to 4 |
| H21W | *2 | H21W/1 to 2 |
| H27W/1 |  | H27W/1 to 3 |
| H27W/2 |  | H27W/1 to 3 |
| HB3 |  | HB3/1 to 4 |
| HB3A |  | HB3/1 to 4 |
| HB4 |  | HB4/1 to 4 |
| HB4A |  | HB4/1 to 4 |
| HIR1 | *3 | HIR1/1 to 3 |
| HIR2 |  | HIR2/1 to 3 |
| HS1 | *6 | HS1/1 to 5 |
| HS2 | *6 | HS2/1 to 3 |
| HS5 |  | HS5/1 to 4 |
| HS5A | *5 | HS5A/1 to 3 |
| HS6 | *4 | HS6/1 to 4 |
| PSX24W | *2 | P24W/1 to 3 |
| PSX26W | *2 | PSX26W1 to 3 |
| PX24W | *2 | P24W/1 to 3 |

Group 2

Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps:

| Category |  | Sheet number(s) |  |
| --- | --- | --- | --- |
| C5W | *6 | C5W/1 |  |
| H6W |  | H6W/1 |  |
| H10W/1 |  | H10W/1 to 2 |  |
| HY6W |  | H6W/1 |  |
| HY10W |  | H10W/1 to 2 |  |
| HY21W |  | H21W/1 to 2 |  |
| P13W |  | P13W/1 to 3 |  |
| P21W | *6 | P21W/1 to 2 |  |
| P21/4W |  | P21/4W/1 | (P21/5W/2 to 3) |
| P21/5W | *6 | P21/5W/1 to 3 |  |
| P24W |  | P24W/1 to 3 |  |
| P27W |  | P27W/1 to 2 |  |
| P27/7W |  | P27/7W/1 to 3 |  |
| PR21W |  | PR21W/1 | (P21W/2) |
| PR21/4W |  | PR21/4W/1 | (P21/5W/2 to 3) |
| PR21/5W |  | PR21/5W/1 | (P21/5W/2 to 3) |
| PR27/7W |  | PR27/7W/1 | (P27/7W/2 to 3) |
| PS19W |  | P19W/1 to 3 |  |
| PS24W |  | P24W/1 to 3 |  |
| PSY19W |  | P19W/1 to 3 |  |
| PSY24W |  | P24W/1 to 3 |  |
| PW13W |  | P13W/1 to 3 |  |
| PW16W |  | PC16W/1 to 3 |  |
| PWR16W |  | PC16W/1 to 3 |  |
| PWY16W |  | PC16W/1 to 3 |  |
| PW19W |  | P19W/1 to 3 |  |
| PWR19W |  | P19W/1 to 3 |  |
| PWY19W |  | P19W/1 to 3 |  |
| PW24W |  | P24W/1 to 3 |  |
| PWR24W |  | P24W/1 to 3 |  |
| PWY24W |  | P24W/1 to 3 |  |
| PY21W |  | PY21W/1 | (P21W/2) |
| PY24W |  | P24W/1 to 3 |  |
| PY27/7W |  | PY27/7W/1 | (P27/7W/2 to 3) |
| R5W | *6 | R5W/1 |  |
| R10W | *6 | R10W/1 |  |
| RR5W | *6 | R5W/1 |  |
| RR10W | *6 | R10W/1 |  |
| RY10W | *6 | R10W/1 |  |
| T1.4W |  | T1.4W/1 |  |
| T4W | *6 | T4W/1 |  |
| W2.3W |  | W2.3W/1 |  |
| W3W | *6 | W3W/1 |  |
| W5W | *6 | W5W/1 |  |
| W10W | *6 | W10W/1 |  |
| W15/5W |  | W15/5W/1 to 3 |  |
| W16W |  | W16W/1 |  |
| W21W |  | W21W/1 to 2 |  |
| W21/5W |  | W21/5W/1 to 3 |  |
| WP21W |  | WP21W/1 to 2 |  |
| WPY21W |  | WP21W/1 to 2 |  |
| WR5W |  | W5W/1 |  |
| WR21/5W |  | WR21/5W/1 | (W21/5W/2 to 3) |
| WY2.3W |  | WY2.3W/1 |  |
| WY5W |  | W5W/1 |  |
| WY10W | *6 | W10W/1 |  |
| WY16W |  | W16W/1 |  |
| WY21W |  | WY21W/1 to 2 |  |

Group 3

For replacement purposes only (see transitional provisions of paragraphs 8.3. and 8.4.):

|  |  |  | As specified by transitional provisions in paragraph 8.3 | As specified by transitional provisions in paragraph 8.4 |
| --- | --- | --- | --- | --- |
| Category |  | Sheet number(s) | Supplement | Period | Supplement | Period |
| C5W | *7, *8 | C5W/1 | 38 | 12 months | 38 | unlimited |
| C21W | *8 | C21W/1 to 2 | 28 | 12 months | 28 | unlimited |
| H1 | *7 | H1/1 to 3 | 38 | 12 months | 38 | unlimited |
| H3 | *7 | H3/1 to 4 | 38 | 12 months | 38 | unlimited |
| H14 |  | H14/1 to 4 | 38 | 12 months | 38 | unlimited |
| HS1 | *7 | HS1/1 to 5 | 38 | 12 months | 38 | unlimited |
| HS2 | *7 | HS2/1 to 3 | 38 | 12 months | 38 | unlimited |
| P19W | *8 | P19W/1 to 3 | 37 | 60 months | 37 | unlimited |
| P21W | *7, *8 | P21W/1 to 2 | 38 | 12 months | 38 | unlimited |
| P21/5W | *7, *8 | P21/5W/1 to 3 | 38 | 12 months | 38 | unlimited |
| PC16W | *8 | PC16W/1 to 3 | 37 | 60 months | 37 | unlimited |
| PCR16W | *8 | PC16W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PCY16W | *8 | PC16W/1 to 3 | 37 | 60 months | 37 | unlimited |
| PR19W | *8 | P19W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PR24W | *8 | P24W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PSR19W | *8 | P19W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PSR24W | *8 | P24W/1 to 3 | 37 | 12 months | 37 | unlimited |
| PY19W | *8 | P19W/1 to 3 | 37 | 60 months | 37 | unlimited |
| R2 |  | R2/1 to 3 | 28 | 12 months | 28 | unlimited |
| R5W | *7, *8 | R5W/1 | 38 | 12 months | 38 | unlimited |
| R10W | *7, *8 | R10W/1 | 38 | 12 months | 38 | unlimited |
| RR5W | *7, *8 | R5W/1 | 38 | 12 months | 38 | unlimited |
| RR10W | *7, *8 | R10W/1 | 38 | 12 months | 38 | unlimited |
| RY10W | *7, *8 | R10W/1 | 38 | 12 months | 38 | unlimited |
| S1 |  | S1/S2/1 to 2 | 28 | 12 months | 28 | unlimited |
| S2 |  | S1/S2/1 to 2 | 38 | 12 months | 38 | unlimited |
| S3 |  | S3/1 | 38 | 12 months | 38 | unlimited |
| T4W | *7, *8 | T4W/1 | 38 | 12 months | 38 | unlimited |
| W3W | *7, *8 | W3W/1 | 38 | 12 months | 38 | unlimited |
| W5W | *7, *8 | W5W/1 | 38 | 12 months | 38 | unlimited |
| W10W | *7, *8 | W10W/1 | 38 | 12 months | 38 | unlimited |
| WY10W | *7, *8 | W10W/1 | 38 | 12 months | 38 | unlimited |

*	Tables, Electrical and Photometric characteristics:

Voltage is expressed in V;

Wattage is expressed in W;

Luminous flux is expressed in lm.

In a case that for a category of filament lamp more than one value of reference luminous flux is specified, the value at approximately 12 V for approval of a lighting device and 13.5 V for approval of a light-signalling device shall be applied unless otherwise specified by the regulation used for the approval of the device.

*2	Not for use in passing beam headlamps.

*3	Not for use in front fog lamps marked "B" as defined in Regulation No. 19.

*4	Not for use in Regulation No. 112 headlamps.

*5	Not for use in headlamps other than Regulation No. 113 class C headlamps

*6	All types except from 6 V type

*7	6 V types only "

*8	Only for use in signalling lamps, cornering lamps, reversing lamps and rear registration plate lamps.

II.	Justification

1.	With the introduction of new light source categories, GTB regularly evaluates which light source categories could be phased out based upon technological progress and our evaluation of the need to keep these categories in the regulation. This is such a proposal.

2.	The proposal is not aimed at completely deleting categories of light sources from Regulation No. 37, but at moving some categories or types of categories from group 1 and group 2 to group 3 of Annex 1. In this way, these categories of light sources can still be approved and used as replacement parts. However, they can no longer be used for type approval of new lamps, unless these lamps are intended as replacement parts for vehicles in use.

3.	Proposal GRE/2011/18 is shifting categories from group 1 and group 2 to group 3.  To several of these categories use restrictions applied when placed in groups 1 or 2.  In group 3, use restrictions make no sense because new applications are no longer allowed.  However, during the transitional period, use restrictions should be maintained, which is proposed in this document.

4.	Categories C21W, R2 and S1 have been specified for replacement purposes since supplement 28.  Originally, use restrictions applied to category C21W.  For consistency reasons and to avoid unintended interpretations, this use restriction is inserted again, though there is no effect because the transitional period has passed.

5. 	In the new proposal GRE/2011/18 some categories are in group 1 and 3, or in group 2 and 3, depending on the type within these categories.  This type distinction should also be reflected in the transitional provisions of paragraphs 8.3 and 8.4.

6.	The tables in paragraphs 8.3 and 8.4 and in annex 1 to describe group 3 list use restrictions for the same categories.  These tables have been merged into one in annex 1.