## Slide 1
<number>
Summary of
8th WLTP-DHC Meeting
9 June 2011
Palais des Nations, Geneva

## Slide 2: Table of contents
<number>
Current status
Open issue list
Regional weighting
Mode construction
Validation Plan
Next action
Next meeting
Notes: <number>

## Slide 3
(1) In-use Data Collection
Region | In-use Data | Traffic Statistical Information
EU | Completed | Completed
India | Completed | Completed
Japan | Completed | Completed
Korea | Completed | Completed
USA | Completed | Completed
China |  | -
1. Current Status
(2) Methodology  It was agreed by DHC group
(refer to WLTP-DHC-06-03e.rev1)
(as of 9 June 2011)
(3) Threshold speed  It was agreed by DHC group
(refer to WLTP-DHC-07-02e)
<number>
 Due to tight schedule, made a decision to move forward developing the harmonized cycle without Chinese data.
60 80 110 (km/h)
LOW  MIDDLE  HIGH  Ex-HIGH
Notes: <number>

## Slide 4
<number>
2.1. Open Issues -1
 | Issues | Discussion points | Status / Proposed Actions
1 | Deadline for submission of driving data | India and China requested deadline be extended to May | Decided to start development of new cycle after 8th DHC meeting. Later data submission is still open for analysis.
2 | Regional Weighting when developing the WLTC | traffic volume same weighting compromised weighting | It was agreed to adopt the traffic volume ratio during the 8th DHC meeting
3 | Threshold Speed for L/M/H | according to DHC-06-03 CP’s requirement | Threshold speeds of 60, 80 and 110km/h were agreed for the cycle phases during 7th DHC meeting
4 | High Phase Cycle Construction (US&EU versus other regions) | only ONE unified cycle possess TWO types of High phase cycle | It was agreed to possess two (2) types of HIGH phase cycle during 7th meeting.
5 | Mode Construction | a) cold start test only b) cold start & hot soak start | Possible mode constructions are introduced during 8th DHC meeting. Further analysis is necessary during the validation 1.
CLOSED
<number>
CLOSED
CLOSED
CLOSED
Notes: <number>

## Slide 5
<number>
2.2. Open Issues -2
 | Issues | Discussion points | Proposed Actions
6 | Unique Weighting Factor for L/M/H Phase | harmonized weighting factors permit regional weighting factors | a) Is target of Informal Group Consider the possibility to accept b) for only CO2/Fuel consumption
7 | Gear Shift Points | fixed points based on vehicle specification others | Ms. Ericsson, Mr. Steven, JRC and JARI work together to finalize the method before developing the 1st WLTC.
8 | How to treat the vehicles which are not able to follow the prescribed cycle | continue to drive with wide-open-throttle exempt the H (or M&H) phase(s) others | Develop the proposal during validation 1 tests.
9 | Check the driving profile based on the vehicle characteristic |  | Analyze the in-use data based on vehicle characteristic (i.e. power to mass ratio)
<number>
Notes: <number>

## Slide 6: 3. 1. Regional weighting for cycle development
It was discussed the following possible options for regional weighting when developing the unified driving characteristic of Low/Middle phases
Options | EU | US | India | Japan | Korea | China | Justification
1 | 1 | 1 | 1 | 1 | 1 | - | A
2 | 1 |  | 1 |  |  | - | B
3 | Traffic volume ratio |  |  |  |  | - | C
A : equal weighting for contracting parties submit in-use driving data ( consider Switzerland as part of EU region)
B : based on population, vehicle density and increasing rate
C : based on traffic volume, same logic as High/extra-High phases weighting
<number>
DHC group has agreed to adopt the option 3
(same logic for High/Ex-High phases)
Notes: <number>

## Slide 7: 3.2. Regional weighting factor
=
=
=
=
=
=
=
<number>

## Slide 8
During the 7th DHC meeting held on 16 May 2011, the possible six(6) options of mode construction were proposed.
Need to study on each option to consider the following views.
a) Testing burden
b) Investment (hard and/or soft)
c) Required measurement items
d) Low concentration pollutants
e) Regional weighting factor
f) others, if necessary
4.1. Mode Construction
<number>
Notes: <number>

## Slide 9
option | Mode construction |  |  | Brief description
 | Series test |  | independent | 
1 |  |  |  | 
2 |  |  |  | MIDDLE&HIGH1 sampling
3 |  |  |  | similar to US procedure
4 |  |  |  | 1 HIGH phase
5 |  |  |  | LOW&MIDDLE 1 sampling
6 |  |  |  | All phases test as a series
4.2. Possible mode constructions
LOW
* 582s
MIDDLE
* 439s
HIGH
* 441s
Ex-HIGH
* 338s
LOW
* 582s
Intermediate
soak
Prep.->
SOAK
MIDDLE
* 439s
Prep.
->
LOW
* 582s
HIGH
* 441s
LOW
* 582s
Intermediate
soak
Prep.->
SOAK
MIDDLE
* 439s
MIDDLE
* 439s
Ex-HIGH
* 338s
LOW
* 582s
MIDDLE
* 439s
HIGH
* 441s
LOW
* 582s
Intermediate
soak
Prep.->
SOAK
MIDDLE
* 439s
Ex-HIGH
* 338s
Prep.
->
LOW
* 582s
MIDDLE
* 439s
HIGH
* 779s
LOW
* 582s
Intermediate
soak
Prep.->
SOAK
MIDDLE
* 439s
LOW
* 582s
HIGH
* 441s
LOW
* 582s
Intermediate
soak
Prep.->
SOAK
MIDDLE
* 439s
MIDDLE
* 439s
Ex-HIGH
* 338s
LOW
* 582s
HIGH
* 441s
LOW
* 582s
Intermediate
soak
Prep.->
SOAK
MIDDLE
* 439s
MIDDLE
* 439s
Ex-HIGH
* 338s
*) phase duration subject to change after data analysis
**) middle phase test after intermediate soak may be required for HEV vehicles
1 sampling
1 sampling
1 sampling
**
**
**
**
**
**
<number>
Notes: <number>

## Slide 10
4.3. Case Study
Option | Testing burden | Investment (hard and/or soft) | measurement item | Low concentration pollutants | Regional WF (weighting factor) | Others (if necessary)
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
3 |  |  |  |  |  | 
4 |  |  |  |  |  | 
5 |  |  |  |  |  | 
6 |  |  |  |  |  | 
B : BAD, W : WORSE, C : CRITICAL
DHC member was requested to submit the written comments and/or counter proposal by next DHC meeting (6-7 July 2011).
<number>
Notes: <number>

## Slide 11
5.1. Validation - Over View -
6 July 2011
3 Oct 2011
2 Apr 2012
Before start each test,
preparation phase is necessary taking into account of the followings
1) Test plan, 2) Participant CPs, Laboratories, 3) Vehicle Procurement
4) Measurement Items, 5) Test Criteria, 6) others.
Validate New Cycle
Validate new Test Procedure with New Cycle
including the OIL (Open Issue List) Study
Confirm the Adaptability of Existing Equipment
including Additional Pollutants Measurement
Check Correlation between the Laboratories
Validation 1
Validation 2
Confirmation
Round Robin
COMPLETED
2 Apr 2012
<number>
Notes: <number>

## Slide 12
5.2. Test Plan for Validation 1 (1)
Participant CP and/or Laboratories
Fuel | power to mass ratio | Sales volume | Transmission
Petrol | Low end (20~40 kW/t ) : Passenger &Truck High end (100 kW/t or more ) : Passenger | within Top 5 sales | at least 1 vehicle
Diesel |  |  | 
HEV/EV | Not must during validation 1 phase |  | 
Participating Parties | Laboratories
Japan | NTSEL, JARI, JAMA
Korea | 
Europe | JRC, UTAC
OICA | ACEA, JAMA
India | 
South Africa | 
Test Conditions
Cold Start Test : LOW and MIDDLE phases
Hot Start Test : ALL phases
<number>
(2) Test Vehicles (in Japan for example) and Test Conditions
Notes: <number>

## Slide 13
Measurement Items | Methods | Criteria
Driving Trace (each mount) | Driving index by SAE J2951 Driven roller counter(10Hz or more) Acceleration ratio | +/- 3%
Tire Speed | Difference between roller speed and tire speed | No slip
Gear Shift Points | Appropriate shift point Clutch off point | +/- 3kph within +/-1sec
Accel Pedal Angle | Positional Sensor | TBD
Difference of Test Drivers | Drive Trace Questionnaire | TBD
* Pollutants - CO2 - (each phase) | Bag (& continuous) sampling | NA
* Pollutants - others - (each phase) | Bag (& continuous) sampling | NA
(3) Measurement Items and Test Criteria
5.2. Test Plan for Validation 1 (2)
*) NOT MUST
# of tests : at least 3 times
<number>

## Slide 14
<number>
6. Next Actions
 | 2011 2012 |  |  |  |  |  |  |  |  | 
 | Apr. | May | Jun | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Jan
Meetings |  |  |  |  |  |  |  |  |  | 
In-use data collection |  |  |  |  |  |  |  |  |  | 
Develop the harmonized cycle |  |  |  |  |  |  |  |  |  | 
Validation |  |  |  |  |  |  |  |  |  | 
Open Issues |  |  |  |  |  |  |  |  |  | 
DTP Activities |  |  |  |  |  |  |  |  |  | 
Proposal of,
The threshold of L/M/H
High phase construction
Agreement of,
The threshold of L/M/H
Validation2
Validation1
Initial
analysis
Develop
1st Draft WLTC
Final DEADLINE
for threshold
7th DHC
10th DHC
Modify, if necessary
preparation
1st draft test procedure
8th DHC
62nd GRPE
2, 3, 4
5, 6, 8
9th DHC
11th DHC
63rd GRPE
Interim Report of Validation 1
Detailed plan for Validation 2
Agreement of OIL
Proposal of,
2nd WLTC for Validation 2
1st Interim Report of Validation 2
7
Final
DEADLINE for cycle development
Proposal of,
Regional weighting
Introduction of first Draft WLTC
Plan for Validation 1
<number>
Notes: <number>

## Slide 15
7. Next Meeting
Next 9th DHC meeting was set on 6~7 July 2011 at Stockholm.
Main agenda items are
Introduce the world-wide harmonized cycle ver.1
Continue to discuss on mode construction
Detailed information will be noticed by 17 June 2011.
Comments should be sent to Mr. Ichikawa,
Technical Secretariat; nick@ichikawa.tec.toyota.co.jp
Notes: <number>