## Slide 1: GFV Task Force Heavy Duty Dual Fuel vehicles (HDDF TF) GRPE 62 – 10 June 2011
GRPE informal document 21
Informal document No. GRPE-62-21
(62 GRPE, 7-10 June 2011, agenda item 8(a))

## Slide 2: suggested HDDF terminology
Digit i: category of HDDF, depending on the gas ratio
  1 for GR > 90%
  2 for 10% < GR < 90%
  3 for GR < 10%
Type 1
Type 2
Type 3
100%
Pure gas
(mono-fuel)
0%
Pure Diesel
(mono-fuel)
Average Gas Ratio (on a cycle – energy based)
Character X: possible operating modes in the category
  A for engines operating solely in Dual Fuel mode
  B for engines capable of operating either in Dual Fuel or in Diesel mode
"HDDF i X"

## Slide 3: Definition issues
GFV proposes the following definitions
  "Dual-Fuel engine" means an engine that uses simultaneously 2 different types of fuels supplied from separate storage systems and where the consumed amount of one of the fuels versus the other one may vary depending on the operation.
  "Dual-Fuel vehicle" means a vehicle that is powered by a Dual-Fuel engine and that supplies the fuels used by the engine from separate on-board storage systems.
GFV recommends these definitions be included in the core text of Regulation 49, not in the Dual-fuel annexes and be limited to Diesel-gas HDDF
Does GRPE agree with GFV recommendation. ?

## Slide 4: Amendments to R85 (informal document GRPE62-17)
Principles
  The declared power and torque are those obtained in the Dual Fuel mode when the Diesel mode is also possible
  Same reference fuels as the ones for the emission test
  One the amendment affects all engines, not solely HDDF
    5.2.1 reads currently "5.2.1. The net power test shall consist of a run at full throttle for positive-ignition engines and at fixed full-load fuel injection pump setting for diesel engines, the engine being equipped as specified in Table 1 of Annex 5 to this Regulation."
    5.2.1 shall be amended to read "5.2.1. The net power test shall consist of a run at full-load, the engine being equipped as specified in Table 1 of Annex 5 to this Regulation."
Because the HDDF definitions shall be common, the formal amendments will be submitted together with the HDDF Annexes in R49 for GRPE approval in June 2012

## Slide 5: EURO V and EURO VI major points of progress since GRPE61
HDDF indicators
  An HDDF mode indicator will indicate the actual operating mode: Dual Fuel, service, or, when appropriate Diesel mode
    "Service mode" indication will be given as soon as the service mode is activated
    "Dual fuel" and "Diesel mode" indication may not be a steady indication but will last at least 1 minute
  An Empty gas tank warning indicator will indicate the gas tank will soon become empty
ISC
  ISC tests shall be performed in the Dual Fuel mode according to the applicable existing EURO V or EURO VI processes for Diesel engines
  When a Diesel mode is also possible
    the tests will be also performed in the pure Diesel mode on the same engine.
    Pass would mean pass both in Diesel mode and in DF mode

## Slide 6: EURO VI major points of progress since GRPE61
NOx control measures
  EURO VI NOx control measures shall apply "mutatis mutandis" to HDDF engines
OBD
  EURO VI HDDF shall be subject to full EURO VI OBD applicable to compression ignition engines
  Gas supply system shall be subject to component monitoring
PEMS test at certification
  Will be performed on the dual fuel mode according to Annex VI
  When a Diesel mode is available
    Will also be performed on the Diesel mode
    Pass conclusion if both the PEMS test on DF mode and the PEMS test on Diesel modes have concluded to pass

## Slide 7: EURO VI - Lack of gas availability
An operability restriction is activated as soon as a lack of gas supply is detected
  This restriction is the same as the "severe inducement" specified in EURO VI Annex XIII (i.e. 20km/h)
  If a Diesel mode is available, possibility to switch to the Diesel mode
The restriction becomes active
  in case of a malfunction of the gas supply system either 30 minutes after activation or after the next time the vehicle is stationary, whatever the earliest
  in case of an empty tank immediately (the driver has been warned)

## Slide 8: Draft time-plan – on time except for R115
Aug – Dec 2010: principles - done
GRPE Jan 2011: status report + informal document - done
Jan – June 2011: draft requirements – done @ 80%
GRPE June 2011: status report (incl. EURO VI HDDF rules) + amendments to R85 (informal document)
July – Dec 2011: amendments to UNECE-R49
GRPE Jan 2012: informal HDDF annexes. + guidance Re Retrofit
Jan - Mar 2012: HDDF annexes
GRPE June 2012: approval of the amendments to UNECE-R49
WP29 Nov 2012: approval of the amendments to UNECE-R49
difficulties regarding amendments to R115 DELAY necessary !