## Slide 1: AEGPL feedback on the last GRSG session amendments to R67_01
Brussels, 10th May, 2011

## Slide 2
Proposals in R67_01 (regulation for LPG only), main principles:
Formal document from the Netherlands GRSG/2011/14
The present version of Regulation No. 67 contains provisions for approving components with a working pressure up to 30 bars. Innovations like direct injection of liquid LPG working at higher pressure are technically possible without jeopardizing safety, but Regulation No. 67 does not contain provisions for the approval of such components as the fuel pump, the fuel rail, the injectors and a safety valve leading back fuel from the high pressure parts to the fuel tank.
This proposal introduces a new Class 0 for components with a working pressure of 3,000 kPa or higher. Where relevant, a distinction has been introduced between components of Class 0 and other classes. In addition to the ECE approval mark the working pressure shall be indicated on parts of Class 0.
Furthermore, the principle of a multi-component, consisting of a combination of already defined components, has been introduced. By doing so, the provisions will not be design restrictive and will not have to be amended for new technologies. The information document and communication document have been extended with information on such multi-components.

## Slide 4: Bi-fuel and running mode insertion
Document Informal 28 from Italy (following request for clarifications by delegates)
I. Proposal
Insert the following new paragraphs:
2.20 “LPG running mode” means an operational mode during which only LPG or more than one fuel is supplied to the engine.
2.21 "Bi-fuel vehicle" means a vehicle that, originally or after the application of a LPG retrofit system, is equipped with two separate fuel storage systems, can run on petrol and also on LPG and is designed to run on only one fuel at a time."
Justification
Definitions of “LPG running mode” and “bi-fuel vehicle”, used in ECE/TRANS/WP.29/GRSG/2011/15, need to be inserted.

## Slide 5: Last GRSG session in April 2011 List of documents approved
Formal: ECE/TRANS/WP.29/GRSG/2011/14 + 15
Informal: 2Rev1 (incorporates inf 02 + formal 14Rev1) + 28
All the documents are on http://live.unece.org/trans/main/wp29/wp29wgs/wp29grsg/grsgrep.html