## Slide 1
Enterprise and Industry Directorate General
European Commission
Mobile Air-conditioning (MAC):
Development of an Emission test procedure
Nikolaus Steininger
Automotive Industry Unit
Enterprise and Industry Directorate-General
European Commission
Nikolaus.steininger@ec.europa.eu

## Slide 2: MAC test procedure: why?
Communication of the Commission on the review of the Community Strategy to reduce CO2 emissions from passenger cars and light-commercial vehicles of 2 February 2007 =>
Euro 5/6 Regulation 715/2007: pollutant emissions to be limited under normal conditions of use (e.g. use of MAC in “real driving” conditions) =>
Commission has to prepare a regulatory proposal for the reduction of emissions from the use of MAC systems
Basis of this proposal is a MAC test procedure
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: MAC test procedure: objectives
Cost-efficient
Should incentivise reduction of emissions resulting from MAC use in real driving:
  No “academic” exercise trying to provide the best possible accuracy for environmental impact of MAC use
  But designed such that technical measures reducing/not-reducing “MAC emissions” established by the test procedure reduce/do-not-reduce “MAC emissions” in real driving => proper “ranking” of MACs
  Encourages “good and appropriate” technology
Suitability for “virtual testing”, which may be developed in parallel or at a latter stage (i.e. availability of virtual testing is no condition for future legislation!)
Assessment of the whole vehicle, including the impact of non-MAC components such as glazing or insulation
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: MAC test procedure: state of play
Consortium of contractors led by TNO, including partners like TUG and the JRC, together with stakeholders has developed test procedure, report is available on UNECE website
Achievements:
  Compares MAC on/off fuel consumption
  Can be run on “normal” chassis dyno
  High reproducibility/repeatability
Main characteristics:
  No NEDC but constant speed cycle (e.g. idling, 50, 100 km/h)
  Ambient temperature < 30° C
  Solar load calculated based on glazing paramters and simulated by variation of interior temperature or MAC mass flow
  Results mathematically corrected for “small” variations of actual test parameters (vehicle speed, ambient temperature/humidity, …)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: MAC test procedure: next steps
Open test issues (a selection):
  Outlet vent or cabin temperature as test target?
  Pre-conditioning (e.g. NEDC provisions)?
  Test tolerances?
  Number of tests?
  => Pilot test phase
Other issues:
  Future “electric” MAC: SOC of batter,…
  Credit for “low ambient temperature” (e.g. < 15° C) MAC management?
  How to present results to the consumer ?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: MAC test procedure: pilot phase
Multi-lab pilot phase:
  Assessment of feasibility, repeatability, reproducibility
  Define open issues
  Assessment of “proper” MAC ranking capability (?)
Participation:
  Industry (e.g. vehicle manufacturers, suppliers)
  Technical services
  Research institutes
  European
  International
  => Test protocol to be made available on UNECE website, for participation please contact European Commission & contractor: nikolaus.steininger@ec.europa.eu & sebastiaan.bleuanus@tno.nl
Notes: <number>
<footer>
<header>
<date/time>