## Slide 1: WLTC* methodology
Proposed by Japan
(Reviewed by UK, JRC and Mr. Steven)
DHC group
under GRPE/WLTP informal group
(*) WLTC : Worldwide harmonized Light duty driving Test Cycle
11~12 January 2011
Palais des Nations, Geneva

## Slide 2: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of High cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 3: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of high cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 4: 1. Purpose
Develop the world wide harmonized light duty test cycle, which will represent typical driving conditions around the world
Define the methodology to develop the WLTC drive cycle
The WLTC drive cycle will be developed based on combination of collected in-use data and suitable weighting factors.
  China, EU, India, Japan, South Korea, USA

## Slide 5: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of high cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 6: 2.1. Overall process
Task of DHC Group Work
Task of DTP Group Work
(*) Remark
DHC : Development of worldwide Harmonized light duty driving Cycle
DTP : Development of Test Procedure
WLTC : Worldwide harmonized Light duty driving Test Cycle
Classification of Influencing Parameters
Collections of statistics on LD vehicles use
Collections of In-use driving data
Determine weighting factor
Development of Reference Database
Re-categorization into L/M/H
Development of
initial WLTC
Validation tests 1
Confirmation tests
Validation tests 2
WLTC
Gearshift analysis
Round robin tests
Modification Short trip & gearshift points
Gearshift prescription
Cold / Hot ratio
Engine On -> Vehicle take-off time
etc
Modification Short trip & gearshift points
PM/PN
ICE-Lab. process
E-Lab. process
Additional pollutant
Reference fuel
input from DTP subgroup
PCs / LDCVs
Urban / Rural / Motorway
Peak / Off peak / Weekend
  ↓
Low / Middle / High

## Slide 7
2.2. Basic concept
Common test cycle is developed based on collected in-use data and weighting factor.
Weighting factor matrix
and
In-use driving data
collection
Common test cycle
Develop unified
speed-acceleration
distribution
chi-squared based analysis
Other parameter comparison
・・・
Compare the short trip combination and the unified distribution
combine the
short trips
Road Category | Region A | Region B | Region C
I | WFA1 | WFB1 | WFC1
II | WFA2 | WFB2 | WFC2
III | WFA3 | WFB3 | WFC3
Weighting factor
Road Category | Region A | Region B | Region C
I |  |  | 
II |  |  | 
III |  |  | 
In-use driving behaviors
・・・

## Slide 8
2.3. Data collection matrix
 | Urban |  |  | Rural |  |  | Motorway |  | 
 | Weekday |  | Week-end | Weekday |  | Week-end | Weekday |  | Week-end
 | On-peak | Off-peak |  | On-peak | Off-peak |  | On-peak | Off-peak | 
Passenger
Car (PC)
LD Commercial
Vehicle (LDCV)
The following matrix is requirement for each in-use data collection CP, with consistency between weighting factors and collected data.
Sub categorization is acceptable with consistency between weighting factors and collected data.
(*) In case of lack of statistical information, annual driving distance in red box
can be acceptable for data analysis.

## Slide 9: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of high cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 10
3.1. Data processing
In-use Driving Data Processing
Raw Data
In-use data in each road type and in each region is processed separately.
Raw data shall be shared within the DHC group.
Filtering & Thinning
(if necessary)
short trip (ST)
database
idling
database
Divide into idling and short trip portions
・Speed-Acceleration
(Positive & Negative)
Distribution
・ST Duration Distribution
・ST Average Speed
Distribution
・ST Average Duration
・Others (refer to 3.5.)
・Idling Duration Distribution
・Idling Average Duration
Gear shift analysis
idling-1
idling-2
ST-2
ST-1
Time (s)
Speed (km/h)
(*) Definition of short trip (ST)
Up shift
Down shift
Calculate the compensated WF
(refer to Appendix)
Data conversion
Convert into L/M/H

## Slide 11: 3.2.1. L/M/H method
Considering the threshold vehicle speed
  Consider threshold based on each countries’ traffic condition and driving characteristic
  Find the threshold that shows similar Speed-Acceleration distribution of each countries
Calculate the compensated WF
  Using Drive condition WF and total driving duration
Convert in-use data（U/R/M => L/M/H）
Analyze speed-acceleration distribution and driving characteristics （L/M/H）
Generate the driving cycle in each phase

## Slide 12: 3.2.2. Consideration of threshold speed - 1
<Method1> Based on similarity of speed-acceleration distribution
The threshold of Low/Middle
  VmaxL/M = 40 / 50 / 60 / 70? and RatioV<60 > 80% etc.
The threshold of Middle/High
  VmaxM/H = 80 / 90 / 100/ 110? and RatioV<90 > 50% etc.

## Slide 13: 3.2.3. Consideration of threshold speed - 2
<Method2> Based on parameter value
Select the candidate threshold speed based on least discrepancy in each characteristic.

## Slide 14: 3.2.4. Consideration of threshold speed - 3
<Method3> Based on maximum speed distribution
50 / 90?
65 / 110?
60 / 90?
After completion of all data acquisition, final threshold speed will be determined by taking into account of three methods.
50 / 80?

## Slide 15: 3.2.5. Data conversion
Convert the each short trip data including the previous idling portion into new categories (Low/Middle/High) from original (Urban/Rural/Motorway) categories with the compensated WF (w’)
  criteria : maximum vehicle speed, speed frequency etc.
Urban
Rural
Motorway
◆Image
Low
Middle
High
The segments that composed of ST and IDLE move into L/M/H categories with the compensated WF.
(*) Calculation formula of the compensated WF are shown in Appendix.

## Slide 16
3.3.1. Develop the speed-acceleration distribution
Develop the speed-acceleration distribution in each region
・・・
・・・
・・・
<Example>

## Slide 17: 3.3.2. Analyze driving characteristics
Distribution
ST speed-acceleration distribution
ST duration distribution
ST average speed distribution
ST maximum speed distribution
ST length distribution
ST cruise speed distribution
ST speed * acceleration distribution
Idling duration distribution
Parameter
Average speed (km/h)
Maximum Speed (km/h)
Maximum Acceleration (km/h/s or m/s2)
Maximum Deceleration (km/h/s or m/s2)
Relative Positive Acceleration (m/s2)
Average short trip duration (s)
Average idling duration (s)
Number of idling per kilometer (#/km)
Number of idling per second (#/s)
Time accelerating (%)
Time decelerating (%)
Time cruising (%)
Time stop (%)
To confirm the representativeness of the unified cycle, the following distributions and parameters will be analyzed.
Max. speed
Short trip duration
Time (s)
Ave. speed
Speed distribution
V-A distribution
Max. acceleration
Vehicle speed (km/h)
Idling duration

## Slide 18
3.3.3. Develop the unified speed-acceleration distribution
Develop the unified speed-acceleration distribution
ex.: speed-acceleration distribution in Low phase
Unified distributions for the following parameters will be generated.
  Short trip duration distribution, Short trip average speed distribution, Idling duration distribution, others
Low speed-acceleration distribution in region A
×
×
RWLow,A
RWLow,B
・・・
・・・
Unified speed-acceleration distribution in Low phase
WF Low
in region A
Low speed-acceleration distribution in region B
WF Low
in region B
RW = Regional Weight

## Slide 19: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of high cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 20
Determine the test cycle duration
< ex. WMTC: 600 x 3phases, WHDC: 1800, LA#4:1371, NEDC: 1180, JC08: 1204 (sec) >
4.1.1. Determination of the number of idle and short trip
Low cycle
Middle cycle
High cycle
Time (TL)
Time (TM)
Time (TH)
Speed (km/h)
drive cycle duration in each phase (Ti) - average idling duration
average short trip duration ＋ average idling duration
number of short trip (NST, i)
=
Determine the number of idle and short trip in each phase
  Calculate the number in each phase (Low, Middle, High)
<example> TL = 600 sec, average low short trip duration = 60 sec, average low idling duration = 20 sec,
number of short trip (NST,L) = (600 – 20) / (60 + 20) = 7.25 => 7
number of idling (NI,L) = 7 + 1 = 8
number of idle (NI, i) = number of short trip (NST, i) + 1

## Slide 21
Determine the NST, i units of short trip duration in each phase
  Generate the cumulative frequency graph based on short trip data base
  Divide into “Ni, ST” equally in Y axis
  Select a average duration in each class respectively. if necessary, adjust the duration to match the target cycle duration
  Pick the candidate short trips which duration are STD1, STD2, .., STDNST, i
Determine the NI, i units of idling duration in each phase
  Generate the cumulative frequency graph based on idling data base
  Divide into “NI, i” equally in Y axis
  Select the average duration in each class
  NI, i units of idling duration ( ID1, ID2, .., IDNI, i ) in each phase are decided
4.1.2. Determination of the idle and short trip duration
ST duration
Cumulative frequency
STD1
STD2
STDN
・・・・・
100%
N
IDLE duration
Cumulative frequency
ID1
ID2
IDN
・・・・・
100%
N
Notes: Determination for the number of idle and short trip

## Slide 22: 4.1.3. Determination of the idle and short trip duration
Select the ST which duration is adjusted by the following formula (Tn) to match the target cycle duration.
  Compensate duration TN = STDN / ΣSTDi * Tshort
Same adjustment for idle duration will be taken, if necessary.
Tshort
STD1
STD2
STD3
STDN
ID1
ID2
ID3
ID4
IDN+1
(*) TN = STDN / ΣSTDi * Tshort
T1
T2
T3
TN
ST duration
Cumulative frequency
STD1
STD2
STDN
・・・・・
100%
N
+TN
・・・
・・・
・・・
Ttarget
・・・

## Slide 23: 4.1.4 Determination of the short trip combination
Generate the speed - acceleration distribution in each combination
・・・・・・・・・・・・
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
20
40
60
80
100
Speed (km/h)
Acc. (km/h/s)
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
20
40
60
80
100
Speed (km/h)
Acc. (km/h/s)
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
20
40
60
80
100
Speed (km/h)
Acc. (km/h/s)
・・・・・・････････････
Unified speed -acceleration distribution
the least χ2 value
STD1
STD2
STDN
・・・・・・
・・・・・・
・・・・・・
NSTD1
NSTD2
NSTDN
・・・・・
Number of combinations
= (NSTD1)*(NSTD2)*･･･*(NSTDN)
Determine the short trip combination in each phase
  Generate the speed-acceleration distribution in each combination from candidate short trips
  Compare with the unified distribution
  Select the short trip combination with the least χ2 value
  Check other distributions and parameters (refer to Appendix 1)
Candidate short trips
Comparison based on
chi-squared analysis

## Slide 24: 4.1.5. Sample of the ST combination
Duration (s) No. of STD | STD1 10sec | STD2 15sec | STD3 18sec | STD4 24sec | STD5 38sec | STD6 60sec
1 |  |  |  |  |  | 
2 |  |  |  |  |  | 
・ | ・ | ・ | ・ | ・ | ・ | ・
N |  |  |  |  |  | 
Combinations | Selected Short Trips | speed-acceleration distribution
1-1-1-1-1-1 |  | 
1-1-1-1-1-2 |  | 
・・・ | ・・・ | ・・・
N-N-N-N-N-N |  | 
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
20
40
60
80
100
Speed (km/h)
Acc. (km/h/s)
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
20
40
60
80
100
Speed (km/h)
Acc. (km/h/s)
-10
-8
-6
-4
-2
0
2
4
6
8
10
0
20
40
60
80
100
Speed (km/h)
Acc. (km/h/s)
This analysis will be done for each phase.

## Slide 25: 4.1.6. Selection of each ST duration
ST selection criteria
  ST within average ±1σ in each ST duration
    Average vehicle speed
    Acceleration duration ratio
    Deceleration duration ratio
  Smaller chi-squared value is higher priority
The number of potential STs in each ST duration
  Longer ST has more potential STs since it has bigger influence on chi-square value.
  Total number of combinations is less than 107～8 .
    Approximately 3 days on Xeon X5492 (Quad core, 3.4GHz)
X1
X2
X3
X4
X5 sec.
Y sec.
N units
N * X5/Y units
N * X4/Y
・・・

## Slide 26: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of high cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 27: 4.2.1. Process of high-speed cycle development
Determine the high-speed cycle duration (e.g. 600 sec.)
Determine the ST duration based on average ST duration and idling duration ratio of in-use data, the divide the ST into XX segments
  5 segments and 1 cruise
  More than 5 segments and 2 cruise
  Others
  <consider 2 phases (High-1 / High-2) cycle profile, if necessary >
Extract the driving data which meet each part’s configuration from in-use STs.
Select the least chi-squared extracted driving data in each part, then combine the these data to develop the High-speed cycle.
(note) if the complete in-use ST is less chi-squared value than combined High-speed cycle, this specific ST can be used for High-speed cycle.

## Slide 28: 4.2.2. (Example) Divide into 5 parts of High-speed cycle
Speed range | Frequency (%) | Target duration | Divide part
Idling | 3.1 | 18 | 9
0~75, 75~0 | 36.1 | 217 | 108
75~90, 90~75 | 30.0 | 179 | 89
90~ | 30.9 | 186 | 
Total | 100 | 600 | 
0 ~ 75 km/h, 108 sec
75 ~ 90 km/h, 89 sec
90 ~ 90 km/h, 188 sec
90 ~ 75 km/h, 89 sec
75 ~ 0 km/h, 108 sec
30%
31%
36%
Adjust 2 sec.
100％ = 600 sec.
3 %
Generate speed range and duration
  Divide into 3 speed range based on dividing frequency distribution
    Example: 0~75 km/h, 75~90 km/h, 90 km/h～
  Decide target duration in each range, then divide into two portions (take-off and slow-down)
    Example of 0~75km/h: 36% => 217 sec => take-off part 108 sec，slow-down 108 sec
(take-off 1)
(Cruise)
(slow-down 2)
(take-off 2)
(slow-down 1)

## Slide 29: 4.2.3. Extraction of driving data
Extract the driving data which meet each part’s definition* from in-use ST.
  Sample definition <Take-off 1 part>
  speed range : 0 ~ 75 km/h (with±0.5km/h), duration : 108sec.
Time
Veh. speed
Time
Veh. speed
Time
Veh. speed
0~75 | 75~90 | 90~90 | ・・・ | 75~0
 |  |  | ・・・ | 
 |  |  | ・・・ | 
 |  |  | ・・・ | 
 |  |  | ・・・ | 
 |  |  | ・・・ | 
0～75 km/h
108 s
0～75 km/h
108 s

## Slide 30: 4.2.4. Connection conditions
Connection conditions：
  Tolerance of the vehicle speed at connection point is ±0.5 km/h
    example: 75 ± 0.5 km/h
  The vehicle speed at connection point is adjusted to average of connected two points.
    The vehicle speed of the end of first segment: 74.8km/h
    The vehicle speed of the start of second segment: 75.2 km/h
    The vehicle speed of connected point will be 75.0 km/h
  Avoid the uncharacteristic connection
    OK: “Acc. => Acc. or Cruise” or “Dec. => Dec. or Cruise”
    Not OK: “Acc. => Dec.” or “Dec. => Acc.”
Acc. => OK
Cruise => OK
Dec. => NG
End point
1st segment
2nd segment
Start point
Acc.

## Slide 31: 4.2.5. Method to develop High-speed cycle
(take-off1)
(Cruise)
(slow-down2)
(take-off2)
(slow-down1)
Candidate driving data
combined
Least chi-squared distribution
Seek the combination cycle with least chi-square value compared with unified cycle

## Slide 32: Table of contents
Purpose
Outline of Test cycle development
  2.1. Overall process
  2.2. Basic concept
  2.3. Data collection matrix
Data processing
  3.1. Data processing
  3.2. Data conversion (U/R/M to L/M/H*)
  3.3. Develop the unified distributions and characteristics
Test cycle development
  4.1. Process of Low/Middle cycle development
  4.2. Process of high cycle development
Appendix. Compensated weighting factor
(*) U/R/M: Urban/Rural/Motorway, L/M/H: Low/Middle/High

## Slide 33: Compensated WF - 1
Weighting factor matrix
The collected data duration
It is expected that the collected data volume in each matrix doesn’t match the weighting factor obtained based on vehicle statistical information.

## Slide 34: Compensated WF - 2
  Need to compensate the weighting factor of each matrix since the specific short trip is possible to move into different matrix.
(1) Calculate the compensated weighting factor (wi’)
WU,PC,ON’ =
TU,PC,ON
WU,PC,ON
× AU,PC
WU,PC,OFF’ =
TU,PC,OFF
WU,PC,OFF
× AU,PC
WU,PC,E’ =
TU,PC,E
WU,PC,E
× AU,PC
Same equation will be applied to others
+
TU,PC,ON
WU,PC,ON
TU,PC,OFF
WU,PC,OFF
TU,PC,E
WU,PC,E
+
AU,PC =
WU,PC,ON
WU,PC,OFF
WU,PC,E
+
+
where

## Slide 35
Compensated WF - 3
The collected data was converted into new categories.
New weighting factors（wL, wM, wH） are calculated as follows.
This process will be done in each data collection CPs.