## Slide 1: Development of World-wide Light-duty Test Cycle -- Proposal for the threshold vehicle speed of Low/Middle/High(/extra-High) phase --
<number>
Proposed by Japan
(Reviewed by JRC, Mr. Steven and Ms. Ericsson)
DHC group
under GRPE/WLTP informal group
16 May 2011
ACEA, Brussels

## Slide 2: Table of contents
<number>
Proposal for the threshold vehicle speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study on data conversion threshold
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 3: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study on data conversion threshold
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 4: 1. Proposal for the threshold speed of L/M/H/ExH
<number>
Phase | Proposed threshold
Low | Vmax*≦60
Middle | 60 km/h＜Vmax*≦80
High | 80 km/h＜Vmax*≦110 km/h
Extra-High | 110 km/h＜Vmax*
Road type
Urban
Rural
Motorway
*)Vmax: Maximum vehicle speed of short trip
 This means that maximum vehicle speed in each test cycle phase will be less than each threshold speed (approximately by several km/h)
It was observed that the less difference of driving characteristics can be obtained on the threshold speed of [60/80/110/~].

## Slide 5: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study on data conversion threshold
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 6: 2.1. Overview of in-use data collection
<number>
(*) In-use data without road type indication will be combined with database after the determination of the threshold speed of L/M/H phase
[Amount of in-use driving data by 6 May 2011 Total: Approx. 840,000 km]

## Slide 7: 2.1. U/R/M analysis – driving characteristics
<number>
[Average speed]
[RPA]
[Average ST duration]
[Average IDLE duration]
Average speed of EU & US are higher than that of Asian countries
Difference was observed in each road category

## Slide 8: 2.2.1. U/R/M analysis – speed acceleration distribution
<number>
Difference in speed-acceleration distribution was observed in each road category.

## Slide 9: 2.2.2. U/R/M analysis – speed acceleration distribution
<number>
Difference in speed-acceleration distribution was observed in each road category.

## Slide 10: 2.3. U/R/M analysis – other distributions
<number>
Difference in each distribution was observed in each road category.

## Slide 11: 2.4. Summary of U/R/M analysis
<number>
It was observed that speed-acceleration distribution/driving characteristics in each region have difference in same road categories.
It is necessary to convert to L/M/H category in where driving characteristics are less difference in each region.
  Considering the threshold vehicle speed
    based on similarity of VA distribution
    based on similarity of V distribution
    based on similarity of other parameters
Max. speed
Short trip
Time (s)
Speed distribution
V-A distribution
Vehicle speed (km/h)
Idling
Ave. speed

## Slide 12: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study on data conversion threshold
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 13: 3.1. Study of data conversion
<number>
A comparative study was conducted between the following candidate criteria
In order to find appropriate criteria, the in-use driving data were converted to L/M/H according to the following criteria, then distributions and parameters were compared.

## Slide 14: 3.2.1. Similarity of speed acceleration distribution
<number>
Compare the average speed acceleration distribution with each region’s distribution.
the differences are evaluated by a normalized chi-squared value.
Zi,j : Frequency of Average distribution
Wi,j : Frequency of each region’s distribution
Normalized chi-squared value:
Compare
[Average of 5 regions]
[Region X]

## Slide 15: 3.2.2 Similarity of speed acceleration distribution
<number>
[Normalized chi-squared value]
It was observed that the less difference can be obtained at the threshold speed of [60/80/110/~], [60/90/110/~], [70/90/110/~] and [70/90/120/~].
If the value in column is small, the criteria have similarity between regions.

## Slide 16: 3.3.1. Similarity of speed frequency distribution
<number>
Compare the average speed frequency distribution with each region’s distribution.
Differences are evaluated by a normalized chi-squared value.
Zi : Frequency of Average distribution
Wi : Frequency of each region’s distribution
Normalized chi-squared value:
Compare
[Average of 5 regions]
[Region X]

## Slide 17: 3.2.2. Similarity of speed frequency distribution
<number>
[Normalized chi-squared value]
It was observed that the less difference can be obtained at the threshold speed of [50/80/110/~], [50/90/110/~], [60/80/110/~] and [70/90/110/~].
If the value in column is small, the criteria have similarity between regions.

## Slide 18: 3.3.1. Similarity of average speed
<number>
Compare the average speed with each region’s average speed.
Differences are evaluated by a Relative standard deviation (RSD).
RSD(%) = Standard Deviation / Average value * 100
Ave: 20.0
S.D.: 1.9
RSD: 9.5
Ave: 38.0
S.D.: 2.6
RSD: 6.7
Ave: 57.0
S.D.: 3.5
RSD: 6.2
Ave: 80.2
S.D.: 8.9
RSD: 11.0
[Example]

## Slide 19: 3.3.2. Similarity of average speed
<number>
It was observed that the less difference can be obtained at the threshold speed of [50/70/100/~], [50/70/110/~], [60/80/110/~] and [70/90/110/~].
[Average speed and Relative standard deviation (RSD)]
If the value in column is small, the criteria have similarity between regions.

## Slide 20: 3.4. Conclusion < appropriate threshold >
<number>
The threshold speed was considered based on 3 methods.
  based on similarity of VA distribution
  based on similarity of V distribution
  based on similarity of parameters
Threshold speed of [60/80/110/~] and [70/90/110/~] are best choice for less difference for all condition. Phase duration balance (refer slide 37) of [60/80/110/~] is better than that of [70/90/110/~].
Criteria | V-A distribution | V distribution | Average speed | Overall
50/70/100/~ |  |  | good | 
50/70/110/~ |  |  | good | 
50/80/110/~ |  | good |  | 
50/80/120/~ |  |  |  | 
50/90/110/~ |  | good |  | 
50/90/120/~ |  |  |  | 
60/80/110/~ | good | good | good | ◎
60/80/120/~ |  |  |  | 
60/90/110/~ | good |  |  | 
60/90/120/~ |  |  |  | 
70/90/110/~ | good | good | good | ○
70/90/120/~ |  |  |  | 
70/100/120/~ | good |  |  | 
[Similarity]

## Slide 21: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study on data conversion threshold
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 22: 4.1.1. L/M/H analysis @60/80/110/~ – Average speed
<number>
[Average speed]
[U/R/M]
[L/M/H]
Average speed is less difference in L/M/H phase but slight difference in Ex-High phase still exists.
*) Indian extra-high phase data is used as reference because there is few data

## Slide 23: 4.1.2. L/M/H analysis @60/80/110/~ – Average ST duration
<number>
[Average ST duration]
[U/R/M]
[L/M/H]
Average short trip duration become closer except India
*) Indian extra-high phase data is used as reference because there is few data

## Slide 24: 4.2. L/M/H analysis @60/80/110/~ – speed acceleration distribution
<number>
It was confirmed that VA distribution is less difference in L/M phase but slight difference in Extra-High phase still exists.

## Slide 25: 4.3. L/M/H analysis @60/80/110/~ – speed acceleration distribution
<number>
It was confirmed that VA distribution is less difference in L/M/H phase but slight difference in Extra-High phase still exists.
Few data

## Slide 26: 4.4. L/M/H analysis @60/80/110/~ – Other distributions
<number>
It was confirmed that vehicle speed frequency distribution is less difference in L/M/H phase
*) Indian extra-high phase data is used as reference because there is few data

## Slide 27: 4.5. Conclusion of verification of L/M/H
<number>
It was confirmed that each region’s driving characteristics and VA distributions comparatively show less difference by converting into Low/Middle/High/Extra-High phase based on threshold speed at 60/80/110/~ km/h.
Difference in Extra-High phase is still observed among US/EU and other regions.

## Slide 28: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study on data conversion threshold
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 29: 5.1. Regional weighting for distributions/characteristics
<number>
Regional weighting for L/M/H phase is necessary to represent each region driving when developing the unified distributions and harmonized cycle
[Regional weighting for each phase (Image)]
traffic volume ratio
Due to difference characteristics, apply absolute traffic volume ratio at each region
equal weighting
Due to same characteristics, apply equal weighting at each region
*) Traffic volume ratio is tentative value
=
=
=
=
=
=
=
=
=
=
=
=
One of recommendations :
Any other recommendations are welcome for more appropriate
regional weighting

## Slide 30: 5.2.1. Influence of the Regional weighting
<number>
Average speed will be similar in L/M/H phase but slight difference in Extra-High phase will be occurred.
Average speed 「60/80/110」
LOW
MIDDLE
HIGH
Extra-HIGH
Similar
Similar
Similar
Differ

## Slide 31: 5.2.2. Influence of Regional weighting
<number>
Traffic volume ratio
equal weighting
Proposal
L/M: equal
H/ExH: Traffic
Speed acceleration distributions are similar in L/M phase but slight difference in High/Extra-High phase.
equal weighting
traffic volume ratio
Similar
Differ
Similar
Differ

## Slide 32: 5.3. L/M/H traffic volume ratio @ 60/80/110/~
<number>
The unified distributions of High/Extra-High phase should be based on traffic volume.
  Due to the fact that the difference of VA distributions still exists in High/Extra-High phase.
  Due to the fact that the ratio of High/Extra-High phase of Japan, Korea and India are smaller than EU and US.
[Traffic volume ratio between L/M/H/ExH phase]
[60/80/110/~]
[70/90/110/~]

## Slide 33: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study of data conversion
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 34
<number>
6. Mode construction
L =www s
M = xxx s
L+M = 1200 s
H = yyy s
+
L =www s
M = xxx s
L+M+H+ExH = 1800 s
H =yyy s
L : M : H : ExH = based on traffic volume
If high phase duration is not enough long for stable sampling, divide into L+M and H+ExH mode construction.
Option-2
Option-1
ExH =zzz s
ExH =zzz s
H+ExH = 600 s

## Slide 35: Table of contents
<number>
Proposal for the threshold speed of Low/Middle/High/(+Extra-High)
In-use driving data analysis
Study of data conversion
Verification of L/M/H
Regional weighting
Mode construction
Next action

## Slide 36
<number>
7. Next Actions
 | 2011 2012 |  |  |  |  |  |  |  |  | 
 | Apr. | May | Jun | Jul. | Aug. | Sep. | Oct. | Nov. | Dec. | Jan
Meetings |  |  |  |  |  |  |  |  |  | 
In-use data collection |  |  |  |  |  |  |  |  |  | 
Develop the harmonized cycle |  |  |  |  |  |  |  |  |  | 
Validation |  |  |  |  |  |  |  |  |  | 
Open Issues |  |  |  |  |  |  |  |  |  | 
DTP Activities |  |  |  |  |  |  |  |  |  | 
Proposal of,
The threshold of L/M/H
High phase construction
Validation2
Validation1
Initial
analysis
Develop
1st WLTC
Final DEADLINE
for threshold
7th DHC
10th DHC
Modify, if necessary
Introduction of Draft WLTC
preparation
1st draft test procedure
8th DHC
62nd GRPE
2, 3, 4
5, 6, 8
Agreement
9th DHC
12th DHC
63rd GRPE
Interim Report of Validation 1
Detailed plan for Validation 2
Agreement of OIL
Proposal of,
2nd WLTC for Validation 2
1st Interim Report of Validation 2
7
Final
DEADLINE for cycle development
Regional weighting
Consider one high phase

## Slide 37
<number>
Open Issues -1
 | Issues | Discussion points | Status / Proposed Actions
1 | Deadline for submission of driving data | India and China requested deadline be extended to May | India has submitted all necessary data and information. Still waiting for China to submit.
2 | Regional Weighting when developing the WLTC | traffic volume same weighting | Expect to have discussion during the 7th DHC meeting based on the proposal in this slide.
3 | Threshold Speed for L/M/H | according to DHC-06-03 CP’s requirement | Expect to get agreement during 7th DHC meeting based on proposal in this slide.
4 | High Phase Cycle Construction (US&EU versus other regions) | only ONE unified cycle possess TWO types of High phase cycle | Expect to have discussion during the 7th DHC meeting based on the proposal in this slide.
5 | Mode Construction | a) cold start test only b) cold start & hot soak start | Basic agreement in DHC group is b).

## Slide 38
<number>
Open Issues -2
 | Issues | Discussion points | Proposed Actions
6 | Unique Weighting Factor for L/M/H Phase | harmonized weighting factors permit regional weighting factors | a) Is target of Informal Group Consider the possibility to accept b) for only CO2/Fuel consumption
7 | Gear Shift Points | fixed points based on vehicle specification others | Ms. Ericsson, Mr. Steven, JRC and JARI work together to finalize the method before developing the 1st WLTC.
8 | How to treat the vehicles which are not able to follow the prescribed cycle | continue to drive with wide-open-throttle exempt the H (or M&H) phase(s) others | Develop the proposal during validation 1 tests.
9 | Check the driving profile based on the vehicle characteristic |  | Analyze the in-use data based on vehicle characteristic (i.e. power to mass ratio)