## Slide 1: Study on cycle modification ~ Reflect validation test 1 result ~
10th DHC sub-group meeting
under GRPE/WLTP informal group
11-12 October 2011
Brussels, Belgium
Prepared by Japan

## Slide 2: Table of contents
Overview of Validation test 1 result
Proposal for Modification parts
Viewpoints of Modification
Proposal for WLTC v2 revised
Influence for X2 value
Justifications
  5.1. Review acceleration
  5.2. Review deceleration
  5.3. Review minimum speed

## Slide 3: 1.1. Overview of Validation test 1 result
can not follow the target speed during acceleration parts
can not trace the target speed during deceleration parts
have adverse influence on drivability / reproducibility

## Slide 4: 1.2. Potential area need to be modified
There are possibility that some vehicles can not trace the target, due to tire lock, shortage of brake power of rear wheel.
There are possibility that low/middle powered vehicles can not follow the target

## Slide 5: 2.1. Proposal for modification parts
1. delete creep drive
2. increase vehicle speed
3. increase vehicle speed (parallel translation)
4. replace short trips according to JRC proposal
5. reduce deceleration
6. reduce deceleration

## Slide 6: 2.2. Proposal for modification parts
7. reduce deceleration
8. reduce deceleration
11. reduce low deceleration
12. increase vehicle speed (parallel translation)
13. reduce acceleration
14.15.16. reduce deceleration
17. reduce acceleration
18. replace acc. portion
19. reduce deceleration
22. reduce deceleration
20. reduce deceleration
9. increase vehicle speed (parallel translation)
10. reduce deceleration
21. smooth dec.

## Slide 7: 2.3. List of proposed modification parts
# | Time | Modification
1 | 90 – 99 | delete creep portion
2 | 145 – 155 | delete deceleration portion during low speed part
3 | 189 – 204 | parallel translation to be minimum speed of 6.2 km/h
4 | 512 – 566 | replaced ST4 and ST5 based on JRC
5 | 661 – 664 | reduce deceleration
6 | 761 – 763 | reduce deceleration
7 | 974 – 978 | reduce deceleration
8 | 1057 – 1060 | reduce deceleration
9 | 1061 – 1064 | parallel translation to be minimum speed of 6.2 km/h
10 | 1127 -1128 | reduce deceleration
11 | 1148 -1149 | reduce deceleration
12 | 1150 -1156 | parallel translation to be minimum speed of 6.2 km/h
13 | 1157 – 1171 | reduce acceleration
14 | 1378 -1381 | reduce deceleration
15 | 1405 – 1406 | reduce deceleration
16 | 1433 – 1434 | reduce deceleration
17 | 1493 – 1500 | reduce acceleration
18 | 1520 – 1552 | replace acceleration phase
19 | 1520 – 1552 | reduce deceleration
20 | 1720 - 1722 | reduce deceleration
21 | 1773, 1776 | smooth deceleration
22 | 1780 - 1783 | reduce deceleration

## Slide 8: 3. Viewpoints of Modification
Acceleration
  Review acceleration portions based on comments from the participant laboratories
  Set maximum acceleration ratio 95 percentiles of cumulative frequency in each speed range
    Ex-HIGH: replace high acceleration part (65 - 130km/h) by alternative acceleration part from in-use database which match the 95 percentiles
Deceleration
  To avoid tire lock and/or shortage of brake power, set maximum deceleration to appropriate value (- 5.31 km/h/s)
Drivability / reproducibility
  Because Low speed portion (e.g. creep drive) have an adverse influence on drivability and reproducibility, minimum speed should be set to Vidle on 1st gear

## Slide 9: 4.1. Proposal for modification
1. delete creep drive
3. increase vehicle speed (parallel translation)
2. increase vehicle speed (delete deceleration portion)

## Slide 10: 4.2. Proposal for modification
4. replace short trips according to JRC proposal
5. reduce deceleration
6. reduce deceleration

## Slide 11: 4.3. Proposal for modification
7. reduce deceleration
8. reduce deceleration
10. become low deceleration
9. increase vehicle speed (parallel translation)
11. reduce deceleration
12. increase vehicle speed (parallel translation)
13. reduce acceleration

## Slide 12: 4.4. Proposal for modification
14.15.16. reduce deceleration
17. reduce acceleration
18. replace acceleration portion
19. reduce deceleration
22. reduce deceleration
20. reduce deceleration
21. smooth deceleration

## Slide 13: 4.5. VA distribution of WLTC v2

## Slide 14: 4.6. VA distribution of WLTC v2 rev.

## Slide 15: 5.1. Influence for X2 value
In HIGH and Ex-high phase, When the cycle was modified, X2 value become smaller and then test cycle have more representativeness

## Slide 16: 5.2. Comparison of VA distribution – LOW & MIDDLE
[Unified distribution]
[WLTC v2]
[WLTC v2 rev]

## Slide 17: 5.3. Comparison of VA distribution – HIGH & Ex-HIGH
[Unified distribution]
[WLTC v2]
[WLTC v2 rev]

## Slide 18: 6.1.1. Review acceleration for MIDDLE phase
1) 30～35 km/h
1) 30~35 km/h
2) 35～40 km/h
84.0 ~ 92.5 percentiles
88.1 ~ 94.7 percentiles
[MIDDLE phase]
Because acceleration in middle phase keep in 95parcentiles, it is not necessary to modify the acceleration parts in middle phase
1 2
2) 35~40 km/h
No need to be modified
No need to be modified

## Slide 19: 6.1.2. Review acceleration for HIGH phase - 1
35～55 km/h, 5km/h steps
(1) 35 – 40 km/h
(2) 40 – 45 km/h
(3) 45 – 50 km/h
(4) 50 – 55 km/h
82.8 ~ 91.0 percentiles
86.1 ~ 93.0 percentiles
89.5 ~ 95.1 percentiles
84.2 ~ 92.2 percentiles
[HIGH phase]
1 2 3 4 5 6 7
No need to be modified
No need to be modified
No need to be modified
No need to be modified

## Slide 20: 6.1.3. Review acceleration for HIGH phase - 2
55～70 km/h, 5km/h steps
88.1 ~ 94.7 percentiles
92.0 ~ 96.5 percentiles
94.6 ~ 97.8 percentiles
[HIGH phase]
In HIGH phase, acceleration exceed 95 percentiles in the range of 60 to 70 km/h, Therefore it is necessary to reduce acceleration
(5) 55 – 60 km/h
(6) 60 – 65 km/h
(7) 65 – 70 km/h
1 2 3 4 5 6 7
Need to be modified
No need to be modified
Need to be modified
95% ≒ 3.6 km/h/s
95% ≒ 3.3 km/h/s

## Slide 21: 6.1.4. Review acceleration for Ex-HIGH phase-1
[Ex-HIGH phase]
90.0 ~ 95.1 percentiles
96.3 ~ 98.4 percentiles
97.3 ~ 98.8 percentiles
96.2 ~ 98.3 percentiles
25～115 km/h, 5km/h steps
(1) 25 – 30 km/h
(2) 35 – 40 km/h
(3) 40 – 45 km/h
(4) 50 – 55 km/h
1 2 3 4
5 6 7 8 9101112
Need to be modified
Need to be modified
Need to be modified
No need to be modified
95% ≒ 5.8 km/h/s
95% ≒ 6.2 km/h/s
95% ≒ 5.2 km/h/s

## Slide 22: 6.1.5. Review acceleration for Ex-HIGH phase-2
[Ex-HIGH phase]
97.3 ~ 99.0 percentiles
99.3 ~ 99.7 percentiles
99.5 ~ 99.8 percentiles
99.1 ~ 99.7 percentiles
25～115 km/h, 5km/h steps
(5) 75 – 80 km/h
(6) 80 – 85 km/h
(7) 85 – 90 km/h
(8) 90 – 95 km/h
1 2 3 4
5 6 7 8 9101112
Need to be modified
Need to be modified
Need to be modified
Need to be modified
95% ≒ 3.3 km/h/s
95% ≒ 3.6 km/h/s
95% ≒ 3.1 km/h/s
95% ≒ 4.0 km/h/s

## Slide 23: 6.1.6. Review acceleration for Ex-HIGH phase-3
[Ex-HIGH phase]
98.1 ~ 99.4 percentiles
98.6 ~ 99.6 percentiles
In Ex-HIGH phase, acceleration exceed 95 percentiles in the range of 35 to 55 km/h and 75 to 115 km/h. Therefore it is necessary to reduce acceleration
25～115 km/h, 5km/h steps
(9) 95 – 100 km/h
(10) 100 – 105 km/h
(11) 105 – 110 km/h
(12) 110 – 115 km/h
1 2 3 4
5 6 7 8 9101112
96.0 ~ 99.0 percentiles
85.6 ~ 96.9 percentiles
Need to be modified
Need to be modified
Need to be modified
Need to be modified
95% = 2.3 km/h/s
95% ≒ 2.4 km/h/s
95% ≒ 2.5 km/h/s
95% ≒ 2.8 km/h/s

## Slide 24: 6.2.1. Acceleration portion for Ex-HIGH
The 95% of cumulative frequency in each speed range are as follows;
Ex-HIGH | 95 percentiles
75 – 85 | 3.5 – 4.5 km/h/s
85 - 100 | 2.5 – 3.5 km/h/s
100 - 115 | 1.5 – 2.5 km/h/s
Search acceleration portion which meet the above criteria from in-use database
Select the shortest / highest acceleration one

## Slide 25: 6.2.2. Ex-HIGH (65-130 km/h)
65-130km/hまでの区間を32秒で到達する加速データを選択
[Time series 60 – 130 km/h]
[Speed vs. Acceleration]

## Slide 26: 6.3. maximum deceleration
For light duty truck and/or FR (front engine – rear drive) vehicle, maximum deceleration should be reviewed. Maximum deceleration of current test cycle for certification is as follows;
 | NEDC | UDDS | JC08
Maximum deceleration | -5.00 km/h/s (-1.389 m/s2) | -5.31 km/h/s (-1.475 m/s2) | -4.05 km/h/s (-1.125 m/s2)
It's preferable to be the maximum deceleration of -5.31 km/h/s

## Slide 27: 6.4. Minimum speed of short trip (Vidle of 1st gear)
Minimum vehicle speed should be 6.2km/h
(*) Vidle: Vehicle speed @ idling engine speed
Gear | Average of V1000 | Average of Vidle
1 | 7.5 | 6.2
2 | 15.0 | 12.4
3 | 22.5 | 18.6
4 | 29.9 | 24.8
5 | 37.6 | 31.0
6 | 46.7 | 37.7
*) Calculated based on vehicle specification of submitted in-use driving data)
(Unite: km/h)