## Slide 1: The important factor to develop test cycle
<number>
10th DHC sub-group meeting
under GRPE/WLTP informal group
11-12 October 2011
Brussels, Belgium
Prepared by Japan

## Slide 2: Driving energy
<number>
◆When the road gradient is small, it is able to estimate cosθ≒1，sinθ≒θ/100
◆In general, there are relationship between Fuel consumption (L/km) and Driving energy (Wh/km=J/km). Driving energy can be calculated as follows;
(*) Work [Nm=J] ＝ Force * Dist., Power [J/s=W] = Work / time
(*) Driving energy [J/km]＝Cum. Work [Wh] / Dist. [km]
Speed and frequency
Speed*Acceleration and frequency

## Slide 3: The important factor
<number>
The important factors are “speed”, “speed * acceleration” and “Time (frequency)”.
  It means that “speed-acceleration distribution” and “speed frequency distribution” are important.
DHC methodology
  speed-acceleration distribution (the least X2 )
  speed frequency distribution
  “Average speed”, “acc./dec./cruise/idle ratio”, RPA and so on

## Slide 4: Summary
<number>
RPA (Dynamics) is one of important factor. However we should also consider other parameter / frequency distribution.

## Slide 5: One idea
<number>
We can modify test cycle which have dynamics based on original method.
At least XX% etc..

## Slide 6
<number>

## Slide 7: Relationship between Average speed and CO2 emission
<number>
20
40
60
80
100
Average speed [km/h]
CO2
[g/km]
WLTC total
WLTC Middle
WLTC Low
WLTC High
WLTC Ex-high
NEDC
CO2 = a * V2 + b * V + c * V-1 + C
Dynamics
+/- 10%
Curve on transient cycle

## Slide 8: Cold / Hot ratio
<number>
Hot
Cold
Hot
Cold
NEDC
1200 sec
1800 sec
WLTC
Cold/Hot ratio should be considered