## Slide 1: WLTP-E-Lab Sub Group Progress report WLTP-DTP-E-LabProc-012
Leader: Per Ohlund / Kazuki Kobayashi

## Slide 2: Meeting
1st meeting:
Date:30.9.2010
Location: Phone conference
Topics: Terms of reference & action plan was proposed.
2nd meeting:
Date:13-14.10.2010
Location: Vienna
Topics: Terms of reference & action plan was agreed.
Top 5 issues were discussed.
To make a comparison table.( to compare the details of Jp/EU/US regulations)

## Slide 3
3rd meeting:
Date:24-25.11.2010
Location: Brussels
Topics: Discussion open issues.
gtr text: part of BEV
4th meeting:
Date:16.12.2010
Location: Phone conference
Topics: working schedule for gtr text.
gtr text :part of Definition

## Slide 4: Open issue list1
A/P/OI | Item | Issue | Action
OI | Utility factor | The us and jp regulation has methods which include statistical analysis. ( EU:25km) | These methods will be considered.
OI | SOC | For CS mode, it could be necessary to compensate the CO2/fuel consumption based on SOC balance to obtain correct value. (for CD mode, no need to compensate). | Need results about the driving cycle from the DHC group to continue the discussion.
P | Shorten the test procedure: | Current requirement (full charge to empty) is basic procedure. As an option, need to adapt the shorten procedure to reduce testing burden (i. e. SAE J1634) | 
OI | CO2 compensation for range test | Separation point of CD mode and CS mode in one cycle is agreed but the method on how is still an open issue. | Still an open issue.
A | Energy consumption test condition | Battery temperature requirements | Follow recommendation from ICE group regarding ambient temperature, in phase 1 only normal ambient temperature and in phase 2 consider cold ambient temperature.
OI | Road load | In case of the vehicle with no mechanical neutral | Follow recommendations from ICE group except in cases where there are differences for example no mechanical neutral gear. Agreed to consider minimum requirement. This will make flexibility for future technical development and prevent judgment variation by contracting parties.
OI | Weighting factor | The vehicles which have difficulty to follow the prescribed cycle. (like as electrified vehicles for only urban) | follow development in the DHC group. Vehicles that will have problem following the driving cycle will be considered by the DHC group.

## Slide 5: Open issue list2
A/P/OI | Item | Issue | Action
OI | Emission worst test | General opinion to avoid to large number of tests. | Still an open issue.
A | Run in mileage | Run in mileage for test | 300km or more
A | Charging condition | to not regulate the possibility to soak outdoor. (proposed by Jp) | It could be a safety issue for by some contracting parties if we do not allow charging outdoor.
A | Charging method | charging method | manufacture's recommended
A | Charging time | Soak time:12 hr or more, less than 36hr.Charging time: Stop with full charged. | Upper limit for charging time is 36 hr.
OI | criteria for end of charging | which is the criteria ”plug-off” or indication of charging completed from the vehicle. | Still an open issue.
P | Interruption condition | Less than 3 minutes interruption is possible for every one cycle. During interruption, main power may be OFF. | still an open issue. Needs the driving cycle from DHC.
OI | test termination condition | Test termination condition for range measurement | Still an open issue.
A | Stop condition | Proposed stop condition :Accel Off ,and press braking pedal when 5 km/h or lower to stop. | agreement

## Slide 6: Open issue list3
A/P/OI | Item | Issue | Action
A | Discharge condition | Discharge condition before test: Discharge until manufacture's recommended level | agreement on the proposal and a wish that this should be optional and not a requirement. And also to add temperature condition for the discharge driving.
OI | Watt-hour meter measurement accuracy | US and JP:+/-2% EU:+/-0.2% | To be discussed
OI | Accuracy of ammeter | JP:+/-1% F.S. EU:+/- 0.5% | To be discussed
OI | LOD of ammeter | JP:0.0001Ah (<=50A) 0.001Ah(>50A) EU:Regulation 0.3% | To be discussed
OI | SOC tolerance | calculation method for delta SOC | To be discussed
OI | CD test | calculation method for CD test (fuel consumption) | To be discussed

## Slide 7: Road map for gtr draft
X: phone conference

## Slide 8: Appendix
Terms of reference
Comparison table (for example)
gtr text (for example)