## Slide 1: WLTP DTP PM-PN Subgroup Activities, Progress & Future Plans
4th DTP Meeting
Geneva
12th January 2011
Chris Parkin

## Slide 2: Outline
      Organisation
      Meetings Held
      Open Issues
      Closed Issues
      Future Plans

## Slide 3: Outline
      Organisation
      Meetings Held
      Open Issues
      Closed Issues
      Future Plans

## Slide 4: Organisation
Terms of Reference & Plan of Activity
  WLTP-DTP-PMPN-01-02
Sub-group divided into small groups reviewing
  Dilution system & PM sampling specifications
  PM weighing chamber specifications, PM calibration and calculations
  Periodic regeneration measurement and DPF conditioning
  Particle number measurement & calibration
Small groups will meet/teleconference between Sub-group meetings & report back to sub-group

## Slide 5: Outline
      Organisation
      Meetings Held
      Open Issues
      Closed Issues
      Future Plans

## Slide 6: Subgroup Meetings Held
1st Web Conference – 7th July
  Agreed Terms of Reference and Plan of Activity
  Agreed decision on whether to mandate both PM and PN measurement was for DTP, WLTP or GRPE
  Measurement ranges of <2 – 50mg/km PM & <6x1011 – 5x1013 #/km PN (to include OBD test cases)
  PN during regen identified as an Open Issue
2nd Web Conference – 11th August
  Regulatory content comparison work subdivided into themes for examination by “small groups”
  Use of secondary dilution, CVS max temperature during regen and background correction identified as additional Open Issues

## Slide 7: Subgroup Meetings Held
3rd Web Conference - 15th September
  Relevant regulatory content template completed
  Small group regulatory comparison initial conclusions reported
  Planning of further small group meetings
4th Web Conference – 1st October
  Further conclusions from small group regulatory comparison work reported
  Plan of post October Activity agreed
5th Meeting – 4th November
  Lab processes dilution system specification reviewed
  Open Issues List reviewed. Some issues closed, agreed data gathering required to resolve other issues, consideration of some (linked) issues deferred

## Slide 8: Outline
      Organisation
      Meetings Held
      Open Issues
      Closed Issues
      Future Plans

## Slide 9: Open Issues
Transfer, dilution & PM sampling
CVS temperature (non-regen tests) <52°C (ECE & Jp), 47°C +/- 5°C (US)
CVS temperature during regen <190°C (ECE & Jp), <52°C single dilution <190°C double dilution (US)
Transfer tube coupling sealing materials – minimise contact with exhaust
Transfer tube insulation
Transfer tube length
Use of remote mixing tee e.g. for SI engines and implications on dilution system requirements
Dilution air filtration efficiency 99.97% (US), 99.95% or H13 (ECE) – 99.95% subject to EPA views
PM/PN dilution air background correction permitted (US & Jp), tunnel background permitted (ECE) – permit up to specified maxima subject to EPA & CARB views
Dilution tunnel pressure variation at mixing point

## Slide 10: Open Issues
Transfer, dilution & PM sampling
Particle pre-classifier probe mounted or in-line alternatives, location of in-line pre-classifier – clarify these are alternatives and need not be on filter holder
Double dilution permitted (Jp & US), not permitted (ECE)
Dilution tunnel pre-conditioning
Temperature of dilute gas should be controlled by dilution not cooling (US)
Requirements to verify proportionality of PM sampling
Dilution air temperature >15°C (Jp), 25°C +/-5°C (US)
Sampling pump location
Single PM filter for whole test or filter per cycle phase – separate filter per phase NB DEPENDS ON DHC DECISIONS ON PHASE LENGTH v WEIGHTING FACTORS
Back-up filters – No back-up filters subject to CARB views on artefact correction
PM probe diameter
Distance/residence time from PM probe to filter holder

## Slide 11: Open Issues
Transfer, dilution & PM sampling
Temperature at PM flow meter, constant or measured real-time for flow correction
PM sampling shut-off valve position relative to filter holder. May need upstream valve for PHEV multiple cycle sampling to facilitate filter paper changes
Minimum filter mass – Delete?
Filter face velocity 20-80cm/s (ECE), 100-105 cm/s (US), 35-100cm/s (Jp)
Filter paper type. Recommend or merely allow PTFE membrane. Velocity at which collection efficiency defined.

## Slide 12: Open Issues
Weighing chamber, microbalance & PM calibration
Tolerances for temperature, dew point temperature and relative humidity. Not all regions have requirements for all three parameters.
Micro-balance precision tighter in US 1065 & J42 than for US 86 and R83. Various recommendations are given for micro-gram balance installation, static neutralisation & shielding. – Consolidate guidance, review precision on a cost-benefit basis
Filter conditioning time US 1065 has no maximum time. Differences exist in max time permitted between removal of filter from stabilisation environment and emissions test; time allowed to return filter to stabilisation environment after the emissions test; and max conditioning time permitted. – Specify static nullifier?
Sample filter handling various guidance provided.

## Slide 13: Open Issues
Weighing chamber, microbalance & PM calibration
Microbalance calibration weight requirements not specified (US part 86 & ECE), “E2” weights (Jp), NIST traceable within 0.1 % uncertainty (US part 1065). Only US part 1065 puts a specification on cal mass relative to unused filter mass.
Microbalance calibration frequency discrepancy between zero/span requirements and annual cal requirements.
Reference filter weighing, max time between sample and ref filter weighing after the emissions test vary. Acceptance criteria and actions if initial results out of tolerance vary. US part 86 requires ref filters to be covered at all times. US part 1065 recommends balance exercise and substitution weighing method.
PM calculations equivalent except US 1065 generalised, not CVS specific.
Specify detailed flow meter calibration procedure in WLTP – Yes?

## Slide 14: Open Issues
PN
PN measurement during DPF regen
  Is VPR volatile removal efficiency sufficient
  Is tetracontane appropriate for evaluating efficiency if used for regeneration measurements
VPR minimum solid particle penetration efficiency (none at present ECE)
Use average or second by second particle concentration reduction factor
PNC calibration frequency (12 months)
PNC calibration aerosol materials
VPR particle concentration factor validation (3 monodisperse sizes)
VPR filtration specification for dilution air and leak checks

## Slide 15: Outline
      Organisation
      Meetings Held
      Open Issues
      Closed Issues
      Future Plans

## Slide 16: Closed Issues
Avoidance of condensation in dilution/sampling systems – Lab Processes Sub-Group proposal has been reviewed and is acceptable
Permissible variation in static pressure at exhaust tailpipe – Lab Processes Sub-Group proposal has been reviewed and is acceptable
Use of heat exchanger for PM sample flow control – Not required
Dilution system residence time - Lab Processes Sub-Group proposal has been reviewed and is acceptable
Molar based PM calculations - Lab Processes Sub-Group proposal has been reviewed and is acceptable

## Slide 17: Closed Issues
Particle sampling system bend radii – WLTP should specify radius of curvature should be “as large as possible”
Dilute exhaust gas thermocouple type – Type need not be specified
PM probe location on CVS centreline – Not necessary
Isokinetic sampling – Outside of WLTP Phase 1 scope
PM filter holder design/stain area – At least 1075mm2 stain area
VPR volatile removal efficiency specification – Retain current specification
PNC flow check 5% tolerance - Retain

## Slide 18: Outline
      Organisation
      Meetings Held
      Open Issues
      Closed Issues
      Future Plans

## Slide 19: Future Plans
to May 2011
Objectives
  Gather (primarily existing) data to review and resolve Open Issues
  Commence drafting of PM-PN elements of GTR text
Working Method
  small groups, meeting by web and telephone conference, will gather data and develop proposed solutions to Open Issues
  Proposed solutions, along with rationales, will be circulated to the subgroup. The subgroup will decide whether to accept the proposed solution or refer back to the small group for further consideration
Sub-group Meetings
  31st January
  March
  May

## Slide 20: Future Plans
June 2011
Objectives
  Reach final agreement on all Open Issues
  Continue drafting PM-PN elements of GTR text
July – September 2011
Objectives
  Complete drafting of PM-PN elements of GTR text