## Slide 1
slide <number>
LabProcICE issues
on DTP level
Zuerich, 12.-14. April 2011
Notes: <number>

## Slide 2
slide <number>
1) RLD: Inertia classes
LabProc: Testroom and soak area temperature
ME: Method for subtraction of pollutant mass in intake air
General: definitions
Overview

## Slide 3
slide <number>
The LabProcICE proposal of refined uniform inertia classes of 60 kg steps was in principle accepted at DTP4. A stepless approach was rejected due to difference to US certification.
Objective is clear information for the customer at lower CO2 levels with future vehicle techniques. However certification should remain efficient (influence of small step approach on family concepts).
COM requested information regarding the influence on CO2 emissions and fuel consumption of the proposed 60 kg inertia steps.
In the meantime ICCT published an additional proposal of a stepless or smaller step approach. Aim is to enable even more refined CO2 values especially for lower vehicle weights.
1) Inertia Classes

## Slide 4
slide <number>
Inertia classes proposal overview (based on WLTP-DTP-LabProcICE-054 by ICCT)

## Slide 5
slide <number>
Current legislation: JP, ECE, US: 20-30 °C
GTR 2 & 4: 25 ± 5 °C
 LabProcICE: setpoint (25 ± 5) °C
Pro: harmonization with GTR 2 & 4 improved reproducibility by set point
Contra: not representative for real world
 Alternative proposal (by EC): lower temperature, e.g. 22°C
EC / JRC and India will provide measurement data to evaluate the influence on CO2 at different temperatures
 Needs decision before start of validation 2 testing
2) Test Room and Soak area temperature

## Slide 6
slide <number>
CVS as well as Bag-Mini-Diluter don’t consider the pollutant level that is contained in the combustion or intake air of the vehicle.
Exhaust emissions and limit values approaching the concentration levels present in ambient air (e.g. for highly electrified-operating vehicles  intake air has increasing influence on the emission result
Aim of proposed method: measure low pollutant mass with higher accuracy
Political discussion of the definition of exhaust emission necessary
Typical contributions of the intake air pollutant level to emission result are illustrated in table 1 of the proposal
3) Method for subtraction of pollutant mass in intake air (WLTP-DTP-LabProcICE-020)

## Slide 7
slide <number>
Different meanings of the word „background“ as a contribution to mass
Background 1
diluent air
Background 2
from mixing point
to point of sampling
Background 3
inside transfer tube
Background 4
Intake air from room
Background 5
Artifacts on Filter

## Slide 8
slide <number>
Background 1
Diluent air
Background 2
from mixing point
to point of sampling
Background 3
inside transfer tube
Background 4
Intake air from room
Background 5
Artifacts on Filter
at point of sampling means there are some left overs, contaminations of THC, PM, PN inside the surface of tubes an pipes
All constituents are important including CH4, N2O for the near future
    Left overs, contamination of PM, PN, H2O and THC are important, with the option - Cap end of tube
All constituents are important including CH4, N2O for the near future
Filter material gains weight from something unknown called artifacts, just in air or other gases
Different meanings of the word „background“ as a contribution to mass

## Slide 9
Feedback at (and after) DTP-4 meeting:
COM, UK in principle supportive, but scrutiny regarding expected effect on emission results
US & Japan had (scrutiny) reservations: - what happens to intake air pollutants (e.g. NOx, N2O or CO2) during the combustion process and post combustion catalytic treatment? - correction for pollutants in the intake air would presumably force US to lower current US emissions standards/limits to maintain current levels of stringency (US EPA definition of exhaust emissions refers to absolute emissions -> in contradiction to relative approach)

## Slide 10
slide <number>
LabProcICE proposes the following Terms of Reference for drafting the definitions in the future WLTP gtr:
  No references to other parts or documents should be included (stand alone)
  Repetition of other parts of the regulation to be avoided
  As short as possible but with sufficient detail to be clear and precise. For example, avoiding repetition of descriptions of test conditions (see above)
4) Definitions

## Slide 11
slide <number>
  Technically neutral definitions wherever possible
  All definitions should be located in one section of the gtr
  Definitions should be listed in alphabetical order with English spelling
All results of the working groups should be frequently delivered to the Drafting Coordinator (DC) who is expected to manage drafting of the definitions, esp. with regard to common definitions used by several subgroups. DC will consolidate them into the gtr text and report to the GRPE Informal Group.
LabProcICE will focus on definitions necessary for validation testing and sees its primary responsibility only for specific definitions, e.g. RLD related.