## Slide 1: WLTP DTP PM-PN Subgroup Activities, Progress & Future Plans
6th DTP Meeting
Geneva
8th June 2011
Chris Parkin

## Slide 2: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 3: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 4: Subgroup Meeting
9th Meeting – 3rd May
  The following Open Issues were reviewed;
    Dilution air filtration,
    Background corrections,
    Sample cooling,
    Sample shut-off valve location,
    Filter media specification, conditioning & handling
    PM Microbalance precision and calibration
    Reference filter weighing
    PM calculations

## Slide 5: Subgroup Meeting
  Open Issues review cont.
    PN during regeneration
    VPR solid particle penetration efficiency
    PNC calibration aerosol
  The draft GTR text was reviewed. An updated text has been circulated as document PMPN-09-06 rev.3.

## Slide 6: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 7: Closed Issues
PM Sampling
A8 Dilution air filtration efficiency: 99.95% agreed [JASIC would prefer 99.97%]
(partial) A9 Background correction: Tunnel or dilution air background included as regional options. Tunnel background should be measured on day of test, following any tunnel pre-conditioning
A16 Sampling cooling: text is acceptable as is, without explicit reference to sample cooling
A20 Data logging frequency: 1Hz for all parameters for consistency
A27 proportionality of PM sample flow rate: verify on system commissioning and then as required by technical authority

## Slide 8: Closed Issues
PM Sampling cont.
A35 Shut-off valve location: downstream of filter holder
A38 Filter media: Either membrane or coated filter, collection efficiency specification corrected based on input from Pall
PM weighing
B2 Microbalance precision: 1g as per GTR 4 accepted
PN
D4 PNC Calibration frequency: 13 month interval agreed with a requirement to either monitor PNC counting efficiency versus a reference or change PNC wick every 6 months

## Slide 9: Closed subject to review e.g. due to Validation 2 or DHC conclusions
PM sampling
A2 CVS temperature during regen: 190C maximum subject to validation experience
A26 Number of PM sample filters required: one for cold start phase, one for all hot start phases combined, subject to DHC cycle design/weighting

## Slide 10: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 11: Open Issues
PM sampling
A9 background correction: Maximum permissible PN correction. Dilution air background measurement (rolling average or on day of test).
A15 Tunnel pre-conditioning procedure: review during validation whether recommended 20 mins at 120kph is sufficient, text amended to clarify that longer, hotter pre-conditioning is permissible.
PM weighing etc
B3 PM sample filter conditioning: reviewing minimum filter conditioning period based on data from different labs and different vehicle technologies
B6 Reference filter weighing: > 2 reference filters of same size and media as test filters, replace every 30 days or more frequently. Still considering acceptance criteria
B7 PM calculations: awaiting proposed text

## Slide 12: Open Issues
Regeneration
C1 PN measurement during regeneration: limited available studies suggest current VPR and PNC cut-off are suitable for regeneration measurements. Propose making additional experimental measurements during Validation 2 to confirm. Need to consider regeneration test procedure/weighting, repeat hot start cycles during regen testing will artificially depress PN.
Particle Number
D1 VPR minimum solid particle penetration efficiency: 70% at 100nm proposed, plus current max ratios for pcrf30nm:pcrf100nm and pcrf50nm:pcrf100nm. Reviewing whether ratios could be tightened based on available data.
D5 PNC calibration aerosol: subgroup will develop updated calibration guidance documents in parallel to Validation 2.

## Slide 13: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 14: Points to Note
DHC construction should permit use of PM single filter for all hot start phases, i.e. no phase weighting factors, to minimise measurement errors
DPF regeneration testing procedures should permit repeat cycles to be run back to back without intermediate cold starts or hot soak.
Want to gather data during validation on PN during DPF regeneration;
  To confirm PN measurement system is capable of excluding worst case volatile material during DPF regenerations
  CVS and filter face temperatures during regenerations?
Want to gather data during validation on tunnel background levels
  Is 20 minutes pre-conditioning at 120kph sufficient?
  Tunnel PN background levels

## Slide 15: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 16: Amendments to GTR Text
Document: WLTP-DTP-PMPN-09-06 rev.3
Definitions
Buoyancy correction
Compression ignition engine
Continuous regeneration
Particle number
Particulate matter
Particulate matter weighing chamber
Periodic regeneration
Positive ignition engine

## Slide 17: Amendments to GTR Text
List of Symbols & Acronyms updated
Exhaust transfer tube – heating added as an optional alternative to insulation. Connection sealing elastomers should be thermally stable and not bridge connection
Dilution tunnel mixing point pressure variation – deleted. Dealt with by pressure variation requirements at tailpipe
PDP & CFV Dilution system schematics – updated and made consistent
PM & PN background measurements – either dilution air or tunnel background permitted at discretion of contracting party up to maxima of 1mg/km and TBD PN/km. Tunnel background measurements must be on day of test after any tunnel pre-conditioning
PM filter weighing procedures – sample and reference filter weighing procedures added

## Slide 18: Amendments to GTR Text
Calibration requirements – microgram balance, VPR and PNC requirements inserted
Tunnel pre-conditioning – text amended to explicitly permit longer and/or higher speed running if required
Double dilution – text added to permit this as an option provided dilution system accuracy requirements are still met
PM & PN calculations – text amended to reflect option to use double dilution and introduction on PN background correction
Partial flow dilution systems – text deleted, not permitted for WLTP phase 1
PM & PN Measurement & weighing chamber specifications – moved to Annex III (measurement equipment) and updated
Regeneration test procedures – text amended to explicitly permit use of a single filter for PM measurement over repeat cycles required to complete regeneration

## Slide 19: Outline
      Meetings
      Closed Issues
      Open Issues
      Points to Note
      Amendments to GTR Text
      Future Plans

## Slide 20: Future Plans
June/July 2011
Objectives
  Reach final agreement on remaining Open Issues
  Finalise PM-PN elements of GTR text
Post July
Objectives
  Update PN calibration guidance documents
  Review data from Validation 2 on tunnel background, tunnel pre-conditioning & PN during regeneration