## Slide 1: WLTP-DTP Subgroup Additional Pollutants Progress report
WLTP-DTP-AP, Mörsch/Astorga
GENEVA UN EC
Date: 08. June 2011
M. C. Astorga Llorens
Sustainable Transport Unit
Institute for ENERGY
EC-DG JRC, Ispra (IT)
Notes: <number>

## Slide 2
Terms of reference and scope of the work of this sub-group
Pollutants addressed and General guidelines
Meetings schedule
Table of candidate methods
Definitions/ Abbreviations
Open questions in the GTR Draft document
Conclusions and next steps; documents loaded in CIRCA Database
WLTP-DTP-AP,
O. Mörsch / C. Astorga
Notes: <number>

## Slide 3
The Additional Pollutants subgroup received a mandate for the development of test procedures for pollutants not currently regulated such as NO2, NH3, N2O including measurement equipment and formulae for the measurement for light duty vehicles.
Additional pollutants subgroup – Terms of reference
Scope of Activity
The subgroup undertakes the following tasks on the basis of procedures in existing legislation and expert knowledge within the group:
  Agree on additional pollutants to be addressed.
  Identify appropriate measurement methods for each pollutant.
  Describe measurement, calibration procedures as well as calculations based on existing legislation and on output from lab procedure subgroup.
  Drafting of GTR legislation text.
in progress
in progress
WLTP-DTP-AP,
O. Mörsch / C. Astorga
Notes: <number>

## Slide 4
WLTP-DTP-AP, Mörsch/Astorga
Meeting schedule
First Meeting: Telephone/Web Conference
Date: 20th July 2010
16 participants
2nd Meeting: Telephone/Web Conference
Date: 20th July 2010
20 participants
3rd Meeting: Face to face meeting at JRC/Ispra
Date: 9/10 Dec. 2010
14 participants
4th Meeting: Face to face meeting at BMW/Munich
Date: 7/8 March 2011
18 participants
5th Meeting: Face to face meeting at JRC/Ispra
10/11 May 2011
5 meetings (2 phone conferences and 3 face to face meetings in December 2010, March and May 2011)
for the time being, no further face to face meeting planned
Notes: <number>

## Slide 5
NO2
NH3
N2O
Ethanol (EtOH)
Aldehydes: Formaldehyde, Acetaldehyde (RCHO, R = H or Me)
Pollutants to be addressed:
NOTE: Any other pollutants not included in this list should be supported by an assessment on negative effects to health or to the environment.
Notes: <number>

## Slide 6
Terms of reference and scope of the work of this sub-group
Pollutants addressed and General guidelines
Meetings schedule
Table of candidate methods
Definitions/ Abbreviations
Open questions in the GTR Draft document
Conclusions and next steps; documents loaded in CIRCA Database
WLTP-DTP-AP,
O. Mörsch / C. Astorga
Notes: <number>

## Slide 7
Possible reference methods have been identified. Possible source of text has been added where possible.
Performance criteria
Gathering of performance data for candidate methods has been tasked within group.
Based on the Range of emission level to be measured performance criteria (LoD, LoQ, rise time and max. interference) have been derived.
A table of candidate methods to be evaluated has been set up.

## Slide 8
Table of candidate methods for additional pollutants
WLTP-DTP-AP, Ol. Mörsch
C. Astorga
Notes: <number>
CDL: Chemiluminiscence Detector for NO2
QCL: Quantum Cascade Tunable Infrared Laser Differential Absorption Spectrometer (QC-TILDAS) for Measurements of Atmospheric Ammonia
LDS: Laser Diode (in situ and tunable); Ammonia slip lost or fall
NDIR non dispersive infra red

## Slide 9
WLTP-DTP-AP, Mörsch/Astorga
  Linearization:
  application of a range of concentrations or materials including zero to establish the mathematical relationship between concentration and system response
  Linearization check:
  application of a range of concentrations or materials including zero to
  verify the mathematical relationship between concentration and
  system response
  Calibration:
  zero, span adjustment with calibration gases or calibration materials
  Verification:
  zero, span check with calibration gases or calibration materials, no adjustment
Definitions:
Notes: <number>

## Slide 10
WLTP-DTP-AP, Mörsch/Astorga
Abbreviations/Definitions:
RCHO Formaldehyde plus Acetaldehyde
HCHO Formaldehyde
CH3CHO Acetaldehyde
EtOH Ethanol
THC Total Hydrocarbons (All compounds measurable by FID)
NMOG Non-methane organic gases (NMHC plus EtOH and RCHO)
NMHC Non-methane hydrocarbons (THC excluding CH4 and EtOH, response factors are applied)
NOx Oxides of nitrogen
NO Nitric oxide
NO2 Nitrogen dioxide
N2O Nitrous oxide
NH3 Ammonia
Notes: <number>

## Slide 11
WLTP-DTP-AP, Mörsch/Astorga
Handling of lost sample in raw exhaust sample
 Proposal:
Limit sample flow (10 l/min) and return sample (no drying, heated or diluted return)
or (at manufacturers request)
Additional cycle
Linearization of in situ instruments  According to instrument manufacturer at least once a year
Verification of in situ instruments  within 24 h at concentration of standard
FTIR: linearization  after manufacture and after major analyzer repair
FTIR: Verification  within 24 h
Open Issues - resolved
Notes: <number>

## Slide 12
WLTP-DTP-AP, Mörsch/Astorga
Allow calculation of NOx from NO + NO2  no
Allow QCL and other technologies for NO
and NO2 from modal dilute  yes
Calibration/verification of CLD for NO-Mode  to be done separately
linearization of CLD for NO-Mode  can be taken over from NOx
Applicability of ETOH and aldehyde
measurement  E21+
Open Issues - resolved
Notes: <number>

## Slide 13
WLTP-DTP-AP, Mörsch/Astorga
NH3 sampling during engine off
Temperature for NH3 sampling (110 – 190?°C)
proposal:  set-point between 110 °C and 190 °C with range of +/- 10 K
 JAMA position: between 110 °C and 133 °C due to decomposition of urea
Traceability to national standards of calibration gas for AP
 DTP  gas industry  difficulties for NH3, EtOH to be expected, achievable accuracy/stability has to be established
Open Issues
Notes: <number>

## Slide 14
WLTP-DTP-AP, Mörsch/Astorga
Continue drafting of GTR [*] in small groups (as well as OIL):
Tasks have been assigned within group and the outcome
will be delivered for the next meeting
Next face-to-face workshop: (……)
Additional Tel/web conferences
Next Steps
[*] Draft GTR proposal: WLTP-DTP-LabProcICE-061
Notes: <number>

## Slide 15
Additional pollutants contact persons:
WLTP-DTP-AP, Mörsch/Astorga
Chair: Daimler-Stuttgart
oliver.moersch@daimler.com
Co-chair: EC-DG JRC Institute for ENERGY
covadonga.astorga-llorens@jrc.ec.europa.eu
Notes: <number>

## Slide 16
Ref.: CIRCA documents WLTP-DTP-AP
Draft GTR proposal:
WLTP-DTP-LabProcICE-061
THANKS FOR YOUR ATTENCION
C. Astorga
covadonga.astorga-llorens@jrc.ec.europa.eu
http://ies.jrc.cec.eu.int
http://ie.jrc.cec.eu.int/Units/
WLTP-DTP-AP,
O. Mörsch / C. Astorga
& open questions:
WLTP-DTP-AP-07-02 Open Issues May 2011
Notes: <number>

## Slide 17
WLTP-DTP-AP, Mörsch/Astorga