## Slide 1: Geneva, June 2011
Effect of ambient temperature (15 °C÷28 °C) on CO2 emissions from LDV over NEDC
Alessandro.Marotta@jrc.ec.europa.eu

## Slide 2
Vehicle test matrix

## Slide 3
Test conditions
Ambient temperature
Vehicle coast down data
Chassis Dyno settings
Which is the best way to deal with these three changing parameters?

## Slide 4
CAT
Resistance to progress
Internal Friction Dyno
CAT
Internal Friction Dyno
Fcorr
Traction F
A) ROAD
C) OUTPUT: DYNO SPECIFIC LOADS WHICH HAVE BEEN CALCULATED TAKING INTO ACCOUNT THE INTERNAL FRICTION OF THE BENCH
B) CHASSIS DYNO: ON-ROAD RESISTANCE TO PROGRESS TO BE SIMULATED
INPUT: ROAD COAST DOWN DATA
Traction F
Ftrazione
Resistance to progress
=
Typical dyno load setting procedure
Coast down times measured on-road are input in the chassis dyno software
The chassis dyno starts an automatic iterative procedure to match the on-road coast down times
After several trials, when the tolerance criteria are met, the software provides corrected dyno loads taking into account the internal dyno friction

## Slide 5
Test conditions
A theoretically correct approach to carry out these tests would require to take into account the effect of T on:
    Vehicle coast down data
    Internal friction of the CD
    ……
For each Temperature of the test, the relevant coast down parameters should be input and the chassis dyno should be allowed to adjust its settings taking into account internal friction.

## Slide 6
Test conditions
If the vehicle coast down data at different temperatures are not available, a pragmatic approach is to carry out the tests (between 15 °C and 28 °C) keeping constant the CD settings used at 22 °C.
A test at 15 °C will thus be characterized by a slightly higher resistance to progress than at 22 °C (due to the increased internal friction of the CD), which in part compensates for the lower coast down times of the vehicle at 15 °C compared to 22 °C.
At 25 °C there is the opposite effect.

## Slide 7
Experimental results
Results are presented as % change of CO2 emissions at 15/25/28 °C over CO2 emissions at 22 °C.
Points on the diagrams represent the ratio between the single test value at 15/25/28 °C and the average CO2 emissions at 22 °C for the same vehicle.

## Slide 14
Discussion
Based on the experimental measurements carried out at JRC (CD settings unchanged), an average correlation of CO2 emissions with T over the NEDC could be proposed.
It should be kept in mind that JRC test results cannot be directly compared to other similar studies due to the different test protocol adopted.
However, a correlation very similar to the one obtained by JRC is being discussed at EU level for the “eco-innovations” that provide engine heat storage during parking times.

## Slide 15
CONCLUSIONS
JRC has carried out a limited test campaign using the most pragmatic approach that was possible in the light of the data and time available.
A correlation between CO2 emissions and ambient Temperature has been detected and seems in line with the findings of the eco-innovations working group.
A more accurate quantification of the CO2/T correlation would require more complex test campaigns and an agreed test protocol.
In the light of all above considerations, it would be preferable to select a test Temperature for the WLTP as close as possible to 20 °C.

## Slide 17
Test conditions

## Slide 18
If we want to correct for the internal friction of the CD ( ex. ~4.0%)
Test conditions

## Slide 19
If we want to correct for the internal friction of the CD ( ex. ~4.0%)
Then we should also correct for the actual vehicle cost-down times at 15 °C (air density at 15 °C/ air density at 22 °C = 1.024)
Test conditions