## Slide 1
slide <number>
Progress Report
DTP Subgroup
Lab Process Internal Combustion Engines
(LabProcICE)
Bern, 13.09.2011
Notes: <number>

## Slide 2
slide <number>
State of the working progress
2) LabProcICE issues on DTP level
3) Work in progress items / proposals / open issues
4) Parameter setting LabProcICE for validation 2
5) Next steps
Overview

## Slide 3
slide <number>
several dates Draft working team meetings
30. – 31.8.2011 Brussels workshop
1.1) Meetings since June DTP 6

## Slide 4
slide <number>
Open issues list
has been updated (LabProcICE-090)
GTR draft
has been updated, incl. Subgroup AP (LabProcICE-089)
Definitions
- overview definition term list (LabProcICE-049)
detailed definition list (LabProcICE-050)
 Review postponed
1.2) OIL, gtr draft, definitions

## Slide 5
slide <number>
State of the working progress
2) LabProcICE issues on DTP level
3) Work in progress items / proposals / open issues
4) Parameter setting LabProcICE for Validation 2
5) Next steps
Overview

## Slide 6
slide <number>
Inertia classes
Objectives:
grouping of vehicles with similar behavior but certain differences in weight to a class for testing.
the class extension should be small enough for sufficient distinction of different characteristics (e. g. CO2 emissions), but large enough for an effective type approval process.
(1) LabProcICE proposal: discrete inertia steps of 60 kg
Impact of 60 kg inertia steps on CO2 : 1,3 to 2,7 g/km CO2 (dependent of vehicle efficiency & test cycle, but independent of vehicle weight). This assessment was supported by ICCT at DTP6 meeting
(2) Updated ICCT proposal (LabProcICE-091):
step-less approach or reduced inertia steps of 28.35 kg

## Slide 7
slide <number>
Open issues connected to inertia classes:
Vehicle weight (definition vehicle test mass)
NL proposal (DTP-06-12, updated proposal) - JAP proposal (LabProcICE-084)
LabProcICE supports that reference weight should not be related to maximum laden mass
family concepts (gtr and/or regional)

## Slide 8
slide <number>
Test room and soak area temperature
LabProcICE: setpoint of target value 298 K, tolerance of actual value ± 5K
 harmonisation with gtr 2 & 4, improved reproducibility
Concern by EU: not representative, tolerance too high
Impact on CO2 results shown at DTP6:
UBA / TUEV study (LabProcICE-038)  significant influence of soak temperature (22 / 28 °C) on emission results (Ǿ 3 - 5%)
UTAC study (LabProcICE-070)  CO2 impact is cycle dependent (FTP < NEDC)  no significant CO2 impact of lower lab temperature (25 -> 22°C)  significant impact of 15 °C, but cost-effectiveness questionable
studies of JRC (DTP-06-13) supported UTAC results, but different interpretation
Decision of DTP is pending  setpoint decision for validation 2 necessary!

## Slide 9
slide <number>
Method for subtraction of pollutant mass in intake air
(LabProcICE-020)
Aim: measure low pollutant mass with higher accuracy by considering the pollutant level that is contained in the combustion and intake air of the vehicle
Concerns by US EPA / Japan:
- increased complexity, without clear benefit
- impact on emission result  in conflict to current stringency of limit values
- conflict with US definition of exhaust emissions
Proposal for further steps:
This issue is put on hold until results of validation and correlation shows the clear need and effect of the proposed method. Then the subgroup will revise the proposal and prepare for decision of the contracting parties.

## Slide 10
slide <number>
State of the working progress
2) LabProcICE issues on DTP level
3) Work in progress items / proposals / open issues
4) Parameter setting LabProcICE for Validation 2
5) Next steps
Overview

## Slide 11
slide <number>
  RLD - Tyre Selection Criteria
  Based on UK proposal (LabProcICE-064):
  selection based on 6 rolling resistances classes the tyres offered by the manufacturer on the production vehicle are belonging to.
  RR measured acc. to ECE-R117.
  Tyres in the worst rolling resistance classes shall be chosen for road load determination. If tyres from more than three rolling resistance classes are specified for the vehicle, tyres from the second worst rolling resistance class shall be chosen.
  CO2 impact? Re-definition of classes necessary?
   ACEA input/proposal expected

## Slide 12
slide <number>
RLD - vehicle selection criteria
General approach for WLTP:
 Measure representative vehicle in a representative test
 Precondition: proper definition & verification of representativity
Aim for vehicle selection:
 Test a vehicle representative for future market
 LabProcICE (T&E-) proposal: Vehicle selection based on expected sales volume

## Slide 13
slide <number>
draft proposal:
The exterior of the coast down test vehicle shall be representative for the average vehicle expected to be sold to the market. This is assured as follows:
- For vehicles sold with optional body parts which influence the aerodynamics (e.g. roof railings, spoilers etc.), every option shall be installed unless it can be made plausible that less than 50% of the customers will choose this option.
- For vehicles sold in different design trims upon selection of the customer (e.g. standard, luxury or sport trim), the trim that is expected to obtain the highest market share shall be installed.
- For the selected tyre the wheel rims with the highest estimated market share shall be used.
The manufacturer’s selection of trim and options should be substantiated by marketing figures and -if applicable- sales numbers of the predecessor vehicle model.

## Slide 14
slide <number>
(a) Sales volume based approach
 Aerodynamic options and trim are fitted if they exceed 50% of the sales volume
 Representativity should be ensured by expected sales numbers
Disadvantages:
- Different interpretation by manufacturers
- Different interpretation by Type Approval Authority
No means of verification before or after

## Slide 15
slide <number>
(b) Worst case criteria - proposal by Japan, LabProcICE-082
Japanese concern:
change in sales fraction may lead to specification change without vehicle design change, e. g. in conflict with tax incentive systems?
Without sufficient definition/verification worst case is the only alternative
 For vehicle family with large variations in aerodynamic options/trims manufacturer may decide to split to be more representative
Disadvantages:
Not representative / increased type approval burden to ensure representativity
(c) certification issue?

## Slide 16
slide <number>
RLD – vehicle coast down mode
Definition (adopted):
Vehicle coast down mode means a special mode of operation for which drivetrain components are mechanically and/or electrically decoupled from the wheels for the purpose of an accurate road load determination.
Requirement is still to be reviewed – Questions:
The vehicle coast down mode is mandatory or not and in which cases? What are the criteria?
Further Steps:
Evaluate technical needs and effects together with subgroup EV considering new techniques
Revise criteria for application of coast down mode

## Slide 17
slide <number>
LabProc - Monitoring of Battery SoC
The energy content of all batteries has to be considered for determination of CO2 and energy consumption in the test cycle.
Agreed by DTP6:
conditioning test cycle before emission testing with fully charged battery
+ battery shall not be charged again before the official testing.
Proposals (based on LabProcICE-056rev2 /-081):
- approach based on method in R101 for not external chargeable hybrid-
electric vehicles
- Monitoring of energy difference during test
- Comparison with energy of consumed fuel during test
- Correction of CO2 value if energy difference exceeds certain threshold

## Slide 18
slide <number>
Open issues:
Threshold criteria: 1% (TUEV Nord) or 2% (ACEA)?
What is feasible? Cost/benefit ratio? Tolerances of Ammeter?
Further data to be provided e.g. by validation phase 2 measurements

## Slide 19
slide <number>
LabProc - Multimode gear boxes / GSI
Definition: Mode means a distinct way to operate a vehicle which can be chosen by the driver (e.g. automatic mode, manual mode)
GSI  not considered as a mode of a multimode gearbox (latest EU regulation)  certification issue
Emissions testing proposal: Compliance with emissions standards in all modes  Test agreed worst case (reservation by NL : test all modes)
CO2 / FE testing proposal:
Single default mode  test default mode
No default mode or multi default modes  test agreed best and worst case modes, average results of both modes (reservations by NL & Japan: test & average all modes)
Japanese proposal incl. special provisions for semi-AT see LabProcICE-083
DTP decision needed until start of correlation!

## Slide 20
slide <number>
LabProc - preconditioning cycle
Basic policy with precon design objectives for lab procedure and measurement equipment was established
 a proposal will be develop based on these objectives and DHC outcome
LabProc - definition of modes
DHC proposal needs to be coordinated with DTP to ensure compliance with lab procedures

## Slide 21
slide <number>
State of the working progress
2) LabProcICE issues on DTP level
3) Work in progress items / proposals / open issues
4) Parameter setting LabProcICE for Validation 2
5) Next steps
Overview

## Slide 22
slide <number>
List of required setpoints and relevant tolerances
 WLTP-DTP-07-03
3) LabProcICE parameter setting for validation 2

## Slide 23
slide <number>
State of the working progress
2) LabProcICE issues on DTP level
3) Work in progress items / proposals / open issues
4) Parameter setting LabProcICE for Validation 2
5) Next steps
Overview

## Slide 24
slide <number>
Small teams (LabProc, ME, RLD) will continue work on draft gtr / OIL / definitions
Next face-to-face workshop: planned in November 2011
Additional Tel/web conferences
Evaluation of new test procedure during Validation Phase 2

## Slide 25
slide <number>
Thanks for your attention.
LabProcICE contact:
Béatrice Lopez de Rodas - beatrice.lopez(at)utac.com
Konrad Kolesa - konrad.kolesa(at)audi.de
Stephan Redmann – stephan.redmann(at)bmvbs.bund.de