## Slide 1: WLTP DTP PM-PN Subgroup Activities, Progress & Future Plans
7th DTP Meeting
Bern
12th – 14th September 2011
Chris Parkin

## Slide 2: Outline
      Meetings
      Closed Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 3: Outline
      Meetings
      Closed Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 4: Subgroup Meeting
10th Meeting – 8th July
  The following Open Issues were reviewed;
    Dilution air background correction,
    Filter media specification,
    Filter conditioning,
    PM Microbalance precision,
    Reference filter weighing,
    PM calculations,
    PN during regeneration investigative measurements,
    VPR minimum penetration efficiency
    PNC calibration frequency
    PNC calibration aerosol

## Slide 5: Subgroup Meeting
  The draft GTR text was reviewed. Updated text reflecting status following the meeting was circulated as document PMPN-10-08 (and now rev.1).

## Slide 6: Outline
      Meetings
      Closed Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 7: Closed Issues
PM Sampling
A9 Dilution air background correction: Dilution air background correction should be made on the basis of a rolling average background measurement. This contrasts with tunnel background correction where the background measured on day of test, following any tunnel pre-conditioning, should be applied.
A38 Filter media: References for filter media collection efficiency measurement have been added
PM weighing
B2 Microbalance precision: 1g as per GTR 4 agreed
B6 Reference filter weighing: Reg 83 provisions on maximum time between sample and reference filter weighing (8 hours) and reference filter weighing acceptance criteria. These are more demanding than GTR 4 provisions.

## Slide 8: Issues for Further Work Following 10th Meeting
A38 Filter Media specification: Chairman to seek clarification of flow rate for filter efficiency check
B7 PM Calculation: PM small group to provide updated/corrected text and equations
C1 Regeneration Experimental Measurements: ACEA and JRC to discuss scope of experimental measurements
D4 PNC calibration frequency: TSI to provide text implementing 13 month interval with a requirement to either monitor PNC counting efficiency versus a reference or change PNC wick every 6 months
D5 PNC calibration aerosol: clarify whether D50 requirements should be met before or after k factor is applied

## Slide 9: Closed subject to review e.g. due to Validation 2 or DHC conclusions
B3 Filter conditioning: minimum of 1 hour conditioning time, unless validation experience suggests longer is necessary
D1 VPR solid particle penetration efficiency: 70% minimum penetration requirement at 100nm to supplement existing 50:100nm and 30:100nm pcrf ratio requirements, subject to review based on data from PMP VPR Round Robin

## Slide 10: Outline
      Meetings
      Closed Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 11: Data To Gather During Validation 2
Experience on PN during DPF regeneration;
  To confirm PN measurement system is capable of excluding worst case volatile material during DPF regenerations
  CVS and filter face temperatures during regenerations?
Dilution tunnel pre-conditioning and background
  Is 20 minutes pre-conditioning at 120kph sufficient?
  Tunnel PN background levels
PM filter conditioning
  Minimum conditioning time required

## Slide 12: PN During Regeneration
Experiments to be conducted during Validation 2 to investigate feasibility of specifying PN measurement during regen
Vehicles
  Will need regen indicator and inhibitor switch
Measure PN before, during and after regeneration
Different PN measurement systems
  Two systems per lab sampling in parallel
Impact of VPR pcrf
  Test over range from 100-3000 (one system at high, one at low setting each test)
Two tests at each pcrf setting
Impact of CVS dilution on nucleation mode particles
  Test at max and min CVS dilution
DPF fill procedure
  Either fast loading on engine dyno or on vehicle loading
  Follow R83 advice on fill state stabilisation for pre-regen tests
VPR sulphate removal capability
  Test with highest sulphur lube oil permitted by OEM and fuel at maximum (10/15mg/kg) sulphur limit

## Slide 13: Outline
      Meetings
      Closed Issues
      Open Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 14: Amendments to GTR Text
Document: WLTP-DTP-PMPN-10-08 rev.1 changes since 09-06 rev.3 are;
List of Symbols & Acronyms - updated to reflect latest changes
PM & PN dilution air background –dilution air background measurements should be based on 20 day rolling average measurements. Maximum permissible corrections (in g/m3 or #/m3) should be equivalent to 1mg/km or 2x109 #/km at flow rate of test
PM & PN dilution tunnel background – dilution tunnel background measurements must be made on day of test following any tunnel pre-conditioning. Maximum permissible correction of 1mg/km and 2x109 #/km. Tunnel background measurements must be on day of test after any tunnel pre-conditioning
PNC Monitoring – requirement to monitor PNC counting efficiency v reference PNC or >2 measurement PNCs added. Alternatively PNC wick may be changed every 6 months
PM Calculation – parameter names and subscripts aligned with GTR 4
PM Temperature control – clarified that components may be heated to achieve <52°C sample temperature

## Slide 15: Amendments to GTR Text
PM sample probe – minimum internal diameter reduced to 8mm in line with GTR 4
PM sampling Particle Transfer Tube – minimum bend radius of 100mm added
PM Secondary dilution requirements – secondary air HEPA filtered, injected into transfer tube as close to sample extraction as possible, 0.25-5 seconds residence time from point of secondary air injection to filter face, proportionality of sample flow must be maintained, returned flow should not interfere with other samples. PM sampling diagrams updated
PM filter spec – test procedure reference and test aerosol added, filter face velocity clarified
PN Sampling diagram – corrected to show LEPA filter in correct place

## Slide 16: Outline
      Meetings
      Closed Issues
      Open Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 17: Future Plans
  Confirm latest changes to GTR text
  Commence updating PN calibration guidance documents
  Review data from Validation 2 on;
    tunnel background,
    tunnel pre-conditioning,
    Minimum filter conditioning time,
    Measurement of PN during regeneration
  Review data from PMP VPR Round Robin on;
    Repeatability of VPR solid particle penetration measurement and implications for VPR solid particle penetration efficiency specification

## Slide 18: Outline
      Meetings
      Closed Issues
      Data To Gather During Validation 2
      Amendments to GTR Text
      Future Plans
      Administrative Issues

## Slide 19: Administrative Issues
Next meeting scheduled for 23rd September
Following this meeting Chairmanship will be taken over by Caro Hosier, Ford Motor Company
Co-chairmanship to be confirmed at next meeting