| Submitted by the expert from OICA (as adopted by GRSG) | Informal document GRSG-101-02-Rev.1 (101st GRSG, 18-21 October 2011 agenda item 10) |
| --- | --- |

Proposal for changes to Regulation No. 121 (Identification of controls, tell-tales and indicators)

Changes to the current text of the Regulation are indicated in bold characters.

I.	Proposal

Paragraph 4.2., amend the words “at present 00 for the Regulation in its original form” to read “at present 01 corresponding to the 01 series of amendments to the Regulation”.

Add a new paragraph 12., to read:

“12.	Transitional provisions

12.1.	As from the official date of entry into force of the 01 Series of amendment to this Regulation, no Contracting Party applying this Regulation shall refuse national or regional type approval of a vehicle type approved to the 01 Series of amendment to this Regulation.

12.2.	Contracting Parties applying this Regulation shall not refuse to grant extensions of approval according to the preceding series of amendments to this Regulation.

12.3.	Until 24 months after the date of entry into force of the 01 Series of amendment to this Regulation, no Contracting Party applying this Regulation shall refuse national or regional type approval of a vehicle type approved to the preceding series of amendments to this Regulation.”

Table 1, amend to read:

| No. | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | ITEM | SYMBOL 2/ | FUNCTION | ILLUMINATION | COLOUR |
| … | … | … | … | … | … |
| 43. | Electronic stability control (including malfunction) | or ESC 17/ | Tell-tale | Yes | see Regs 13-H and 13 as appropriate Yellow |
| 44. | Electronic stability control system “OFF” | or ESC OFF 17/ 20/ | Control | Yes |  |
|  |  |  | Tell-tale | Yes | Yellow |

Footnote 17/, for reference (remains unchanged):

“17/	The vehicle outline shown is not intended to be restrictive, but is the recommended outline. Alternative vehicle outlines may be used in order to better represent the actual outline of a given vehicle.”

Add a new footnote 20/, to read:

“20/	The supplementary letters "OFF" may be positioned on or adjacent to the outline of the symbol of item No. 43. The font of the letters ‘OFF’ or ‘ESC OFF’ is not intended to be restrictive.”

Annex 2, approval mark models A and B, amend to read:

“Model A

(See paragraph 4.4. of this Regulation)

a = 8 mm min.

The above approval mark affixed to a vehicle shows that the vehicle type concerned has, with regard to the location and identification of hand controls, tell-tales and indicators, been approved in the Netherlands (E4) pursuant to Regulation No. 121 under the approval No. 011234.  The first two digits (01) of the approval number indicated that the approval was granted in accordance with the requirements of Regulation No. 121 as amended by the 01 series of amendments.

Model B

(See paragraph 4.5. of this Regulation)

a = 8 mm min.

The above approval mark affixed to a vehicle shows that the vehicle type concerned has been approved in the Netherlands (E4) pursuant to Regulation No. 121 and Regulation No. 331. The approval number indicates that, at the dates when the respective approvals were granted in accordance with Regulation No. 121 as amended by the 01 series of amendments and with Regulation No. 33 which was still in its original form.

_______________

1	The number is given merely as an example.”