## Slide 1: CRS internal measurement checking gauge
Annex 19
Erik Salters,
Dorel
Safety Research Department
CRS-23-03

## Slide 2: EN1888 device
Origin not clear, EN1888 secretary does not know. Not intended to represent <1 yr old children.
Mass is 9 kg, so too heavy for children with a stature smaller then ~600 mm.
Width is 200mm, so too wide for children with a stature smaller then ~750 mm
Chosen to design our own device.

## Slide 3: Input
Where possible, body parts were made adjustable to represent children with a stature from 400-1500 mm
Where not possible, Q1,5 was used as reference (e.g. hip joint location)
  Upr arm ball diameter 44 mm
  Shoulder rotation point from backrest 50 mm
  Hip joint height from seating plane 36 mm
  Hip joint distance from backrest 60 mm
  Buttock radius 45 mm
  Thigh thickness 60 mm
50 N spring force in hip and shoulder cups.

## Slide 4
Backrest length
Shoulder width
Hip Width

## Slide 5: Hip width device
Top view
Isometric view with shell

## Slide 6: Shoulder width device
Top view
Isometric view with shell

## Slide 7
Isometric view
with half CRS shell

## Slide 8: Ranges 400-1500 mm (0 to ~12yrs)
Backrest height 400-800 mm
Shoulder breadth 120-400 mm
Hip breadth 150-400 mm
Shoulder height 250-550 mm

## Slide 9: Open issues
Naked dummy; 5 mm compensation for clothing proposes (all directions).
Verification of shoulder height is OK; belt length check is not required.
Non sizable measures, might need adjustment for Q0 sized child
  Leg diameter
  Shoulder backrest distance
  Diameter of hip + shoulder cups
Is it really a problem? Legs are only a few mm’s too thick, shoulder a few mm’s too far from backrest. to represent a newborn.
Hip + shoulder Ø are equal in Q dummies (realistic?)