## Slide 1: FIMCAR Global Strategy
GRSP IG FI 20101014
FI-10-06

## Slide 2: Global Strategies for FIMCAR
Proposed Working plan
Define compatibility characteristics based on accident analysis
Develop assessment procedures
Establish criteria for rating the assessment procedures
Select final procedure and finalise test protocol

## Slide 3: List of Open Issues From WG 15
Global Issues
  Further accident analysis and benefit analysis to update information on changing vehicle fleet
Status in FIMCAR
in-depth analysis completed, information from GRSP available, benefit analysis to start later in project

## Slide 4: List of Open Issues From WG 15
Global Issues
2. Finalise the test severity (EES) for regulation test.
Status in FIMCAR
2. Test severity should not reduce compartment strength – need to define mass effect (more details later)

## Slide 5: List of Open Issues From WG 15
Global Issues
3. Finalise assessment criteria for regulation test.
Status in FIMCAR
3. Assessment Criteria under development

## Slide 6: List of Open Issues From WG 15
Global Issues
4. Finalise objective assessment proce-dures to analyse results of car-to-car tests
Status in FIMCAR
4. Test database complete as a tool, work on the analysis of car-to-car tests is planned

## Slide 7: List of Open Issues From WG 15
Global Issues
5. Identify critical injury mechanisms (in particular relevance of thorax injuries in high deceleration pulse type accidents)
Status in FIMCAR
Accident analysis highlighted thorax as most common AIS 2+ injury Input from THORAX project expected for the injury mechanism

## Slide 8: List of Open Issues From WG 15
Global Issues
6. Finalise a compatibi-lity scale for a rating system.
Status in FIMCAR
6. Not first priority within FIMCAR

## Slide 9: Global Priorities from FIMCAR and Previous Work
 | Assessment requirements |  |  |  |  |  |  | 
 | Structural Interaction |  | Front End Force / Deformation (Consisting of) |  | Compartment integrity |  | Restraint system | 
 | Alignment | Load spreading (load paths / connections) | Deformation forces of frontal structures | Energy absorption management | Sufficient for single vehicle accident | Enhanced for light vehicles in vehicle to vehicle accident | (Assess over range of pulses) | Test restraint capacity
Priorities for FIMCAR | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 1
Strong Evidence in the existing and previous studies
Acceleration injuries need to be addressed, small car issues hard to identify in current data
Current R94 / EuroNCAP gains must be maintained accident data needs further analysis for car-car
Acceleration injuries need to be addressed, expand test types to test sensing systems

## Slide 10: How Frontal Impact and Compatibility Priorities are being addressed in FIMCAR
No. | Assessment requirements |  |  |  |  |  |  | 
 | Structural Interaction |  | Front End Force / Deformation (Consisting of) |  | Compartment integrity |  | Restraint system | 
 | Alignment | Load spreading (load paths / connections) | Deformation forces of frontal structures | Energy absorption management | Sufficient for single vehicle accident | Enhanced for light vehicles in vehicle to vehicle accident | (Assess over range of pulses) | Test restraint capacity
FWRB |  |  |  |  |  |  |  | 
FWDB |  |  |  |  |  |  |  | 
ODB |  |  |  |  |  |  |  | 
PDB |  |  |  |  |  |  |  | 
MDB (fixed mass/speed) |  |  |  |  |  |  |  | 
MDB (variable mass/speed) |  |  |  |  |  |  |  | 
FIMCAR has high priority on establishing structural interaction assessments using both a FW and Offset test – Choice of barrier types under investigation

## Slide 11: How Frontal Impact and Compatibility Priorities are being addressed in FIMCAR
No. | Assessment requirements |  |  |  |  |  |  | 
 | Structural Interaction |  | Front End Force / Deformation (Consisting of) |  | Compartment integrity |  | Restraint system | 
 | Alignment | Load spreading (load paths / connections) | Deformation forces of frontal structures | Energy absorption management | Sufficient for single vehicle accident | Enhanced for light vehicles in vehicle to vehicle accident | (Assess over range of pulses) | Test restraint capacity
FWRB |  |  |  |  |  |  |  | 
FWDB |  |  |  |  |  |  |  | 
ODB |  |  |  |  |  |  |  | 
PDB |  |  |  |  |  |  |  | 
MDB (fixed mass/speed) |  |  |  |  |  |  |  | 
MDB (variable mass/speed) |  |  |  |  |  |  |  | 
Vehicles must have minimum energy absorption requirements, likely resolved with FW test.
Force level issues rated as priority 2 and are unlikely to be resolved.

## Slide 12: How Frontal Impact and Compatibility Priorities are being addressed in FIMCAR
No. | Assessment requirements |  |  |  |  |  |  | 
 | Structural Interaction |  | Front End Force / Deformation (Consisting of) |  | Compartment integrity |  | Restraint system | 
 | Alignment | Load spreading (load paths / connections) | Deformation forces of frontal structures | Energy absorption management | Sufficient for single vehicle accident | Enhanced for light vehicles in vehicle to vehicle accident | (Assess over range of pulses) | Test restraint capacity
FWRB |  |  |  |  |  |  |  | 
FWDB |  |  |  |  |  |  |  | 
ODB |  |  |  |  |  |  |  | 
PDB |  |  |  |  |  |  |  | 
MDB (fixed mass/speed) |  |  |  |  |  |  |  | 
MDB (variable mass/speed) |  |  |  |  |  |  |  | 
FIMCAR will maintain an offset test with sufficient test severity as current levels.
Special actions for small vehicles are still being investigated by accident studies

## Slide 13: How Frontal Impact and Compatibility Priorities are being addressed in FIMCAR
No. | Assessment requirements |  |  |  |  |  |  | 
 | Structural Interaction |  | Front End Force / Deformation (Consisting of) |  | Compartment integrity |  | Restraint system | 
 | Alignment | Load spreading (load paths / connections) | Deformation forces of frontal structures | Energy absorption management | Sufficient for single vehicle accident | Enhanced for light vehicles in vehicle to vehicle accident | (Assess over range of pulses) | Test restraint capacity
FWRB |  |  |  |  |  |  |  | 
FWDB |  |  |  |  |  |  |  | 
ODB |  |  |  |  |  |  |  | 
PDB |  |  |  |  |  |  |  | 
MDB (fixed mass/speed) |  |  |  |  |  |  |  | 
MDB (variable mass/speed) |  |  |  |  |  |  |  | 
Full Width test is proposed to assess restraint capacity and address acceleration injuries found in accident analysis
Combination of tests is advised for sensor and restraint performance evaluation

## Slide 14: Planned FIMCAR Results
Full Width test will be proposed
  In order to create a high deceleration pulse
  Use of deformable barrier to be determined
  Metric for structural alignment to be proposed
  Possible concept for frontal force level requirements
Offset Barrier test will be proposed
  In order to test compartment integrity
  PDB is only barrier being investigated for load spreading evaluation
  Existing ODB will be maintained if PDB cannot meet necessary performance requirements

## Slide 15: Planned FIMCAR Results
MDB will be developed with a PDB barrier face
  structural evaluation criteria will be tied to PDB research
  MDB barrier can address mass ratio compatibility issues which are probably not fully addressed in the fixed barrier tests
  MDB may replace or complement fixed offset barrier