## Slide 1: Priorities for the protection of children in cars: available data from the field
Philippe LESIRE
Heiko JOHANNSEN
Informal document GRSP-49-25
(49th GRSP, 16-20 May 2011,
agenda items 20)
Transmitted by the expert from France

## Slide 2: Priorities for children in cars
Introduction
Fatal accident analysis
  Casimir project
Representative real world data
  GIDAS
Observation data campaign
  CEDRE
  CASPER
Synthesis

## Slide 3: Children in cars - context
CARE database 2008 :
  Data for EU27 ( except Cyprus, Bulgaria, Lithuania)
  Children (0–11y) , car passengers
  340 killed, 2790 severely injured
The United Nations General Assembly:
  proclaimed “the period from 2011 to 2020 as the Decade of Action for Road Safety “
European Commission:
  proposed “to continue with the target of halving the overall number of road deaths in the European Union by 2020 starting from 2010 “

## Slide 4: Context - Europe
On-going research works
  EPOCh (Enabling Protection for Older Children)
    Objectives:
      Produce a 10/12 year old prototype dummy
      Extend the NPACS testing and rating protocols for older children
      Make proposals for Q10/12 dummy use in UN-ECE Regulation
  CASPER (Child Advanced Safety Project for European Roads)
    Objectives:
      Analysis of the reasons and consequences of the conditions of transportation of children both on scientific and sociological aspects.
      Improvement of the efficiency of child protection

## Slide 5: Context – Europe and others
New regulation – initiated in Jan08 - on going work
  Objectives:
The informal group shall consider the development of a new regulation for “Restraining devices for child occupants of power-driven vehicles” for consideration by GRSP.
A step by step approach shall be implemented
  Phase1: Develop definitions, performance criteria and test methods for ISOFIX Integral “Universal” CRS status : to be validated by GRSP.
  Phase2 – ISOFIX CRS non integral (Child is restraint by the adult safety belt) status : TOR to be agreed
  Phase3 – during phase2, discussions will take place in order to see if an additional phase is necessary to cover the other types of CRS.

## Slide 6: Fatal accident analysis
CASIMIR: (Child Accident Study Investigating Mortal Incident on the Road)
  French project, results published May 2010
  Analysis of police reports:
    child fatalities (<12 years) (all car accidents) in France in the period oct 2001 to sept 2003.
    sample size: 206 killed children out of 210
    France: In 2003, 2/3 of total number of children killed on the road were car occupants
  Distribution of fatalities per types of impact:
Impact type | Frontal | Side | Roll over | Rear | Others
children | 34% | 28% | 18% | 4% | 15%
All occupants | 45% | 32% | 13% | 2% | 7%

## Slide 7: Incorrectly restained children
Explanations
  Incorrectly restraining situation can be
    Inappropriate restraint system (e.g., adult belt only for children that should use a CRS)
    Wrong installation of CRS (e.g., wrong routing of vehicle belt) (called misuse) or not authorized seating position (active frontal airbag, floor resistance,...)
    Mistakes by restraining the child in the CRS (e.g., slack in harness system, seatbelt under the arm,...) (called misuse)

## Slide 8: Fatal accident analysis CASIMIR
Analysis
  Drivers: 80% are parents, 11% are close family
Total ejection rate
(all types of impact)
Maximum rate of correctly restrained children = 31%
(misuse is underestimated when based on accident reports analysis)
average: | 23%
not restrained | 49%
misuse (appropriate or not) | 35%
no misuse (inappropriate) | 10%
correctly restrained | 3%
Restraint use and misuse have a high influence killed children that have been ejected

## Slide 9: Fatal accident analysis CASIMIR
Main results per type of crash
  FRONTAL
    Not correctly restrained = 55% (including 32% not restrained at all)
    Crash severity over physiologic limits (EES>=75kph) = 25%
  SIDE IMPACT
    with intrusion (72% of side impact)
      57 % level of intrusion >=450mm at seating position
      19% not restrained
    Child not in the area of intrusion
      38% not restrained
  ROLL OVER
    76% not restrained – ejection is the main reason of death

## Slide 10: Representative real world data
GIDAS (German In Depth Accident Study)
  Data collection:
    Hannover , Dresden (and surrounding areas)
    2 shifts every day
    Minimum severity level guaranteed (at least one person injured)
    Representative of German accidents
    Approx. 1% of German accidents
  Sample
    Accidents between 1999 and 2008 (multiple impacts included)
    Children up to 12 YO as car occupants,
    accident against cars, objects or lorries

## Slide 11: Representative real world data GIDAS
Injury level per impact direction

## Slide 12: Representative real world data GIDAS
Note: The safety level guaranteed by the current regulation seems satisfying
for most of the accidents in frontal impacts
(which represents more than 80% of the accidents in frontal impact)
Injury level per delta-v in frontal impacts
5 MAIS3+ cases resulted from accidents out of the scope of car design or misuse.

## Slide 13: Observation data campaign
CEDRE ( Controle et Etude de Dispositifs de Retenue Enfant):
  Aim: getting a better understanding of
      the global situation of transportation of children in cars
      the main reasons of incorrect use (profiles of “mis-users”)
  419 children in France (177 vehicles - August 08 -July 09).
  Collaborative project:
    Insurances, industry, police, administration, hospital

## Slide 14: Observation data campaign CEDRE
Main results:
From interviews, it clearly appears that parents do not measure correctly the level of safety for their children (especially parents from new borns)
Influence of knowledge in child safety
Notes:   Information is necessary but not sufficient to ensure a high rate of correct use of restraint systems.
<number>

## Slide 15: Observation data campaign CEDRE
Main results
  Very few ISOFIX CRS (1%) although more than 45% cars are equipped with rigid anchorages
  Approximately 20% of drivers knew what ISOFIX is.
  Combination car equipped with rigid anchorages and drivers knowing what it means : 7% of the total sample!

## Slide 16: Observation data campaign
CASPER: Child Advanced Safety Project for European Roads
  36 months duration project co-funded by EC
    (FP7-SST-2007-RTD-1 - GA no.: 218564)
  15 partners (industry, research, universities) from 7 countries (D, E, F, I, NL, S,UK)
  Budget 5.5 M€
  Analysis of sociological aspects child safety in cars
  Questionnaires filled by parents (232 F, 176 E, 113 I)
  Aim to
    understand the reality of child environment as car passenger
    determine what are the social barriers, for drivers in charge of children transportation, to a correct use of CRS ?
    Cultural comparison using the same methodology and questionnaire

## Slide 17: Observation data campaign
CASPER: First sociological results
  France, Italy, and Spain:
    children are travelling almost everyday in cars
    According to parents:
      the main source of accident is other drivers : this is contradictory to CASIMIR results (a large majority drivers of the cars in which children were killed is responsible of the accident).
  France:
    29% of parents do not use an appropriate restraint system to transport their children.
    more than 40% of children with a weight lower than 9 kg are already using a FWD FC system

## Slide 18: Synthesis
Improve use and the quality of use is the priority
    CASIMIR, CEDRE, CASPER
Children are mostly safe
    GIDAS
Information campaigns and practice clinics dedicated to parents – sensibilisation
  CEDRE: Information is a useful and necessary step to limit misuse but not sufficient: misuse rate is still > 50% influencing parameter studied
  CEDRE and CASPER: About inappropriate use : reason is the switch of one system to another too early including the use of the seatbelt only
ISOFIX to be promoted
    CEDRE – low use of ISOFIX, very low knowledge of parents
    CASPER – To fix the CRS to the car, many parents feel/admit that they are not doing it correctly but are not able to tell what is wrong in their installation

## Slide 19: Synthesis
Frontal impacts, rear impacts and roll overs seem to be correctly covered by current regulation and do not seem do be an issue for most of the correctly restrained children.
    CASIMIR, GIDAS
Reduction of the impact severity in order to be in range where the car protects its occupants mainly for frontal and side impacts (mainly on near side)
    CASIMIR

## Slide 20: Thanks for your attention
philippe.lesire@lab-france.com
heiko.johannsen@tu-berlin.de