## Slide 1: Hydrogen Fueled Vehicle Global Technical Regulation (GTR) Subgroup Safety (SGS) Nha Nguyen 49th GRSP Session May 2011
<number>
Informal document GRSP-49-28
(49th GRSP, 16-20 May 2011,
agenda item 7)
Notes: <number>

## Slide 2: Overview
Background
Global Technical Regulation (GTR) goals and safety requirements
Hydrogen GTR Objectives
GTR Milestones and Timeline
GTR Details
<number>
Notes: <number>

## Slide 3: Background Hydrogen-Fueled Vehicle GTR
  The HFV GTR is co-sponsored by Japan, Germany and US; Germany as the overall ‘task manager’; US and Japan co-chair the meetings; US also acts as the Secretariat of the Sub-group on Hydrogen Safety (SGS)
  GTR Objectives:
  Attains equivalent levels of safety as those for conventional gasoline powered vehicles
  Performance based (not design specific) and traceability of requirements to on-road performance
  Data driven and science-based
  System/Whole vehicle-based
  Objectively measurable compliance
  2007 Action Plan: 2 phases of GTR development
<number>
Notes: <number>

## Slide 4: GTR Development Phases
In order to develop the GTR in the context of an evolving hydrogen technology, the trilateral group proposes to develop the GTR in two phases:
Phase 1: Establish a GTR for hydrogen-fueled vehicles based on a component level, subsystems, and whole vehicle crash test approach. For the crash testing, the GTR would specify that each contracting party will use its existing national crash tests but develop and agree on maximum allowable level of hydrogen leakage. The Japanese regulation, and any available research and test data will be used as a basis for the development of this first phase of the gtr.
Phase 2: Assess future technologies and harmonize crash tests. Amend the GTR to maintain its relevance with new findings based on new research and the state of the technology. Discuss how to harmonize crash test requirements for HFCV regarding whole vehicle crash testing for fuel system integrity.
<number>

## Slide 5: Milestones and Timeline
June 2007 - WP.29 approved GTR Action Plan - ECE/TRANS/WP.29/2007/41
11 Safety Subgroup meetings; next SGS 12th meeting is scheduled for the end of June 2011
May 2011 - draft GTR as informal document to the Group of Experts on Passive Safety (GRSP)
June 2011 – SGS-12 meeting
December 2011 - SGS will submit the draft GTR as ‘formal document’ to GRSP
March 2012 - If no objections or substantive changes, GRSP submits GTR as an informal document to WP.29/AC.3
June 2012 - If no objections or substantive changes, WP.29 votes on the GTR
<number>
Notes: <number>

## Slide 6: GTR Scope
This GTR applies to all hydrogen fueled vehicles of Category 1-1 and 1-2, with a gross vehicle mass (GVM) of 4,536 kilograms or less
  Compressed gaseous hydrogen system
  Liquefied hydrogen system
Motorcycles and buses are not covered and will be addressed in Phase II
<number>
Notes: <number>

## Slide 7: Compressed Gaseous Hydrogen System (CGHS) Requirements
  High pressure fuel container system
  Fuel system at vehicle level: in-use and post-crash hydrogen leakage limits
  Electrical integrity of high voltage system: in-use and post-crash
<number>
Notes: <number>

## Slide 8: Compressed Gaseous Hydrogen System Requirements
  High pressure fuel container system
  Verification Test for Performance Durability: sequential hydraulic cycling and static pressure tests
  Verification Test for Expected On-Road Performance: sequential pneumatic/hydraulic cycling tests
  Verification Test for Service Terminating Performance: fire test
  Label requirements: container and vehicle
Fuel system integrity
  In-use: fuel leakage mitigation
  post crash: maximum allowable leakage limit
Electrical Safety
  High voltage safety for in-use and post crash
<number>
Notes: <number>
The system-level performance tests in Part B were developed to demonstrate capability to perform critical functions throughout service including fueling/de-fueling and parking under extreme conditions, and performance in fires.
Performance test requirements for all compressed hydrogen storage systems in on-road vehicle service are specified in PART B 5.1. These criteria apply to qualification of storage systems for use in new vehicle production.

## Slide 9: Compressed Gaseous Container
<number>
Notes: Currently only Type 3 and type 4 containers are used for this application
<number>

## Slide 10
<number>
Verification Test for Performance Durability Sequential hydraulic cycling tests
Number of cycles is specified by the individual contracting party (from 5,500 to 11,000)
Proof pressure test
Drop (impact) test
Surface damage
Chemical exposure and ambient temperature pressure cycling tests
High temperature static pressure test
Extreme temperature pressure cycling
Residual proof pressure test (180% NWP-
4 min)
Residual strength burst test
180% NWP
(4 min)
Notes: The verification test for on-road performance durability ensures the system is fully capable of avoiding rupture under extreme conditions of usage that include extensive fueling frequency (perhaps associated with replacement of drivetrain components), physical damage and harsh environmental conditions.
Drop from handing; primary for aftermarket risk; fork lift. Test procedure requires drops from several angles.
Cut characteristic of wear form mounting straps
Such as handling, impact by road debris, chemicals from roads and vehicle (battery acid washer fluid; chemicals on or near roadways (fertilizer nitrate and lye) fluids used in fueling station (methanol and gasoline).
Residual strength burst test: within 20% of the initial burst pressure (Pb0)
<number>

## Slide 11
<number>
Verification Test for On-Road Performance
Sequential pneumatic/hydraulic cycling tests
Number of cycles: 500
Proof pressure test
Ambient and extreme temperature gas pressure cycling test (pneumatic)
Extreme temperature static gas pressure leak/permeation test (pneumatic)
Residual proof test (180% NWP – 4 min)
Residual strength burst test (hydraulic)
180% NWP
(4 min)
Notes: The verification test for expected on-road performance requires the demonstration of capability to perform essential safety functions under worst-case conditions of expected exposures.
Pneumatic testing with hydrogen gas provides stress factors associated with rapid interior pressure and temperature swings and infusion of hydrogen into materials; therefore, pneumatic testing is focused on the container interior and strongly linked to the initiation of leakage.
This test is important because it identifies the failure modes that would not be detected by the hydraulic tests.
In addition this will allow us to test for permeation of the container system.
There’s 500 cycles but normally, the leakage/failure would occurs within the first 50 cycles.
<number>

## Slide 12: Container Fire Test
<number>
3
8
600
o
C
800
o
C
Localized fire
Engulfing fire
minutes
10
TPRD
venting
Signifies a continuous temperature increase (need not be linear)
Region outside of localized impact
(1.65 m linear extent)
Region of
localized impact
Combined localized and engulfing fire
Notes: This is a combined fire test on a container: localized and engulfing fire
NHTSA and Transport Canada had jointly conducted a series of research: TC identified the need for localized fire test and developed the test procedures; NHTSA picked up the second phase of the research by conducting a series of test to identify the mitigation materials.
<number>

## Slide 13: Liquefied Hydrogen System
<number>
Notes: <number>

## Slide 14: Liquefied Hydrogen System
Verification of baseline metrics:
  Proof pressure test
  Baseline Initial Burst Pressure (hydraulic)
Verification of on-road performance:
  Boil-off test
  Permeation/Leak test
  Vacuum loss test
Fire test: Still under discussion to determine whether localized fire test is required
<number>
Notes: Boil-off test: During normal operation the boil-off management system shall limit the pressure below MAWP. The most critical condition for the boil-off management system is a parking period after a refueling to maximum filling level in a liquefied hydrogen storage system with a limited cool-down period of maximum 48 hours.
Vacuum loss test: This test is necessary to ensure that the PRD does not allow air to flow into the vacuum layer and creates high heat to the container. In order to prove the proper function of the pressure relief devices and the compliance with the allowed pressure limits of the liquefied hydrogen storage system, a sudden vacuum loss due to air inflow in the vacuum jacket is considered as the “worst case” failure condition.
<number>

## Slide 15: Fuel system integrity
In-use: fuel leakage mitigation and warning
  Fuel system safety requirements:
    Fueling port – to prevent back flow
    PRD release direction – to prevent H2 release into enclosed spaces and wheel wells
    Exhaust system – to prevent build up of H2 in the exhaust system
    Hydrogen leakage in enclosed compartments – No hydrogen can enter the passenger and trunk spaces. However, the vehicle will provide warning to the driver and activate shut off valves of the fuel cylinders if H2 concentration in air exceeding 4% in the semi enclosed or enclosed spaces of the vehicle
    Tell-tale: Shall be yellow in color if the detection system malfunctions ; and shall be red in compliance with hydrogen leakage in the enclosed spaces
<number>
Notes: <number>

## Slide 16: Fuel system integrity
Post crash: Contracting parties maintain their current crash test requirements and apply the following requirements for post crash
Maximum allowable leakage limit: average of 118NL per minute within 60 minutes after the crash
Controlled leakage into enclosed spaces: no built up of hydrogen concentration in air of more than 4% in the passenger or trunk/luggage compartments
Container Displacement: The storage container(s) shall remain attached to the vehicle at a minimum of one attachment point
<number>
Notes: <number>

## Slide 17: Electrical Safety
  Protection from direct and indirect contact from high voltage
In-use:
  Protection from direct contact: Protection of (1) IPXXD inside the passenger or luggage compartment and (2) IPXXB in other areas
  Electric isolation – 100 Ω/volt for DC and 500 Ω/volt for AC
    [for combined AC and DC buses: 100 Ω/volt providing (1) the electric system consists of double or more layers of solid insulators, (2) mechanically robust protections that have sufficient durability over vehicle service life such as motor housings, electronic converter cases or connectors]
  Electrical isolation monitoring – Currently applies only to fuel-cell vehicles
  Vehicle functional safety: “At least a momentary indication shall be given to the driver when the vehicle is in "active driving possible mode''
<number>
Notes: <number>

## Slide 18: Electrical Safety
Post-crash:
  Maximum voltage - 30 VAC and 60 VDC
  Resistance isolation - 100 Ω/volt for DC and 500 Ω/volt for AC
    For combined AC/DC buses: 100 Ω/volt providing AC bus meets the physical protection
  [Physical protection: protection of IPXXB] NHTSA is conducting safety risk study
  [Energy option at 2.0 Joules] inconsistent safety criteria with resistance isolation option.
  Electrolyte spillage: Maximum of 7% spillage in 30 minutes
  Battery and RESS retention: “RESS located inside the passenger compartment shall remain in the location... No part of any RESS that is located outside the passenger compartment for electric safety assessment shall enter the passenger compartment during or after the impact test.”
<number>
Notes: <number>

## Slide 19: Component Requirements
Component qualification requirements: PRD, shut-off valve and check valve
Fueling receptacle requirements: to provide proper fueling protocols, performance and location
Pressure regulator: The set pressure of the overpressure protection device shall be lower than or equal to the maximum allowable working pressure for the appropriate section of the hydrogen system
<number>
Notes: <number>

## Slide 20: Outstanding Issues
Some of the test procedures have not been validated
Liquefied hydrogen fuel system: limited experience; post crash and fire test requirements; limited available test data
Electric safety:
  [Post crash barrier option] – NHTSA research on safety risks
  Energy option – inconsistent criteria; optional requirement
Material compatibility (Hydrogen embrittlement): CP to decide. Complete in Phase 2
<number>
Notes: <number>

## Slide 21
<number>
Thank you
Notes: <number>