## Slide 1
Pedestrian Safety
Request For
Clarification Of Test Procedures
49th Session of UNECE GRSP,
Geneva, 16 – 20 May 2011
Informal document GRSP-49-31
(49th GRSP, 16-20 May 2011,
agenda items 4(c))

## Slide 2
Request For Clarification Of Test Procedures
CONTENT
Clarification Of Headform Test Procedure
Clarification Of Headform Test Area
Clarification Of Legform Test Procedure
Pedestrian Safety

## Slide 3
Clarification Of Headform Test Procedure
As pointed out in informal document GRSP-48-27, the headform test procedure as described in gtr No 9 is not fully clear
The headform test procedure is an interaction of three different points but just two points are clearly defined
During the discussion on gtr No 9, it was accepted that describing only 2 points may be sufficient
However, corrigendum 2 to gtr No 9 made inconsistencies more obvious despite the intention of this corrigendum is fully supported by OICA
OICA therefore suggests the following clarification of the headform test procedure
Pedestrian Safety

## Slide 4
Clarification Of Headform Test Procedure – Suggestion
A second drawing should be added to describe the three-dimensional interaction of the points
The three different points need to be clearly described
Pedestrian Safety
Drawing: gtr No. 9, part B, figure 6
Point B should read „measuring point“
C
B
Point C should be added
as „first contact point“
New, additional drawing:
Schematic front view
B: Measuring Point
C: First contact point
Existing drawing: Schematic side view

## Slide 5
Pedestrian Safety
In several cases, different terms are used to describe identical points
Therefore, it is proposed to add the following references, e.g. to the definitions:
  “Target point” A is also referred to as “aiming point”
  “Measuring point” B is also referred to as “selected impact point” or “test point”
  “First contact point” C is also referred to as “impact point”
However, clear and easy understandable definitions are wished for by OICA to avoid misunderstandings
Clarification Of Headform Test Procedure – Suggestion (2)

## Slide 6
Pedestrian Safety
Finally, a test result achieved during a test should be allocated to the respective “measuring point” and not to the “first contact point”
If accepted, the changes mentioned above should also be incorporated into the draft ECE Regulation
Clarification Of Headform Test Procedure – Suggestion (3)

## Slide 7
Advantages Of The Suggested Clarifications
Pedestrian Safety
During the gtr No 9 discussion, it was accepted that a “first contact point” always exists but:
realistic bonnet
curvature
First contact points
It is unclear how to position the headform in relation to this point
For very different impactor positions (as e.g. shown in the sketch) the first contact point could be nearly identical!
However, headform center of gravity clearly influences the behavior of the headform during and after the impact
Different HIC results can be possible
Using the measuring points, a clear allocation of the test result is possible
Measuring points

## Slide 8
Advantages Of The Suggested Clarifications (2)
Pedestrian Safety
There can be areas where a “measuring point” cannot be directly contacted, but:
Clear positioning of the headform nevertheless possible
Due to the headform’s center of gravity the headform will travel mainly in the intended direction
Even if the same “first contact point” will be hit the resulting HIC can differ
Areas that cannot be contacted may be misused as “black holes” preventing critical points from being tested
Using the proposed procedure, each point on the bonnet that can be finger-pointed to will have an allocated test result!
Measuring points cannot be hit!

## Slide 9
Advantages Of The Suggested Clarifications (3)
Pedestrian Safety
There can be multiple contacts with 2 or even more “first contact points” hit during the same impact, but:
Usually, kinetic energy is transferred in the plane of the headform’s center of gravity
Independent of the number of first contact points: There will be just one calculated HIC result achieved
Using the proposed procedure, the test result will be allocated to the point that was assigned as measuring point!
Two first contact points

## Slide 10
Pedestrian Safety
82.5
first contact point
of contour 1
first contact point
of contour 2
possible reduction of test area due to the
bonnet curvature
Side
Reference
Line
Advantages Of The Suggested Clarifications (4)
Vehicles with an identical overall width but with different bonnet designs will be tested differently:
Can be avoided with the proposed test procedure: Vehicles that create the same risk to pedestrians will be tested in the same way

## Slide 11
Request For Clarification Of Test Procedures
CONTENT
Clarification Of Headform Test Procedure
Clarification Of Headform Test Area
Clarification Of Legform Test Procedure
Pedestrian Safety

## Slide 12
Further difficulties are seen for the area subjected to headform tests that is defined different when comparing existing legislation in Japan and the EU to gtr No 9 and Draft ECE Regulation:
  Japan/EU: exclude the ½ headform diameter (82.5 mm) offset area from HIC zones calculation
  Gtr9/draft ECE: include offset area in HIC zones calculation
  Position of measuring points / selected impact points always in the test area excluding the offsets
  Leads to different sizes of HIC zones
  Gtr9/draft ECE procedure is unclear since the HIC1000 criterion may be assigned to the offset areas that cannot be tested
Clarification Of Headform Test Area
Pedestrian Safety

## Slide 13
The ½ headform diameter (82.5 mm) offset area should be excluded from the area used for HIC zones calculation
Tests should be conducted to the same area
Clarification Of Headform Test Area – Suggestions
Pedestrian Safety

## Slide 14
Schematic example, exact position of HIC zones
to be specified by the vehicle manufacturer!
Pedestrian Safety
Example for HIC zones using the 1/3 // 2/3 split (areas to be defined by the manufacturer)
Offset area: No test!
A much larger HIC1700 zone will result (that may be spread in the testable area) from considering the offset area during the calculation of the HIC zones
Photograph + original sketch (blue areas): BGS Boehme & Gehring
Advantages Of The Suggested Clarifications
Using the proposed procedure, this will not be possible

## Slide 15
Request For Clarification Of Test Procedures
CONTENT
Clarification Of Headform Test Procedure
Clarification Of Headform Test Area
Clarification Of Legform Test Procedure
Pedestrian Safety

## Slide 16
Clarification Of Legform Test Area
Pedestrian Safety
For the legform test area, the principle test procedure should follow the one used for the headform tests
Suggestion
The measuring point should be aligned with the impactor’s center line, the test result should always be allocated to the measuring point

## Slide 17
<number>
Thank you!