|  | United Nations | ST/SG/AC.10/C.3/2013/1 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 11 March 2013 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-third session

Geneva, 24–28 June 2013
Item 3 (c) of the provisional agenda

Listing, classification and packing: miscellaneous

New organic peroxide formulations be listed in 2.5.3.2.4 and IBC 520

Transmitted by the International Council of Chemical Association (ICCA)

Introduction

- Since several new peroxides and formulations have become commercially available, there is a need to update, 2.5.3.2.4 and IBC 520. A list of new products, proposed classification, the accompanying competent authority approval references and a summary of the supporting test data are given in the annex to this proposal.

Proposals

- ICCA proposes to include two amended entries and a correction in 2.5.3.2.4, list of currently assigned organic peroxides, as indicated in paragraph 3 below. Further, ICCA proposes to include two changes in packaging IBC520, as indicated in paragraph 4 below. Al changes indicated in gray shading.

3.	Proposed amendments to 2.5.3.2.4 List of currently assigned organic peroxides:

| ORGANIC PEROXIDE | Concentration (%) | Diluent type A (%) | Diluent type B 1) (%) | Inert solid (%) | Water | Packing Method | Control temperature (°C) | Emergency temperature (°C) | Number (Generic entry) | Subsidiary risks and remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CORRECT: DIBENZOYL PEROXIDE INTO DIBENZOYL PEROXIDE Remark: typing error since 8th revision | >51 - 100 >52 - 100 |  |  | ≤ 48 ≤ 48 |  | OP2 OP2 |  |  | 3102 3102 | 3) 3) |
| CHANGE: tert-BUTYL CUMYL PEROXIDE INTO tert-BUTYL CUMYL PEROXIDE | >42 - 100 >42 - 100 |  |  |  |  | OP8 OP8 |  |  | 3107 3109 |  |
| CHANGE: DICETYL PEROXYDICARBONATE INT0 DICETYL PEROXYDICARBONATE | ≤ 100 ≤ 100 |  |  |  |  | OP7 OP8 | +30 +30 | +35 +35 | 3116 3120 |  |
| CHANGE: tert-BUTYL PEROXY-3,5,5-TRIMETHYLHEXANOATE INTO tert-BUTYL PEROXY-3,5,5-TRIMETHYLHEXANOATE | >32-100 ≤ 32 >37-100 ≤ 37 | ≥ 68 ≥ 63 |  |  |  | OP7 OP8 OP7 OP8 |  |  | 3105 3109 3105 3109 |  |

- Proposed amendments to packaging instruction IBC520

| UN No. | Organic peroxide | Type of IBC | Maximum quantity (litres) | Control temper-ature | Emer-gency Tempe-rature |
| --- | --- | --- | --- | --- | --- |
| 3109 | ORGANIC PEROXIDE TYPE F, LIQUID |  |  |  |  |
|  | ADD NEW ENTRY: |  |  |  |  |
|  | tert-Butyl cumyl peroxide | 31HA1 | 1000 |  |  |
| 3119 | ORGANIC PEROXIDE TYPE F, LIQUID, TEMPERATURE CONTROLLED |  |  |  |  |
|  | ADD NEW ENTRY: |  |  |  |  |
|  | 1,1,3,3-Tetramethylbutyl peroxy-2-ethylhexanoate, not more than 67%, in diluent type A | 31HA1 | 1000 | +15 ºC | +20 ºC |
|  | ADD TO EXISTING ENTRY: |  |  |  |  |
|  | Di-(2-ethylhexyl) peroxydicarbonate, not more than 62%, stable dispersion, in water | 31HA1 | 1000 | -20 ºC | -10 ºC |

Annex: test results of new organic peroxides and formulations to be added/amended  (2.5.3.2.4 or IBC520)	(English only)

| No | Product | packaging | UN | Detonation | P/T / C.1 | Deflagration / C.2 | Koenen/ E.1 | DPVT/ E.2 | (mod) Trauzl F.3 or F.4 | SADT (H.3 or H.4) | Competent Authority approval number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | tert-Butyl cumyl peroxide, ≤100% | OP8 | 3109 | Test A.1 No propagation | <2170kPa, No | 0.05 mm/s, No | 1.0 mm Low | 1.0 mm (10g), Low | F.4 4.5 ml, Low | H.3 70 °C | NL TNO 12EM/327 |
| 2 | Dicetyl peroxydicarbonate, ≤100% | OP8 | 3120 | Test A.1 No propagation | <2170kPa, No | 0.0 mm/s, No | < 1mm (“O”), No | <1.0 mm (10g), Low | n.a. | H.4 40 °C (400ml) | NL TNO 12EM/562 |
| 3 | Di-(2-ethylhexyl) peroxydicarbonate, not more than 62%, stable dispersion, in water | 31HA1 | 3119 | Test A.1 No propagation | <2170kPa, No | 0.0 mm/s, No | <1.0mm ("O"),No | 1.0 mm (50g), Low | F.4 0.4 ml, Low | H.3 0 °C | NL TNO 08DV3/2133 |
| 4 | 1,1,3,3-Tetramethylbutyl peroxy-2-ethylhexanoate, not more than 67%, in diluent type A | 31HA1 | 3119 | Test A.6 No propagation (90%) | <2170kPa, No (94%) | 0.33 mm/s, No (70%) | <1 mm ("A”), Low (70%) | < 3.5 mm, Low (70%) | F.4 4 ml, Low (70%) | H.3 +30°C (65%) | NL TNO 11 HPE/612 |

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2013-2014 approved by the Committee at its sixth session (refer to ST/SG/AC.10/C.3/84, para. 86 and ST/SG/AC.10/40, para. 14).

This change is proposed because in packing instruction IBC520, this product with a concentration of ≤ 37% is already listed as UN 3109

# Text boxes

2

ST/SG/AC.10/C.3/2013/1