UN/SCETDG/42/INF.30

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 22 November 2012 Forty-second session Geneva, 3 – 11 December 2012 Item 7 of the provisional agenda New proposals for amendments to the Model Regulations on the Transport of Dangerous Goods

Correction to P501, P502, P 504 and P802

Transmitted by the expert from Germany

- P 501, P502, P 504 and P802 refer to 6PD2 as authorized packaging type under composite packagings. The descriptions mention (plywood) boxes, though 6PD2 is defined as glass, porcelain or stoneware receptacle in wickerwork hamper according to 6.1.2.7. Furthermore it should be reflected that 6PH1 and 6PH2 are listed as plastic packagings but not as drums.

- It is proposed to amend the wording as follows:

P 501, P 502 and P504

”glass receptacle in steel, aluminium, fibre or plywood drum (6PA1, 6PB1, 6PD1 or 6PG1) or in a steel, aluminium, wood or fiberboard box or in wickerwork hamper (6PA2, 6PB2, 6PC, 6PG2 or 6PD2) or in solid or expanded plastics packaging (6PH1 or 6PH1).”

P 802

“Composite packagings: Glass receptacle in steel, aluminium or plywood drum (6PA1, 6PB1 or 6PD1) or in a steel, aluminium or wood box or in wickerwork hamper (6PA1, 6PB2, 6PC or 6PD2) or in solid plastics packaging (6PH2); maximum capacity: 60 litres.”.